## Slide 1: Head-to-TOE Evaluation of High Performance Sockets over Protocol Offload Engines
P. Balaji¥ W. Fengα Q. Gao¥
R. Noronha¥ W. Yu¥ D. K. Panda ¥
¥Network Based Computing Lab,
Ohio State University
αAdvanced Computing Lab,
Los Alamos National Lab

## Slide 2: Ethernet Trends
Ethernet is the most widely used network architecture today
Traditionally Ethernet has been notorious for performance issues
  Near an order-of-magnitude performance gap compared to InfiniBand, Myrinet
    Cost conscious architecture
    Relied on host-based TCP/IP for network and transport layer support
    Compatibility with existing infrastructure (switch buffering, MTU)
  Used by 42.4% of the Top500 supercomputers
  Key: Extremely high performance per unit cost
    GigE can give about 900Mbps (performance) / 0$ (cost)
10-Gigabit Ethernet (10GigE) recently introduced
  10-fold (theoretical) increase in performance while retaining existing features
  Can 10GigE bridge the performance between Ethernet and InfiniBand/Myrinet?

## Slide 3: InfiniBand, Myrinet and 10GigE: Brief Overview
InfiniBand (IBA)
  Industry Standard Network Architecture
  Supports 10Gbps and higher network bandwidths
  Offloaded Protocol Stack
  Rich feature set (one-sided, zero-copy communication, multicast, etc.)
Myrinet
  Proprietary network by Myricom
  Supports up to 4Gbps with dual ports (10G adapter announced !)
  Offloaded Protocol Stack and rich feature set like IBA
10-Gigabit Ethernet (10GigE)
  The next step for the Ethernet family
  Supports up to 10Gbps link bandwidth
  Offloaded Protocol Stack
  Promises a richer feature set too with the upcoming iWARP stack

## Slide 4: Characterizing the Performance Gap
Each High Performance Interconnect has its own interface
  Characterizing the performance gap is no longer straight forward
Portability in Application Development
  Portability across various networks is a must
  Message Passing Interface (MPI)
    De facto standard for Scientific Applications
  Sockets Interface
    Legacy Scientific Applications
    Grid-based or Heterogeneous computing applications
    File and Storage Systems
    Other Commercial Applications
Sockets and MPI are the right choices to characterize the GAP
  In this paper we concentrate only on the Sockets interface

## Slide 5: Presentation Overview
Introduction and Motivation
Protocol Offload Engines
Experimental Evaluation
Conclusions and Future Work

## Slide 6: Interfacing with Protocol Offload Engines
Application or Library
Traditional
Sockets Interface
High Performance Sockets
User-level Protocol
TCP/IP
Device Driver
High Performance Network Adapter
Network Features
(e.g., Offloaded Protocol)
High Performance Sockets
toedev
TOM
Application or Library
Traditional Sockets Interface
TCP/IP
Device Driver
High Performance Network Adapter
Network Features
(e.g., Offloaded Protocol)
TCP Stack Override
Notes: Reverse order!

## Slide 7: High Performance Sockets
Pseudo Sockets-like Interface
  Smooth transition for existing sockets applications
    Existing applications do not have to rewritten or recompiled !
  Improved Performance by using the Offloaded Protocol Stack on networks
High Performance Sockets exist for many networks
  Initial implementations on VIA
  Follow-up implementations on Myrinet and Gigabit Ethernet
  Sockets Direct Protocol is an industry standard specification for IBA
    Implementations by Voltaire, Mellanox and OSU exist
[shah98:canpc, kim00:cluster, balaji02:hpdc]
[balaji02:cluster]
[balaji03:ispass, mellanox05:hoti]

## Slide 8: TCP Stack Override
Similar to the High Performance Sockets approach, but…
  Overrides the TCP layer instead of the Sockets layer
Advantages compared to High Performance Sockets
  Sockets features do not have to be duplicated
    E.g., Buffer management, Memory registration
  Features implemented in the Berkeley sockets implementation can be used
Disadvantages compared to High Performance Sockets
  A kernel patch is required
  Some TCP functionality has to be duplicated
This approach is used by Chelsio in their 10GigE adapters

## Slide 9: Presentation Overview
Introduction and Motivation
High Performance Sockets over Protocol Offload Engines
Experimental Evaluation
Conclusions and Future Work

## Slide 10: Experimental Test-bed and Evaluation
4 node cluster: Dual Xeon 3.0GHz; SuperMicro SUPER X5DL8-GG nodes
512 KB L2 cache; 2GB of 266MHz DDR SDRAM memory; PCI-X 64-bit 133MHz
InfiniBand
  Mellanox MT23108 Dual Port 4x HCAs (10Gbps link bandwidth); MT43132 24-port switch
  Voltaire IBHost-3.0.0-16 stack
Myrinet
  Myrinet-2000 dual port adapters (4Gbps link bandwidth)
  SDP/Myrinet v1.7.9 over GM v2.1.9
10GigE
  Chelsio T110 adapters (10Gbps link bandwidth); Foundry 16-port SuperX switch
  Driver v1.2.0 for the adapters; Firmware v2.2.0 for the switch
Experimental Results:
  Micro-benchmarks (latency, bandwidth, bi-dir bandwidth, multi-stream, hot-spot, fan-tests)
  Application-level Evaluation

## Slide 11: Ping-Pong Latency Measurements
SDP/Myrinet achieves the best small message latency at 11.3us
  10GigE and IBA achieve latencies of 17.7us and 24.4us respectively
As message size increases, IBA performs the best  Myrinet cards are 4Gbps links right now !

## Slide 12: Unidirectional Throughput Measurements
10GigE achieves the highest throughput at 6.4Gbps
  IBA and Myrinet achieve about 5.3Gbps and 3.8Gbps  Myrinet is only a 4Gbps link

## Slide 13: Snapshot Results (“Apples-to-Oranges” comparison) 10GigE: Opteron 2.2GHz IBA: Xeon 3.6GHz Myrinet: Xeon 3.0GHz Provide a reference point ! Only valid for THIS slide !
SDP/Myrinet with MX allows polling and achieves about 4.6us latency (event-based is better for SDP/GM ~ 11.3us)
10GigE achieves the lowest event-based latency of 8.9us on Opteron systems
IBA achieves a 9Gbps throughput with their DDR cards (link speed of 20Gbps)

## Slide 14: Bidirectional and Multi-Stream Throughput

## Slide 15: Hot-Spot Latency
10GigE and IBA demonstrate similar scalability with increasing number of clients
Myrinet’s performance deteriorates faster than the other two

## Slide 16: Fan-in and Fan-out Throughput Test
10GigE and IBA achieve a similar performance for the fan-in test
10GigE performs slightly better for the fan-out test

## Slide 17: Data-Cutter Run-time Library (Software Support for Data Driven Applications)
http://www.datacutter.org
Designed by Univ. of Maryland
Component framework
User-defined pipeline of components
  Each component is a filter
  The collection of components is a filter group
  Replicated filters as well as filter groups
  Illusion of a single stream in the filter group
  Stream based communication
Flow control between components
  Unit of Work (UOW) based flow control
  Each UOW contains about 16 to 64KB of data
Several applications supported
  Virtual Microscope
  ISO Surface Oil Reservoir Simulator
Notes: Talk about data-cutter applications

## Slide 18: Data-Cutter Performance Evaluation
InfiniBand performs the best for both the data-cutter applications (especially Virtual Microscope)
The filter-based approach makes the environment medium message latency sensitive

## Slide 19: Parallel Virtual File System (PVFS)
Network
Compute
Node
Compute
Node
Compute
Node
Compute
Node
Meta-Data
Manager
I/O Server
Node
I/O Server
Node
I/O Server
Node
Meta
Data
Data
Data
Data
  Designed by ANL and Clemson University
Relies on Striping of data across different nodes
Tries to aggregate I/O bandwidth from multiple nodes
Utilizes the local file system on the I/O Server nodes

## Slide 20: PVFS Contiguous I/O
Performance trends are similar to the throughput test
  Experiment is throughput intensive

## Slide 21: MPI-Tile I/O (PVFS Non-contiguous I/O)
10GigE and IBA perform quite equally
Myrinet is very close behind inspite of being only a 4Gbps network

## Slide 22: Ganglia Cluster Management Infrastructure
Cluster Nodes
Management Node
connect()
Request Information
Receive Data
Developed by UC Berkeley
For each transaction, one connection and one medium sized message (~6KB) transfer is required
Ganglia Daemon

## Slide 23: Ganglia Performance Evaluation
Performance is dominated by connection time
  IBA, Myrinet take about a millisecond to establish connections while 10GigE takes about 60us
  Optimizations for SDP/IBA and SDP/Myrinet such as connection caching are possible (being implemented)

## Slide 24: Presentation Overview
Introduction and Motivation
High Performance Sockets over Protocol Offload Engines
Experimental Evaluation
Conclusions and Future Work

## Slide 25: Concluding Remarks
Ethernet has traditionally been notorious for performance reasons
  Close to an order-of-magnitude performance gap compared to IBA/Myrinet
10GigE: Recently introduced as a successor in the Ethernet family
  Can 10GigE help bridge the gap for Ethernet with IBA/Myrinet?
We showed comparisons between Ethernet, IBA and Myrinet
  Sockets Interface was used for the comparison
  Micro-benchmark as well as application-level evaluations have been shown
10GigE performs quite comparably with the IBA and Myrinet
  Better in some cases and worse in others; but around the same ballpark
  Quite ubiquitous in Grid and WAN environments
  Comparable performance in SAN environments

## Slide 26: Continuing and Future Work
Sockets is only one end of the comparison chart
  Other middleware are quite widely used too (e.g., MPI)
  IBA/Myrinet might have an advantage due to RDMA/multicast capabilities
Network interfaces and software stacks change
  Myrinet coming out with 10Gig adapters
  10GigE might release a PCI-Express based card
  IBA has a zero-copy sockets interface for improved performance
  IBM’s 12x InfiniBand adapters increase the performance of IBA by 3 fold
  These results keep changing with time; more snapshots needed for fairness
Multi-NIC comparison for Sockets/MPI
  Awful lot of work at the host
  Scalability might be bound by the host
iWARP compatibility and features for 10GigE TOE adapters

## Slide 27: Acknowledgements
Our research is supported by the following organizations
Funding support by
Equipment donations by

## Slide 28: Web Pointers
Network Based Computing
Laboratory
Websites:
http://nowlab.cse.ohio-state.edu
http://public.lanl.gov/radiant/index.html
Emails:
balaji@cse.ohio-state.edu
feng@lanl.gov
panda@cse.ohio-state.edu
NBCL
LANL

## Slide 29: Backup Slides

## Slide 30: 10GigE: Technology Overview
Broken into three levels of technologies
  Regular Ethernet adapters
    Layer-2 adapters
    Rely on host-based TCP/IP to provide network/transport functionality
    Could achieve a high performance with optimizations
  TCP Offload Engines (TOEs)
    Layer-4 adapters
    Have the entire TCP/IP stack offloaded on to hardware
    Sockets layer retained in the host space
  iWARP-aware adapters
    Layer-4 adapters
    Entire TCP/IP stack offloaded on to hardware
    Support more features than TCP Offload Engines
      No sockets ! Richer iWARP interface !
      E.g., Out-of-order placement of data, RDMA semantics
[feng03:hoti, feng03:sc, balaji03:rait]
[balaji05:hoti]