## Slide 1: On the Provision of Prioritization and Soft QoS in Dynamically Reconfigurable Shared Data-Centers over InfiniBand
P. Balaji, S. Narravula, K. Vaidyanathan, H. –W. Jin and D. K. Panda
Network Based Computing Laboratory (NBCL)
The Ohio State University

## Slide 2: Presentation Outline
Introduction and Motivation
Overview of Dynamic Reconfigurability over InfiniBand
Issues with Basic Dynamic Reconfigurability
Dynamic Reconfigurability with Prioritization and Soft QoS
Experimental Results
Conclusions and Future Work

## Slide 3: COTS Clusters
Commodity-Off-the-Shelf (COTS) Clusters
  High Performance-to-Cost Ratio
  Enabled through High Performance Networks
Advent of High Performance Networks
  Ex: InfiniBand, Myrinet, Quadrics, 10-Gigabit Ethernet
  High Performance Protocols: VAPI / IBAL, GM, EMP
    Provide applications direct and protected access to the network
InfiniBand: An Industry Standard High Performance Network Architecture
  Low latency (< 4us) and high throughput (near wire speed = 10Gbps)
  Offloaded Protocol Stack, Zero-copy data transfer, One-sided communication (RDMA read/write, atomics, etc)
InfiniBand-based COTS Clusters are becoming extremely popular !
Notes: Explain more abt RDMA read/write and compare and swap

## Slide 4: Cluster-based Data-Centers
Increasing adoption of Internet
  Primary means of electronic interaction
  Highly Scalable and Available Web-Servers: Critical !
Utilizing Clusters for Data-Center environments?
  Studied and Proposed by the Industry and Research communities
(Courtesy CSP Architecture Design)
Nodes are logically partitioned
  Interact depending on the query
  Provide services requested
Load increases in the inner tiers
Edge
Services
Front tier
Applications
Mid tier
Applications
Back end
Applications
Internet
Enterprise
Network
Notes: No need to explain too much. Stick to load increasing part

## Slide 5: Shared Multi-Tier Data-Centers
WAN
Clients
Clients
Load Balancing Cluster (Site A)
Load Balancing Cluster (Site B)
Load Balancing Cluster (Site C)
Website A
Website B
Website C
Servers
Servers
Servers
Fragmentation of resources
Service differentiation
QoS guarantees
Notes: Explain the inherent assumption of load balancers, give examples of IBM., HP… in reality most data-centers host unrelated services (multiple websites)

## Slide 6: Objective
Fragmentation of resources needs to be curbed [balaji04_reconf]
  Dynamically configuring nodes allotted to each service
Service differentiation for different websites hosted
  Intelligent dynamic reconfiguration based on pre-defined prioritization rules
QoS guarantees for low-priority requests
  Ensure that low priority websites are given certain minimal resources at all times
Can the advanced features provided by InfiniBand help in providing dynamic reconfigurability with QoS and prioritization for different websites?
balaji04_reconf: “Exploiting Remote Memory Operations to Design Efficient Reconfiguration for Shared Data-Centers over InfiniBand”. P. Balaji, K. Vaidyanathan, S. Narravula, S. Krishnamoorthy, H. –W. Jin and D. K. Panda. In the RAIT workshop, held in conjunction with Cluster 2004.

## Slide 7: Presentation Outline
Introduction and Motivation
Overview of Dynamic Reconfigurability over InfiniBand
Issues with Basic Dynamic Reconfigurability
Dynamic Reconfigurability with Prioritization and Soft QoS
Experimental Results
Conclusions and Future Work

## Slide 8: Basic Dynamic Reconfigurability (Reconf)
WAN
Clients
Clients
Load Balancing Cluster (Site A)
Load Balancing Cluster (Site B)
Load Balancing Cluster (Site C)
Website A
Website B
Website C
Servers
Servers
Servers
Nodes reconfigure themselves to highly loaded websites at run-time

## Slide 9: Reconf Design
Support for Existing Applications
  Utilizing External Helper Modules (external programs running on each node) to take care of load monitoring, reconfiguration, etc.
Load-Balancer based vs. Server based Reconfiguration
Remote Memory Operations based Design
  Locking and Data Sharing are based on InfiniBand one-sided operations and atomics
  Load-balancers remotely monitor and reconfigure the system
Notes: Load balancer – network hardware can help becoz of remote memory operation, explain pros and cons of both the approaches
Mention Over-selling resources

## Slide 10: Utilizing InfiniBand Features
Two-level hierarchical locking mechanism
  Both locks performed remotely using InfiniBand Atomic Operations
Completely load resilient design
Server
Website A
Load
Balancer B
Server
Website B
Not Loaded
Loaded
Load Query
Load Query
Lock
Data Sharing
Reconfigure Node (Atomic)
Unlock
Load Shared
Load Shared
Notes: Emphasize load resilient design, server doesn’t send messages… so completely load resilient

## Slide 11: Presentation Outline
Introduction and Motivation
Overview of Dynamic Reconfigurability over InfiniBand
Issues with Basic Dynamic Reconfigurability
Dynamic Reconfigurability for Prioritization and Soft QoS
Experimental Results
Conclusions and Future Work

## Slide 12: Issues with Reconf on High Priority Requests
WAN
Clients
Clients
Load Balancing Cluster (Site A)
Load Balancing Cluster (Site B)
Load Balancing Cluster (Site C)
Website A (low priority)
Website B (medium priority)
Website C (high priority)
Servers
Servers
Servers
High Priority website may get lesser number of servers compared to medium/low priority websites since Reconf does not have any idea about Prioritization between websites
SCARCITY

## Slide 13: Presentation Outline
Introduction and Motivation
Overview of Dynamic Reconfigurability over InfiniBand
Issues with Basic Dynamic Reconfigurability
Dynamic Reconfigurability for Prioritization and Soft QoS
Experimental Results
Conclusions and Future Work

## Slide 14: Dynamic Reconfigurability with Prioritization (Reconf-P)
Prioritization support for Reconf
  Reconf requires additional logic to be priority aware
  Pre-defined rules for prioritization amongst various websites
Reconfiguration is website priority aware
  A node is said to be a free node if one of the following is true:
    It is lightly loaded
    It is serving a website with a lower priority than the requesting website

## Slide 15: Reconf with Prioritization
WAN
Clients
Clients
Load Balancing Cluster (Site A)
Load Balancing Cluster (Site B)
Load Balancing Cluster (Site C)
Website A (low priority)
Website B (medium priority)
Website C (high priority)
Servers
Servers
Servers
Low Priority websites may never get guaranteed number of servers since Reconf-P does not have any idea about QoS guarantees for websites
SCARCITY

## Slide 16: Dynamic Reconfigurability with Prioritization and Soft QoS Guarantees (Reconf-PQ)
Prioritization based Dynamic Reconfigurability
  Allows high paying websites to achieve a better performance
  Can result in scarcity of resources for low priority websites
QoS guarantees required to ensure scarcity-free reconfiguration
  Static allocation always provides QoS guarantees
    Low priority requests are given resources statically and never taken away
    QoS provided based on the resources available
  Reconf-PQ based design
    We want to ensure that low priority requests have some guaranteed resources (Hard QoS)
    We also want to achieve greater revenue by over-selling our resources
    Soft QoS Guarantees: Maximum resources we can allot based on other requests !
    Soft QoS ensures that a websites allocation does not deny other websites of their Hard QoS
Notes: Change figure to accommodate.. Hard QoS – A:1, B:2, C:3.. Soft Qos.. C:4. B:3

## Slide 17: Reconf with Prioritization and QoS
WAN
Clients
Clients
Load Balancing Cluster (Site A)
Load Balancing Cluster (Site B)
Load Balancing Cluster (Site C)
Website A (low priority)
Website B (medium priority)
Website C (high priority)
Servers
Servers
Servers
Reconf-PQ reconfigures nodes for different websites but also guarantees fixed number of nodes to low priority requests
Hard QoS Maintained

## Slide 18: Presentation Outline
Introduction and Motivation
Overview of Dynamic Reconfigurability over InfiniBand
Issues with Basic Dynamic Reconfigurability
Dynamic Reconfigurability for Prioritization and Soft QoS
Experimental Results
Conclusions and Future Work

## Slide 19: Experimental Test-bed
Cluster 1 with:
  8 SuperMicro SUPER X5DL8-GG nodes; Dual Intel Xeon 3.0 GHz processors
  512 KB L2 cache, 2 GB memory; PCI-X 64-bit 133 MHz
Cluster 2 with:
  8 SuperMicro SUPER P4DL6 nodes; Dual Intel Xeon 2.4 GHz processors
  512 KB L2 cache, 512 MB memory; PCI-X 64-bit 133 MHz
InfiniBand Interconnect with:
  Mellanox MT23108 Dual Port 4x HCAs; MT43132 24-port switch
Apache 2.0.50 Web and PHP 4.3.7 servers; MySQL 4.0.12 Database server

## Slide 20: Experimental Outline
Load resilience capabilities of InfiniBand in the data-center environment
Performance of Reconf comparing with static allocation schemes
Performance of Reconf, Reconf-P, Reconf-PQ
QoS meeting capabilities for Reconf, Reconf-P, Reconf-PQ
Notes: Move case 1,2,3 to two slides later

## Slide 21: Load resilience capabilities of InfiniBand
Remote memory operations are not affected AT ALL with remote server load
Notes: Explain the data-center environment… load in the back-end increasing… explicit message (load) vs implicit message (network).. Since the network hardware doing everything, its good for us

## Slide 22: Basic Reconfigurability Performance
Large Burst Length allows reconfiguration of the system closer to the best case; reconfiguration time is negligible;
Performs comparably with the static scheme for small burst sizes
Notes: Explain burst length, second graph.. Say Time scale instead of interations

## Slide 23: Reconfigurability Performance with QoS and Prioritization
Reconf does not perform any additional reconfiguration
Reconf and Reconf-P allocate maximum number of nodes to the low-priority website whereas Reconf-PQ allocates nodes to the QoS guaranteed to that website.
Case 1: A load of high priority requests arrives when a load of low priority requests already exists
Case 2: A load of low priority requests arrives when a load of high priority requests already exists
Case 3: Both high and low priority requests arrive simultaneously
Notes: Reconf performance varies a lot for all cases… we want some kind of guaranteed performance

## Slide 24: QoS Meeting Capability
Reconf and Reconf-P perform well only in some cases and lack consistency in providing the guaranteed QoS requirements to both websites
Reconf-PQ meets the guaranteed QoS requirements in all cases

## Slide 25: QoS Meeting Capability – Zipf and Worldcup Traces
Similar trends are seen for Zipf and Worldcup traces with QoS meeting capability of nearly 100% for Reconf-PQ

## Slide 26: Presentation Outline
Introduction and Motivation
Overview of Dynamic Reconfigurability over InfiniBand
Issues with Basic Dynamic Reconfigurability
Dynamic Reconfigurability for Prioritization and Soft QoS
Experimental Results
Conclusions and Future Work

## Slide 27: Concluding Remarks & Future Work
Shared Data-Centers are commonly used by several ISPs
  Resource Fragmentation
  Prioritization for high paying websites
  QoS guarantees for all websites
Extended our previous Dynamic Reconfigurability scheme
  Prioritization improves the performance of high priority websites
  QoS guarantees protect the low priority websites from scarcity of resources
Multi-Stage Reconfigurations
  Least loaded servers might not be the best server to reconfigure, Caching constraints, Hardware heterogeneity
Fine Grained Resource Reconfigurations
  Have done some initial study on file system reconfigurations
  Memory reconfiguration: utilizing remote memory in clusters as secondary cache

## Slide 28: Web Pointers
Network Based Computing
Laboratory
Group Homepage: http://nowlab.cis.ohio-state.edu
Emails: {balaji, narravul, vaidyana, jinhy, panda}@cse.ohio-state.edu
NBC-LAB