## Slide 1: Supporting iWARP Compatibility and Features for Regular Network Adapters
P. Balaji H. –W. Jin K. Vaidyanathan D. K. Panda
Network Based Computing Laboratory (NBCL)
Ohio State University

## Slide 2: Ethernet Overview
Ethernet is the most widely used network infrastructure today
Traditionally Ethernet has been notorious for performance issues
  Near an order-of-magnitude performance gap compared to other networks
    Cost conscious architecture
    Most Ethernet adapters were regular (layer 2) adapters
    Relied on host-based TCP/IP for network and transport layer support
    Compatibility with existing infrastructure (switch buffering, MTU)
  Used by 42.4% of the Top500 supercomputers
  Key: Reasonable performance at low cost
    TCP/IP over Gigabit Ethernet (GigE) can nearly saturate the link for current systems
    Several local stores give out GigE cards free of cost !
10-Gigabit Ethernet (10GigE) recently introduced
  10-fold (theoretical) increase in performance while retaining existing features

## Slide 3: Ethernet: Technology Trends
Broken into three levels of technologies
  Regular Ethernet adapters
    Layer-2 adapters
    Rely on host-based TCP/IP to provide network/transport functionality
    Could achieve a high performance with optimizations
  TCP Offload Engines (TOEs)
    Layer-4 adapters
    Have the entire TCP/IP stack offloaded on to hardware
    Sockets layer retained in the host space
  iWARP-aware adapters
    Layer-4 adapters
    Entire TCP/IP stack offloaded on to hardware
    Support more features than TCP Offload Engines
      No sockets ! Richer iWARP interface !
      E.g., Out-of-order placement of data, RDMA semantics
[feng03:hoti, feng03:sc, balaji04:rait]
[balaji05:hoti, balaji05:cluster]
[jin05:hpidc, wyckoff05:rait]

## Slide 4: Current Usage of Ethernet
System Area Network or Cluster Environment
Wide
Area
Network
Distributed Cluster Environment
Regular Ethernet
TOE
iWARP
Regular Ethernet Cluster
TOE Cluster
iWARP Cluster

## Slide 5: Problem Statement
Regular Ethernet adapters and TOEs are completely compatible
  Network level compatibility (Ethernet + IP + TCP + application payload)
  Interface level compatibility (both expose the sockets interface)
With the advent of iWARP, this compatibility is disturbed
  Both ends of a connection need to be iWARP compliant
    Intermediate nodes do not need to understand iWARP
  The interface exposed is no longer sockets
    iWARP exposes a much richer and newer API
    Zero-copy, asynchronous and one-sided communication primitives
    Not very good for existing applications
Two primary requirements for a wide-spread acceptance of iWARP
  Software Compatibility for Regular Ethernet with iWARP capable adapters
  A common interface which is similar to sockets and has the features of iWARP

## Slide 6: Presentation Overview
Introduction and Motivation
TCP Offload Engines and iWARP
Overview of the Proposed Software Stack
Performance Evaluation
Conclusions and Future Work

## Slide 7: What is a TCP Offload Engine (TOE)?
Sockets Interface
Application or Library
Hardware
User
Kernel
TCP
IP
Device Driver
Network Adapter
(e.g., 10GigE)
Sockets Interface
Application or Library
Hardware
User
Kernel
TCP
IP
Device Driver
Network Adapter (e.g., 10GigE)
Offloaded TCP
Offloaded IP
Traditional TCP/IP stack
TOE stack
Data Path

## Slide 8: iWARP Protocol Suite
MPA
RDMAP ULP
RDMAP
RDDP ULP
RDDP
TCP
SCTP
IP
Courtesy iWARP Specification
In-order Delivery and Out-of-order Placement
Middle Box Fragmentation
Feature Rich Interface
More details provided in the paper or in the iWARP Specification

## Slide 9: Presentation Overview
Introduction and Motivation
TCP Offload Engines and iWARP
Overview of the Proposed Software Stack
Performance Evaluation
Conclusions and Future Work

## Slide 10: Proposed Software Stack
The Proposed Software stack is broken into two layers
  Software iWARP implementation
    Provides wire compatibility with iWARP-compliant adapters
    Exposes the iWARP feature set to the upper layers
    Two implementations provided: User-level iWARP and Kernel-level iWARP
  Extended Sockets Interface
    Extends the sockets interface to encompass the iWARP features
    Maps a single file descriptor to both the iWARP as well as the normal TCP connection
    Standard sockets applications can run WITHOUT any modifications
    Minor modifications to applications required to utilize the richer feature set

## Slide 11: Software iWARP and Extended Sockets Interface
Application
Extended Sockets Interface
User-level iWARP
IP
Sockets
TCP
Device Driver
Network Adapter
Application
Extended Sockets Interface
Kernel-level
iWARP
TCP (Modified with MPA)
IP
Device Driver
Network Adapter
Sockets
Application
Extended Sockets Interface
High Performance Sockets
Sockets
Network Adapter
TCP
IP
Device Driver
Offloaded TCP
Offloaded IP
Software
iWARP
Application
Extended Sockets Interface
High Performance Sockets
Sockets
Network Adapter
TCP
IP
Device Driver
Offloaded TCP
Offloaded IP
Offloaded iWARP
Regular Ethernet Adapters
TCP Offload Engines
iWARP compliant Adapters

## Slide 12: Designing the Software Stack
User-level iWARP implementation
  Non-blocking Communication Operations
  Asynchronous Communication Progress
Kernel-level iWARP implementation
  Zero-copy data transmission and single-copy data reception
  Handling Out-of-order segments
Extended Sockets Interface
  Generic Design to work over any iWARP implementation

## Slide 13: Non-Blocking and Asynchronous Communication
Post_send()
setsockopt()
write()
Post_recv()
setsockopt()
Recv_Done()
User-level iWARP is a multi-threaded implementation
Main Thread
Async Thread
Main Thread
Async Thread

## Slide 14: Zero-copy Transmission in Kernel-level iWARP
Memory map user buffers to kernel buffers
Mapping needs to be in place till the reliability ACK is received
Buffers are mapped during memory registration
  Avoids mapping overhead during data transmission
User Virtual Address Space
Physical Address Space
Kernel Virtual Address Space
Memory Registration
Data Transmission

## Slide 15: Handling Out-of-order Segments
Out-of-Order Packet arrives
INTR on arrival
NIC
socket buffers
Wait for Intermediate packets
checksum
DMA
Data is retained in the Socket buffer even after it is placed !
This ensures that TCP/IP handles reliability and not the iWARP stack
Iwarp_wait()
Data Placed
Application NOT notified
copy

## Slide 16: Presentation Overview
Introduction and Motivation
TCP Offload Engines and iWARP
Overview of the Proposed Software Stack
Performance Evaluation
Conclusions and Future Work

## Slide 17: Experimental Test-bed
Cluster of Four Node P-III 700MHz Quad-nodes
1GB 266MHz SDRAM
Alteon Gigabit Ethernet Network Adapters
Packet Engine 4-port Gigabit Ethernet switch
Linux 2.4.18-smp

## Slide 18: Ping-Pong Latency Test

## Slide 19: Uni-directional Stream Bandwidth Test

## Slide 20: Software Distribution
Public Distribution of User-level and Kernel-level Implementations
  User-level Library
  Kernel module for 2.4 kernels
  Kernel patch for 2.4.18 kernel
  Extended Sockets Interface for software iWARP
Contact Information
  {panda, balaji}@cse.ohio-state.edu
  http://nowlab.cse.ohio-state.edu

## Slide 21: Presentation Overview
Introduction and Motivation
TCP Offload Engines and iWARP
Overview of the Proposed Software Stack
Performance Evaluation
Conclusions and Future Work

## Slide 22: Concluding Remarks
Ethernet has been broken down into three technology levels
  Regular Ethernet, TCP Offload Engines and iWARP-compliant adapters
  Compatibility between these technologies is important
Regular Ethernet and TOE are completely compatible
  Both the wire protocol and the ULP interface are the same
  iWARP does not share such compatibility
Two primary requirements for a wide-spread acceptance of iWARP
  Software Compatibility for Regular Ethernet with iWARP capable adapters
  A common interface which is similar to sockets and has the features of iWARP
We provided a software stack which meets these requirements

## Slide 23: Continuing and Future Work
The current Software iWARP is only built for Regular Ethernet
  TCP Offload Engines provide more features than Regular Ethernet
  Needs to be extended to all kinds of Ethernet networks
    E.g., TCP Offload Engines, iWARP-compliant adapters, Myrinet 10G adapters
Interoperability with Ammasso RNICs
  Modularized approach to enable/disable components in the iWARP stack
Simulated Framework for studying NIC architectures
  NUMA Architectures on the NIC for iWARP Offload
Flow Control/Buffer Management Features for Extended Sockets

## Slide 24: Acknowledgments

## Slide 25: Web Pointers
Network Based Computing
Laboratory
Website: http://www.cse.ohio-state.edu/~balaji
Group Homepage: http://nowlab.cse.ohio-state.edu
Email: balaji@cse.ohio-state.edu
NBCL

## Slide 26: Backup Slides

## Slide 27: DDP Architecture
Extended sockets API
  Connection management handled by the standard sockets API
  Data transfer carried out using two communication models
    Untagged Communication Model
    Tagged Communication Model
Out-of-Order Placement; In-order Delivery
Segmentation and Re-assembly of messages

## Slide 28: DDP Untagged Communication Model
SQ
RQ
SQ
RQ

## Slide 29: DDP Untagged Model Specifications
Simple send-receive based communication model
Receiver has to inform DDP about a buffer before hand
When data arrives, it is placed in the buffer directly
Zero-Copy data transfer
No flow control guaranteed by DDP; application takes care of this
Explicit message delivery required on the receiver side

## Slide 30: DDP Tagged Communication Model
SQ
RQ
SQ
RQ

## Slide 31: DDP Tagged Model Specifications
One-sided communication model
Receiver has to inform the sender about a buffer before hand
Sender can directly read or write to the receiver buffer
Zero-Copy data transfer
No flow control required since the receiver is not involved at all
No message delivery on the receiver side; only data placement

## Slide 32: Out-of-Order Data Placement
DDP allows out-of-order data placement
  Two segments in a message can be transmitted out of order
  Two segments in a message can be placed out of order
  A message cannot be delivered till all segments in it are placed
  A message cannot be delivered till all previous messages are delivered
Reduced buffer requirements
Most beneficial for slightly congested networks
  TCP Fast retransmit avoids performance degradation
  Out-of-order placement avoids extra copies and buffering

## Slide 33: Segmentation and Reassembly
DDP does not deal with IP fragmentation
IP layer does IP reassembly and hands over to DDP
Segmentation is tricky in DDP
  Message boundaries need to be retained unlike TCP streaming
  Sender performs segmentation while maintaining boundaries
  Receiver can perform reassembly as long as boundaries are maintained
  What about TCP segmentation/reassembly on intermediate nodes?
  Layer-4 switches such as Load-Balancers
    TCP aware; can assume TCP streaming semantics

## Slide 34: Layer-4 Switches
Load
Balancer
WAN
Google
Servers
Client

## Slide 35: TCP Splicing
Load Balancing Application
TCP/IP Stack with TCP Splicing
Network Interface Card
The TCP stack can assume streaming
No one-to-one correspondence between the received segments and transmitted segments

## Slide 36: Marker PDU Aligned Protocol
DDP segments created by sender need not be retained
  TCP Splicing
DDP header needs to be recognized
  If message boundaries are not retained, this is not possible !
  Need a solution independent of message segmentation
MPA Protocol
  Places strips of data at regular intervals
    Interval denoted by the TCP sequence number
  Each strip points to the DDP header

## Slide 37: MPA Protocol
DDP Header
ULP Payload (if any)
DDP Header
ULP Payload (if any)
CRC
Pad
Segment Length