## Slide 1: Asynchronous Zero-copy Communication for Synchronous Sockets in the Sockets Direct Protocol over InfiniBand
P. Balaji, S. Bhagvat, H. –W. Jin and D. K. Panda
Network Based Computing Laboratory (NBCL)
Computer Science and Engineering
Ohio State University

## Slide 2: InfiniBand Overview
An emerging industry standard
High Performance
  Low latency (about 2us)
  High Throughput (8Gbps, 16Gbps and higher)
Advanced Features
  Hardware offloaded protocol stack
  Kernel bypass – direct access to network for applications
  RDMA operations – direct access to remote memory

## Slide 3: Sockets Direct Protocol (SDP)
High-Performance Alternative to TCP/IP sockets for IB, etc.
Hijack and redirect socket calls
Application transparent
  Binary compatibility (most cases)
Utilizes IB capabilities
  Offloaded Protocol
  RDMA operations
  Kernel bypass
Sockets Direct
Protocol
App #1
App #2
High-speed Network
Device Driver
IP
TCP
Traditional
Sockets
Sockets Interface
Offloaded
Protocol
App #N
Advanced
Features

## Slide 4: Sockets APIs Supported by SDP
 | Synchronous Sockets | Asynchronous Sockets | Extended Sockets (OSU Specific)*
Communication | Synchronous | Asynchronous | Asynchronous
Operations Outstanding | At most one | More than one | More than one
SDP Implementations | BSDP, ZSDP | BSDP, ZSDP | BSDP, ZSDP
Existing Applications | Most | Few | Very few
Potential for Performance | Limited | High | High
(Portions of this table have been borrowed from Mellanox Technologies)
* RAIT05: “Supporting iWARP compatibility and features for regular network adapters”. P. Balaji, H. –W. Jin, K. Vaidyanathan and D. K. Panda. RAIT Workshop; in conjunction with Cluster ‘05
BSDP, ZSDP,
AZ-SDP

## Slide 5: Presentation Layout
Introduction and Background
Understanding Asynchronous Zero-copy SDP
Design Issues in AZ-SDP
Performance Evaluation
Conclusions and Future Work

## Slide 6: Buffer-copy SDP (BSDP)
Several buffer-copy based implementations of SDP exist
  OSU, Mellanox, Voltaire
HCA offloads transport and network layers
Copy overhead still present
Data Source
App
Buffer
App
Buffer
SDP
Buffer
SDP
Buffer
SDP
Buffer
SDP
Buffer
SDP
Buffer
SDP
Buffer
Data Sink
SDP Data
Message
ISPASS04: “Sockets Direct Protocol over InfiniBand in Clusters: Is it Beneficial?”. P. Balaji, S. Narravula, K. Vaidyanathan, S. Krishnamoorthy and D. K. Panda. IEEE International Conference on Performance Analysis of Systems and Software (ISPASS), 2004.

## Slide 7: Zero-copy SDP (ZSDP)
Implemented by Mellanox
  RDMA Read based design
Benefits of zero-copy
Limited by the API of Synchronous Sockets
  At most one outstanding communication request
  Control message latency (50% time for 16K message)
Intolerant to Skew
Data Source
App
Buffer
Data Sink
SRC AVAIL
App
Buffer
send()
Send Complete
Application Blocks
App
Buffer
SRC AVAIL
App
Buffer
send()
Send Complete
Application Blocks
GET COMPLETE
GET COMPLETE

## Slide 8: Asynchronous Zero-copy SDP (AZ-SDP)
Basic zero-copy communication is synchronous
  Data communication accompanied by control messages
  Communication will be latency bound
Asynchronous Zero-copy SDP
  Utilize the benefits of asynchronous communication (more than one outstanding communication operation)
  Maintain the semantics of synchronous sockets (application can assume that it is using synchronous sockets)
  Objectives: Correctness, Transparency and Performance
  Key Idea: Memory protect buffers

## Slide 9: AZ-SDP Functionality
Memory Protect
Memory Protect
Send returns as soon as communication is initiated
  Application “thinks” communication is synchronous
Memory unprotected after communication completes
If application touches buffer
  Communication complete: Great!
  Else PAGE FAULT generated
SRC AVAIL
send()
App
Buffer1
SRC AVAIL
send()
App
Buffer2
Memory Unprotect
GET COMPLETE
App
Buffer1
App
Buffer2
Data Source
Data Sink
Get Data

## Slide 10: Presentation Layout
Introduction and Background
Understanding Asynchronous Zero-copy SDP
Design Issues in AZ-SDP
Performance Evaluation
Conclusions and Future Work

## Slide 11: Design Issues in AZ-SDP
Handling a Page Fault
  Block-on-Write: Wait till the communication has finished
  Copy-on-Write: Copy data to internal buffer and carry on communication
Handling Buffer Sharing
  Buffers shared through mmap()
Handling Unaligned Buffers
  Memory protection is only in the granularity of a page
  Malloc hook overheads

## Slide 12: Handling a Page Fault
Memory protection needed to disallow the application from accessing an occupied communication buffer
Page fault generated on access
  Number of page faults generated are application dependent
Two approaches for handling the page-fault
  Block on Write
  Copy on Write

## Slide 13: Block-on-Write
Memory Protect
Optimistic approach to avoid blocking for communication
  ZSDP blocks during the communication call
  AZ-SDP delays blocking
Advantage:
  Zero-copy communication
  SDP specification compliant
Disadvantage:
  Not skew tolerant
SRC AVAIL
send()
App
Buffer1
Memory Unprotect
GET COMPLETE
App
Buffer1
Data Source
Data Sink
Get Data
Application touches buffer
PAGE FAULT generated
Block

## Slide 14: Copy-on-Write
Memory Protect
Enhances the functionality of Block-on-Write
  Does not blindly block
Advantage:
  Zero-copy communication when possible
  Skew tolerant when receiver is not ready
Disadvantage
  Not SDP specification compliant
SRC AVAIL
send()
App
Buffer1
Memory Unprotect
GET COMPLETE
App
Buffer1
Data Source
Data Sink
Application touches buffer
PAGE FAULT generated
Block
Atomic Lock
Atomic Lock Failed
App
Buffer1
Atomic Lock Successful
Copy to temp. buffer
SRC UPDATE

## Slide 15: Presentation Layout
Introduction and Background
Understanding Asynchronous Zero-copy SDP
Design Issues in AZ-SDP
Performance Evaluation
Conclusions and Future Work

## Slide 16: Experimental Test-Bed
4 node cluster
  Dual 3.6 GHz Intel Xeon EM64T processors (2 MB L2 cache), 512 MB of 333 MHz DDR SDRAM
  Mellanox MT25208 InfiniHost III DDR PCI-Express adapters (capable of a link-rate of 16 Gbps)
  Mellanox MTS-2400, 24-port fully non-blocking DDR switch

## Slide 17: Throughput and Comp./Comm. Overlap
30% improvement in the throughput
Up to 2X improvement in computation/communication overlap tests

## Slide 18: Impact of Page-faults
When application touches the communication buffer very frequently, PAGE FAULT overheads degrade AZ-SDP’s performance

## Slide 19: Presentation Layout
Introduction and Background
Understanding Asynchronous Zero-copy SDP
Design Issues in AZ-SDP
Performance Evaluation
Conclusions and Future Work

## Slide 20: Conclusions and Future Work
Current Zero-copy SDP approaches: Very restrictive
AZ-SDP brings the benefits of asynchronous sockets to synchronous sockets in a TRANSPARENT manner
30% better throughput and 2X improvement in computation-communication overlap tests
Analysis with applications and large-scale clusters
Integration with OpenIB/Gen2

## Slide 21: Acknowledgements
Our research is supported by the following organizations
Current Funding support by
Current Equipment support by

## Slide 22: Web Pointers
Network Based Computing
Laboratory
Website: http://www.cse.ohio-state.edu/~balaji
Group Homepage: http://nowlab.cse.ohio-state.edu
Email: balaji@cse.ohio-state.edu
NBCL

## Slide 23: Backup Slides

## Slide 24: Sockets Programming Model
Several high-speed networks available today
  E.g., InfiniBand (IB), Myrinet, 10-Gigabit Ethernet
Common programming models
  E.g., Sockets, MPI, Shared Memory Models
  Network independent parallel and distributed applications
Sockets programming model is of particular interest
  Scientific apps, file/storage systems, commercial apps
  Traditionally built over TCP/IP (and others)
  Performance of such implementations is not the best

## Slide 25: Limitations of TCP/IP Sockets for High-speed Networks
Network/Transport layers processed by the host
  Limited performance
  Excessive resource usage (CPU, Memory traffic)
Generic optimizations for TCP/IP sockets
  Cannot sustain the performance of high-speed networks
  Performance on IB (16Gbps) adapters limited to 2Gbps
Sockets Direct Protocol (SDP) proposed
  Alternative to TCP/IP Sockets

## Slide 26: Zero-Copy Mechanisms in SDP
SRC Available
RDMA Read Data
GET Complete
Sender
Receiver
SINK Available
RDMA Write Data
PUT Complete
Sender
Receiver
Register Buffer
Register Buffer
SOURCE-AVAIL
SINK-AVAIL

## Slide 27: Prior Research
Prior Research on High-Performance Sockets spanning various networks (Giganet CLAN, VIA, GbE, Myrinet)
SDP over IBA: Buffer-copy based implementation
Recent research on Zero-copy SDP [Goldenberg05]
Zero-copy schemes to optimize TCP and UDP stacks
  Mostly for asynchronous sockets
  May require kernel/NIC firmware modifications

## Slide 28: Latency and Throughput

## Slide 29: Computation/Communication Overlap

## Slide 30: Multi-connection Tests

## Slide 31: Hot-spot Latency Test

## Slide 32: Buffer Sharing
Memory-protect B1 and disallow all access to it
Override the mmap() call (libc) with a new mmap call
  New mmap() call contains mapping of all memory-mapped buffers
B1
B2
B1 and B2 are memory mapped to each other
Send()
Write()

## Slide 33: Managing Un-aligned Buffers
Two approaches
  Malloc Hook
  Hybrid approach with Buffered SDP
Physical
Page
VAPI Control Buffer
Application Buffer
Shared Page

## Slide 34: Malloc Hook
Approach overrides the malloc() and free() system calls
New Malloc() allocates physical page boundary-aligned N + PAGE_SIZE bytes, when N bytes are requested
Advantage :
  Simple Approach
Disadvantage :
  Very small buffer requests may result in buffer wastage
  Time to malloc few bytes to Physical Page size is the same

## Slide 35: Hybrid approach with Buffered SDP
Hybrid Mechanism between BSDP and AZ-SDP
Physical
Page
VAPI Control Buffer
Application Buffer
AZ-SDP
communication
BSDP
comm.
BSDP
comm.
A single communication might be carried out in multiple operations (upto three)
5-10% better performance than Malloc-hook based scheme

## Slide 36: Copy-on-Write
Control maintained via Locks at the receiver end by the AZ-SDP layer
Receiver obtains the lock, if recv() is called first
Sender can obtain the lock on generation of a page fault and can perform a copy-on-write operation