## Slide 1: High Performance MPI over iWARP: Early Experiences
S. Narravula, A. Mamidala, A. Vishnu, G. Santhanaraman, and D. K. Panda
Network Based Computing Laboratory (NBCL)
Computer Science and Engineering, Ohio State University
Presented by Pavan Balaji, Argonne National Laboratory

## Slide 2: High-performance Parallel Computing with Ethernet
Most widely used network infrastructure today
  Used by 41.2% of the Top500 supercomputers
Traditionally notorious for performance issues
  Large performance gap compared to IB, Myrinet
  Key: Reasonable performance at low cost
    TCP/IP over Gigabit Ethernet (GE) saturates the network
    Several local stores give out GE cards free of cost ! 
10-Gigabit Ethernet (10GE) recently introduced
  10-fold (theoretical) increase in performance while retaining existing features

## Slide 3: 10GE: Technology Trends
Broken into three levels of technologies
  Regular 10GigE adapters
    Software TCP/IP stack
  TCP Offload Engines (TOEs)
    Hardware TCP/IP stack
  iWARP Offload Engines
    Standardized by the RDMAC and IETF
    Hardware TCP/IP stack
    More features: Remote Direct Memory Access (RDMA), Asynchronous communication, Zero-copy data transfer
[feng03:hoti, feng03:sc, balaji03:rait]
[feng05:hoti, balaji05:cluster]
[jinhy05:hpidc, wyckoff05:rait]

## Slide 4: Message Passing Interface
Message Passing Interface (MPI)
  De-facto standard for message passing communication
Traditional implementations over Ethernet
  Relied on TCP/IP (e.g., MPICH2)
  Reasonable for traditional Ethernet networks (e.g., GE)
Advent of iWARP over 10GE
  Provides hardware offload capabilities and scalability features
  Traditional TCP/IP based implementations not sufficient
Need a high-performance MPI over iWARP !!

## Slide 5: Presentation Outline
Introduction
10GE and iWARP Background
Designing MPI over iWARP
Performance Evaluation
Conclusions and Future Work

## Slide 6: 10-Gigabit Ethernet and iWARP
10 fold increase in Ethernet performance
  40G and 100G speeds in development
Hardware offloaded TCP/IP Stack
RDMA Capability
  Asynchronous communication
  Zero copy data transfers
  One-sided interface
WAN capability
Existing iWARP enabled Interconnects
  Chelsio, NetEffect, NetXen
Notes: WAN compatability linked to cluster-of-clusters

## Slide 7: iWARP Architecture and Components
RDDP
Application or Library
Hardware
User
SCTP
IP
Device Driver
Network Adapter
(e.g., 10GigE)
iWARP Offload Engines
TCP
RDMAP
MPA
Courtesy iWARP Specification
RDMA Protocol (RDMAP)
  Feature-rich interface
  Security Management
Remote Direct Data Placement (RDDP)
  Data Placement and Delivery
  Multi Stream Semantics
  Connection Management
Marker PDU Aligned (MPA)
  Middle Box Fragmentation
  Data Integrity (CRC)

## Slide 8: iWARP Software Stack
OFED Gen2 verbs support
  Open Fabrics Alliance – http://www.openfabrics.org
  RDMA CM for connection setup
  ibverbs for communication
Queue pair (QP) based communications
  Post Work Queue Entries (WQEs)
  WQE describes the buffer to be sent from/received into
Connection
  Needs an underlying TCP/IP connection
  Connection setup: Client/Server like mechanism

## Slide 9: Presentation Outline
Introduction
10GE and iWARP Background
Designing MPI over iWARP
Performance Evaluation
Conclusions and Future Work

## Slide 10: Designing MPI over iWARP
Protocol
Mapping
Buffer
Management
Flow
Control
Connection
Management
Communication
Progress
Collective
Communication
Multirail
Support
Substrate
RDMA
Operations
Shared
Receive Queues
Out-of-order
Placement
MPI Design Components
One-sided
Active/Passive
Send /
Receive
Dynamic
Rate Control
QoS
Multi-Pathing
VLANs
iWARP/Ethernet Features

## Slide 11: Design Components
Several components similar to other MPI designs
  E.g., MVAPICH and MVAPICH2
This paper deals only with a few of them:
  Connection Semantics
    Semantics mismatch between iWARP and MPI
  Multi-channel requirements
    Multi-rail and direct one-sided communication
  RDMA Fast Path optimization for small messages
    Message completion with RDMA
    Correctness depends on iWARP implementation

## Slide 12: Connection Management
MPI assumes fully-connected model
  Communication between multiple peers without explicit connections
  Any node can start communicating with any other node
  Peer-to-peer semantics
iWARP assumes client/server model
  Client initiates connection and server accepts it
  TCP/IP like semantics
  Message initiation restrictions (client has to initiate)
  Need to establish pairs of clients/servers for connection setup

## Slide 13: Basic Connection Management
MPI processes divided into client/servers pairs
  (Pi, Pj): i is the server if (i < j)
Exchange ports/IPs
Resolve addresses
Initiate connection request
MPI level communication
  Not yet ready
Listen
Exchange
IPs/Ports
Resolve Address
And Route
Barrier
Accept
Connection
Established
Connection
Established
Process i
Process j
(i < j)
Notes: Connection will be ready to use once the dummy message is sent from client to server. Explained in the next slide.

## Slide 14: Client->Server Message Initiation
Dummy message is created and sent from client to server
MPA requirement
NOOP packet used
Listen
Exchange
IPs/Ports
Resolve Address
And Route
Barrier
Accept
Connection
Established
Connection
Established
Initiate Dummy
Data Transfer
Process i
Process j
(i < j)
MPI peers ready
to communicate

## Slide 15: Implementation Details
Integrated into MVAPICH2
  High Performance MPI-1/MPI-2 implementation over InfiniBand and iWARP
  Has powered many supercomputers in TOP500 supercomputing rankings
  Currently being used by more than 545 organizations (academia and industry worldwide)
  http://mvapich.cse.ohio-state.edu/
  The iWARP design is available with current MVAPICH2 release

## Slide 16: Presentation Outline
Introduction
10GE and iWARP Background
Designing MPI over iWARP
Performance Evaluation
Conclusions and Future Work

## Slide 17: Experimental Testbed
Quad core Intel Xeon 2.33Ghz, 4 GB memory
Chelsio T3B 10GE PCIe RNICs, 24 port Fulcrum switch
OFED 1.2 rc4 software stack, RH4 U4
MPIs
  MPICH2 1.0.5p3  TCP/IP based
  MVAPICH2-R  RDMA based
  MVAPICH2-SR  Send/Recv based
  MVAPICH2-1SC  RDMA one-sided enabled
Notes: MVAPICH2-SR is essentially MVAPICH2 without the RDMA fast path optimization

## Slide 18: Experiments Performed
Basic MPI two sided benchmarks
  Latency and Bandwidth
MPI one sided benchmarks
  Get and Put
MPI collectives
  Barrier, Allreduce and Allgather
NAS parallel benchmarks
  IS and CG

## Slide 19: Latency
MVAPICH2-R supports a low latency of about 7 us

## Slide 20: Bandwidth
MVAPICH2 achieves a peak bandwidth of 1231 MB/s

## Slide 21: MPI Put Latency
MVAPICH2 shows an improvement of about 4 times in latency
over MPICH2

## Slide 22: MPI Put Bandwidth
MVAPICH2 shows an improvement in bandwidth of up to 40%
over MPICH2

## Slide 23: MPI Allgather
MVAPICH performs up to 84% better for Allgather for 32 processes

## Slide 24: MPI Allreduce
MVAPICH performs up to 80% better for Allreduce for 32 processes

## Slide 25: MPI Barrier
MVAPICH2 performs up to 80% better for barrier for 32 processes

## Slide 26: NAS
MVAPICH2 performs up to 16% better than MPICH2 for IS

## Slide 27: Presentation Outline
Introduction
10GE and iWARP Background
Designing MPI over iWARP
Performance Evaluation
Conclusions and Future Work

## Slide 28: Conclusions and Future Work
High performance MPI design over iWARP
  First Native iWARP capable MPI
Significant performance gains over TCP/IP based implementations
Integrated into MVAPICH2 release 0.9.8 onwards
Future Work
  Utilize iWARP capabilities like SRQ’s, multi-pathing VLANs, etc to further optimize MPI-iWARP
  Optimize and evaluate MPI-iWARP in emerging cluster-of-cluster scenarios

## Slide 29: Questions?
Web Pointers
http://mvapich.cse.ohio-state.edu
{narravul, mamidala, vishnu, santhana, panda}
@ cse.ohio-state.edu

## Slide 30: Backup Slides

## Slide 31: MPI Get Latency
MVAPICH2 shows a latency improvement of about 3.6 times over MPICH2

## Slide 32: MPI Get Bandwidth

## Slide 33: iWARP Capabilities
Features | iWARP capability
Hardware offloaded Protocol | Supported
RDMA | Supported
Atomic Operations | Not supported
Multicast | Not supported by current implementations
QoS | Not supported by current implementations
Data Placement | Out-of-order
Data Rate-control | Dynamic and Fine-grained