## Slide 1: Designing NFS With RDMA For Security, Performance and Scalability
Ranjit Noronha*, Lei Chai*, Thomas Talpey+ and Dhabaleswar K. Panda*
Network Based Computing Laboratory (NBCL) *
The Ohio State University
&
Network Appliances +
Presented by Pavan Balaji, Argonne National Laboratory

## Slide 2: Outline of the talk
Introduction and Motivation
  Network File Systems
  RDMA Operations InfiniBand
Design Issues
  Read-Read Design
  Read-Write Design
  Evaluation of Read-Read versus Read-Write
Registration Strategies
  Issues with Registration
  Techniques to reduce overhead
  Impact of Registration Strategies
Scalability With Multiple Clients
Conclusions and Future Work

## Slide 3: Network File Systems
Popular file system for distributed environments
Used for exporting home directories in many UNIX clusters
Single Server, multiple client model
Usually uses TCP or UDP
TCP may introduce considerable overhead at the server
May not be able to deliver performance on networks like InfiniBand

## Slide 4: InfiniBand
Open Industry Standard Network
Low latency, high-bandwidth
  Single Data Rate (SDR)
  Less than 4us ping-pong latency for a 4 byte message
  Up to 2GB/s bi-directional bandwidth for large transfers
Remote Direct Memory Access (RDMA) operations
  Appropriately authorized hosts may read or write directly from each others address space
  Very little CPU involvement
  Zero-copy protocol

## Slide 5: Problem Statement
Design a high performance implementation of NFS/RDMA for OpenSolaris keeping in mind the security of the server
Design considerations for the relative limitations and potential solutions to the problem of registration overhead
Application evaluation of the NFS/RDMA protocols
Impact of RDMA on the scalability of NFS protocols with multiple clients and real disks supporting the back-end file system

## Slide 6: Outline of the talk
Introduction and Motivation
  Network File Systems
  RDMA Operations InfiniBand
Design Issues
  Read-Read Design
  Read-Write Design
  Evaluation of Read-Read versus Read-Write
Registration Strategies
  Issues with Registration
  Techniques to reduce overhead
  Impact of Registration Strategies
Scalability With Multiple Clients
Conclusions and Future Work

## Slide 7: Communication Operations in InfiniBand
Reliable Connection (RC) Model
  Queue Pair
  Channel Primitives
  Memory Primitives
Channel Primitives
  Send/Receive
  RDMA Send/RDMA Receive
Memory Primitives
  RDMA Operations
  RDMA Read/RDMA Write
 | Channel Primitives | Memory Primitives
Receive Buffer Exposed |  | √
Receive Buffer Pre-posted | √ | 
Steering Tags |  | √
Rendezvous |  | √

## Slide 8: NFS/RDMA Architecture
Small Requests (< 1K bytes)
  Use the inline protocol
  Request from client to server (RPC Call)
  Response from server to client (RPC Reply)
  Inline protocol uses a pool of 1K buffers and RDMA Send/RDMA receive
  RPC Call/RPC Reply and most NFS Procedures are usually small and may be transferred through the inline protocol
Bulk data transfer
  NFS Procedures READ, WRITE, READDIR, READLINK
  Existing Read-Read design (RDMA Read for all operations)
  Read-Write design (Combination of RDMA Read and RDMA Write)

## Slide 9: NFS/RDMA Architecture
Requests sent from the client to the server  RPC Call
Response sent from server to the client  RPC Reply

## Slide 10: NFS Write Procedure
Client
Server
RPC Call
WRITE
(RDMA Read)
RPC Reply
Read-Read and Read-Write use the same design

## Slide 11: NFS Procedure READ
Client
Server
RPC Call
RPC Reply
RDMA Read
RDMA Done
Client
Server
RPC Call
RPC Reply
RDMA Write
Read-Read
Read-Write
Server Buffer Exposed
Client Controls Server Buffer
Additional Interrupt

## Slide 12: NFS Procedures READDIR, READLINK
READDIR and READLINK designs similar to READ
Client
Server
RPC Call
RPC Reply
Client
Server
RPC Call
RPC Reply
Long Reply
(RDMA Read)
RDMA Done
Long Reply
(RDMA Write)
Read-Read
Read-Write

## Slide 13: Comparison of the Read-Read and Read-Write Designs
Limitations of the Read-Read Design
  Security
    Server buffers exposed
    Malicious or Malfunctioning clients
  Performance
    Additional Completion Interrupt
    Synchronous RDMA Read Limitations (ordering between reads)
    Outstanding RDMA Reads (8 in current network adapters)
Potential Advantages of the Read-Write Design
  Better Security
  Reduced Interrupts
  Number of outstanding requests (RDMA read vs. RDMA write)

## Slide 14: Experimental Setup
Two x2200’s
  Dual 2.2 GHz Opterons
  2GB main memory
  SDR PCI-Express HCA’s
File System
  Memory Based File System (tmpfs)
  128 MB file size for all experiments
Experiments
  IOzone
  Direct I/O

## Slide 15: Bandwidth Comparison
2.2 GHz dual Opterons with 2GB memory and SDR HCA’s running OpenSolaris bv33
Read-Write achieves a peak READ BW of 392 MB/s and Read-Read achieves a
READ BW of 374 MB/s
CPU Utilization lower for Read-Write

## Slide 16: Outline of the talk
Introduction and Motivation
  Network File Systems
  RDMA Operations InfiniBand
Design Issues
  Read-Read Design
  Read-Write Design
  Evaluation of Read-Read versus Read-Write
Registration Strategies
  Issues with Registration
  Techniques to reduce overhead
  Impact of Registration Strategies
Scalability With Multiple Clients
Conclusions and Future Work

## Slide 17: Registration Issues
NFS traffic is bursty and unpredictable
InfiniBand requires buffers to be registered with the HCA
NFS Buffers must be registered on the fly
Registration is expensive
Client
Server
RPC Call
RPC Reply
RDMA Write
READ Client Buffer Registered
READ Server Buffer Registered
READ Client Buffer Unregistered
READ Server Buffer Unregistered
Critical Path
Critical Path
Critical Path

## Slide 18: Comparison of Registration Strategies
Steps involved in registration
  Convert virtual address to physical addresses
  Pin buffer
  Store virtual to physical addresses in the HCA TPT cache
  Get a steering tag from the HCA
Fast Memory Registration
  Preallocate TPT entries steering tags
  Size and number of available buffers limited
Server buffer registration Cache
  Store the buffer instead of unregistering it
  Reuse the buffer
All Physical Registration
  Only use physical addresses
  Reserved L_Key available to priviliged consumers
  No need to store TPT entry on the HCA
  Maximum limit of 4KB (page size on transfers)
IOzone used for evaluation
  X2200’s (dual Opterons) with 2GB memory and SDR PCI-Express HCA’s
  OpenSolaris bv33 and Linux RHEL 5.0
  Server used a 128 MB memory based file system

## Slide 19: Impact of Registration Strategies-OpenSolaris
Read
Write
Registration Cache READ bandwidth is 730 MB/s
Registration Cache WRITE bandwidth is 515 MB/s

## Slide 20: Impact of Registration Strategies on Linux
Read
Write
Version for kernel 2.6.18 (November 2006) from http://sourceforge.net/projects/nfs-rdma
All Physical READ bandwidth is 876 MB/s
All Physical WRITE bandwidth is 297 MB/s

## Slide 21: Impact of Registration Cache on Filebench (OpenSolaris)
Use the online transaction workload from filebench
Tune the mean I/O size to be 128 KB
Registration Cache improves throughput by upto 50%

## Slide 22: Outline of the talk
Introduction and Motivation
  Network File Systems
  RDMA Operations InfiniBand
Design Issues
  Read-Read Design
  Read-Write Design
  Evaluation of Read-Read versus Read-Write
Registration Strategies
  Issues with Registration
  Techniques to reduce overhead
  Impact of Registration Strategies
Scalability With Multiple Clients
Conclusions and Future Work

## Slide 23: Scalability
Impact of RDMA on an NFS server with multiple clients
Linux NFS/RDMA with All Physical Registration Mode
Intel 3.6 Xeon boxes with an InfiniBand DDR HCA’s
Clients have 4GB memory
Server is configured with 4GB and 8GB memory
Server has eight HighPoint SCSI disks with RAID-0 stripping
SGI XFS file system installed on the server
A 1GB file size per process with a 1MB record size is used for all the experiments.
Compare the aggregate Read bandwidth of 
  Linux NFS/RDMA (RDMA) implementation
  Regular NFS implementation over TCP on InfiniBand (IPoIB)
  Gigabit Ethernet (GigE)

## Slide 24: Scalability
4GB
8GB
NFS/TCP is a bottlneck on current generation systems
NFS/RDMA limited by the performance of the back-end file system

## Slide 25: Outline of the talk
Introduction and Motivation
  Network File Systems
  RDMA Operations InfiniBand
Design Issues
  Read-Read Design
  Read-Write Design
  Evaluation of Read-Read versus Read-Write
Registration Strategies
  Issues with Registration
  Techniques to reduce overhead
  Impact of Registration Strategies
Scalability With Multiple Clients
Conclusions and Future Work

## Slide 26: Conclusions and Future Work
Designed and evaluated an NFS/RDMA protocol for high performance RDMA networks such as InfiniBand
Design is based on a combination of RDMA Read and RDMA Write
The design principles considered include NFS server security, performance and scalability
To improve performance of the protocol, we have incorporated several different registration mechanisms into our design the NFS/RDMA
Design can achieve throughput, close to that of the underlying network and improve throughput of an OLTP workload by 50%
We also studied the scalability of NFS/RDMA with multiple clients.
  NFS/RDMA is limited by the performance of the back-end file system
Would like to study buffer management and credit flow control

## Slide 27: Acknowledgements
Our research is supported by the following organizations
Current Funding support by
Current Equipment support by

## Slide 28: Web Pointers
http://nowlab.cse.ohio-state.edu/
NBC
home page
OpenSolaris NFS/RDMA Project Webpage:
http://nowlab.cse.ohio-state.edu/projects/nfsrdma/