## Slide 1: Analyzing the Impact of Supporting Out-of-order Communication on In-order Performance with iWARP
P. Balaji, W. Feng, S. Bhagvat, D. K. Panda, R. Thakur and W. Gropp
Mathematics and Computer Science, Argonne National Laboratory
Department of Computer Science, Virginia Tech
Scalable Systems Group, Dell Inc.
Computer Science and Engineering, Ohio State University
Computer Science, University of Illinois at Urbana Champagne

## Slide 2: Motivation
High-end computing systems growing rapidly in scale
  128K processor system at LLNL (HPC CPU growth of 50%)
  1M processor systems as soon as next year
Network subsystem has to scale accordingly
  Fault-tolerance and hot-spot avoidance important
Possible Solution: Multi-pathing
  Supported by many networks
    InfiniBand uses subnet management to discover paths
    10-Gigabit Ethernet uses VLAN based multi-pathing
  Disadvantage: Out-of-order Communication!

## Slide 3: Out-of-order Communication
Different packets taking different paths mean that later injected packets might arrive earlier
  Physical networks only deal with sending packets out-of-order
  Protocols on top of networks (either in hardware or software) have to deal with reordering packets
Networks such as IB handle this by dropping out-of-order packets
  FECN, BECN and throttling on congestion
  Network buffering (with FECN/BECN) helps, but not perfect
1
2
3
4
1
2
3
4

## Slide 4: Overview of iWARP over Ethernet
Relatively new initiative by IETF and RDMAC
Backward compatibility with TCP/IP/Ethernet
  Sender stuffs iWARP packets within TCP/IP packets
  When sent, one TCP packet contains one iWARP packet
  What about on receive?
Application
Sockets
SDP, MPI etc.
Software
TCP/IP
10-Gigabit Ethernet
RDMAP Verbs
RDDP
MPA
Offloaded
TCP/IP

## Slide 5: Ethernet Packet Segmentation
Packet
Header
iWARP
Header
Data Payload
Packet
Header
iWARP
Header
Data
Payload
Packet
Header
iWARP
Header
Data
Payload
Packet
Header
iWARP
Header
Partial
Payload
Packet
Header
Partial
Payload
Packet
Header
iWARP
Header
Data
Payload
Packet
Header
iWARP
Header
Data
Payload
Delayed Packet
Out-Of-Order Packets
(Cannot identify iWARP header)
Intermediate Switch Segmentation
Intermediate switch segmentation
  Packets split or coalesced
Current iWARP implementations do not handle out-of-order packets
  Follow approaches used by IB

## Slide 6: Problem Statement
How do we design a feature-complete iWARP stack?
  Provide support for out-of-order arriving packets
  Maintaining performance of in-order communication
What are the tradeoffs in designing iWARP?
  Host-based iWARP
  Host-offloaded iWARP
  Host-assisted iWARP

## Slide 7: Presentation Layout
Introduction and Motivation
Details of the iWARP Standard
Design Choices for iWARP
Experimental Evaluation
Concluding Remarks and Future Work

## Slide 8: Dealing with Out-of-order packets in iWARP
iWARP specifies intelligent approaches to deal with out-of-order packets
Out-of-order data placement and In-order data delivery
  If packets arrive out-of-order, they are directly placed in the appropriate location in memory
  Application notified about the arrival of the message only when:
    All packets of the message have arrived
    All previous messages have arrived
It is necessary that iWARP recognize all packets !

## Slide 9: MPA Protocol Frame
DDP
Header
Payload (IF ANY)
DDP
Header
Payload (IF ANY)
Pad
CRC
Marker
Segment
Length
Deterministic approach to identify packet header
  Can distinguish in-order packets from out-of-order packets

## Slide 10: Presentation Layout
Introduction and Motivation
Details of the iWARP Standard
Design Choices for iWARP
Experimental Evaluation
Concluding Remarks and Future Work

## Slide 11: iWARP components
iWARP consists of three layers
  RDMAP: Thin layer that deals with interfacing upper layers with iWARP
  RDDP: Core of the iWARP stack
    Component 1: Deals with connection management issues and packet de-multiplexing between connections
  MPA: Glue layer to deal with backward compatibility with TCP/IP
    Component 2: Performs CRC
    Component 3: Adds marker strips of data to point to the packet header

## Slide 12: Component Onload vs. Offload
Connection Management and Packet Demultiplexing
  Connection lookup and book-keeping --> CPU intensive
  Can be done efficiently on hardware
Data Integrity: CRC-32
  CPU intensive
  Can be done efficiently on hardware
Marker Strips:
  Tricky as they need to be inserted in between the data
  Software implementation requires an extra copy
  Hardware implementation might require multiple DMAs

## Slide 13: Task distribution for different iWARP designs
RDMAP
RDDP
CRC
Markers
TCP/IP
RDMAP
Markers
TCP/IP
RDDP
CRC
Markers
TCP/IP
RDMAP
RDDP
CRC
HOST
NIC
Host-based
Host-offloaded
Host-assisted

## Slide 14: Host-based and -offloaded Designs
Host-based iWARP: Completely in software
  Deals with overheads for all components
Host-offloaded iWARP: Completely in hardware
  Good for packet demultiplexing and CRC
  Is it good for inserting marker strips?
    Ideal: True Scatter/Gather DMA engine. Not available.
    Contiguous DMA and Decoupled Marker Insertion
      Large chunks DMAed and moved on the NIC to insert markers
      A lot of NIC memory transactions
    Scatter/Gather DMA with Coupled Marker Insertion
      Small chunks DMAed and non-contiguously
      A lot of DMA operations

## Slide 15: Hybrid Host-assisted Implementation
Performs tasks such as:
  packet demultiplexing and CRC in hardware
  marker insertion in software (requires an extra-copy)
Fully utilizes both the host and the NIC
Summary:
  Host-based design suffers from software overheads for all tasks
  Host-offloaded design suffers from the overhead of multiple DMA operations
  Host-based design suffers from the extra memory copy to add the markers but benefits from less DMAs

## Slide 16: Presentation Layout
Introduction and Motivation
Details of the iWARP Standard
Design Choices for iWARP
Experimental Evaluation
Concluding Remarks

## Slide 17: Experimental Test bed
4-node cluster
  2 Intel Xeon 3.0GHz processors with 533MHz FSB, 2GB 266-MHz DDR SDRAM and 133 MHx PCI-X slots
  Chelsio T110 10GE TCP Offload Engines
  12-port Fujitsu XG800 switch
  Red Hat Operating system (2.4.22smp)

## Slide 18: iWARP Microbenchmarks
iWARP Latency
iWARP Bandwidth

## Slide 19: Out-of-cache Communication
iWARP Bandwidth

## Slide 20: Computation Communication Overlap
Message Size 4KB
Message Size 128KB

## Slide 21: Iso-surface Visual rendering application
Data Distribution Size : 8KB
Data Distribution Size : 1MB

## Slide 22: Presentation Layout
Introduction and Motivation
Details of the iWARP Standard
Design Choices for iWARP
Experimental Evaluation
Concluding Remarks

## Slide 23: Concluding Remarks
With growing scales of high-end computing systems, network infrastructure has to scale as well
  Issues such as fault tolerance and hot-spot avoidance play an important role
While multi-path communication can help with these problems, it introduces Out-of-order communication
We presented three designs of iWARP that deal with out-of-order communication
  Each design has its pros and cons
  No single design could achieve the best performance in all cases

## Slide 24: Thank You
Email Contacts:
P. Balaji: balaji@mcs.anl.gov
W. Feng: feng@cs.vt.edu
S. Bhagvat: sitha_bhagvat@dell.com
D. K. Panda: panda@cse.ohio-state.edu
R. Thakur: thakur@mcs.anl.gov
W. Gropp: wgropp@uiuc.edu

## Slide 25: Backup Slides

## Slide 26
IDLE
READY
DMA
BUSY
SDMA
Send
Request
Host
DMA
Free
Host DMA
Busy
Integrated
Segment
Complete
Host DMA
Free
READY
DMA
BUSY
SDMA
Host
DMA
Free
Host DMA
Busy
Host DMA
Free
Marker
Inserted
Segment
Not Complete

## Slide 27
IDLE
READY
DMA
BUSY
SDMA
Host DMA
Free
Send Request
SDMA
Done
Host
DMA
Free
Host DMA
In Use
SDMA
IDLE
READY
COPY
PARTIAL
SEGMENT
INSERT
MARKERS
Segment
Available
Processing
Segment Not
Complete
Marker
Inserted
Segment
Complete
IDLE
Calculate
CRC
Segment
Available
Segment
Complete
IDLE
SEND
Segment
Available
Segment
Complete
CRC
SEND

## Slide 28: iWARP Out-of-Cache Communication Bandwidth
Cache Traffic (Transmit Side)
Cache Traffic (Receive Side)

## Slide 29: Impact of marker separation on iWARP performance
Host-offloaded iWARP Latency
NIC-offloaded iWARP Bandwidth