## Slide 1: Are Nonblocking Networks Needed for High-End Computing Workloads? N. Desai, P. Balaji, P. Sadayappan, M. Islam
Narayan Desai
desai@mcs.anl.gov
Cluster '08
September 29th, 2008

## Slide 2: Switch-based Interconnect Networks
Provide high-performance communication to parallel jobs
  Low latency
  High bandwidth
Constructed from non-blocking switch ASICs into multi-stage switch complexes
  Clos Networks
  Fat Trees
Dominant interconnect architecture
  Except for high-end systems (Blue Gene, Cray)
Bisection bandwidth cost grows non-linearly with port count
  Is this cost justified?
  What is the impact of reduced bisection bandwidth?

## Slide 3: Multi-stage Switch Networks

## Slide 4: Approach
Build a demand model for bisection bandwidth
  Worst case (100% communication)
  Probabilistic model
Reduce available uplink capacity
  Model performance impact on jobs
Process real-world workloads using these models
  Jazz (production system at ANL)
  Atlas (capability system at LLNL)
  Thunder (capacity system at LLNL)

## Slide 5: Probabilistic View of Contention

## Slide 6: Demand Model
Assumption: nodes only communicate with other nodes in the same job
Demand computed on a per-switch ASIC basis
Each job has an uplink demand per ASIC
  min (local job nodes, sum(remote job nodes))
Demand aggregated for simultaneous jobs
  Yields a single uplink demand for each switch ASIC for each time interval
  Describes which ASIC/time intervals would be impacted by uplink reduction

## Slide 7: Uplink Reduction
Remove individual uplinks for each switch ASIC
  Will reduce performance if uplink demand is higher than reduced supply
Reduced performance is the ratio of demand to supply
  i.e., if demand is 6 and supply is 4, interval runtime is extended by 50%
Jobs are slowed down at a uniform pace
  Factor depends on most contended switch
A workload can be analyzed in terms of individual job slowdowns
  Can show overall system impact of uplink removal

## Slide 8: Contended Architecture

## Slide 9: Input Workloads
Jazz system at Argonne
  350 node production cluster
  Capacity workload
  1 core per node
Atlas system at Livermore
  1152 nodes
  Capability workload
  8 cores per node
Thunder system at Livermore
  1024 nodes
  Capacity workload
  4 cores per node

## Slide 10: Analysis
Contention as uplinks are removed
  System-wide impact
  Impact on jobs experiencing contention
Impact of multicore nodes on workloads
Impact of increasing switch size

## Slide 11: System Slowdowns

## Slide 12: Impact of Multi-core Growth

## Slide 13: Conclusions and Future Work
Most workloads don't show much sensitivity to bisection bandwidth reduction
  Most workloads show modest (< 5%) aggregate performance penalty for substantial bisection bandwidth reduction
  Even counting worst-case communication
As switch sizes increase, this penalty decreases on a per-uplink basis
Multi-core systems result in fatter nodes, spreading jobs across fewer nodes and hence fewer network ports
All of these trends suggest that bisection bandwidth will decrease in importance for common workloads over time
Future Work
  Need to take I/O into consideration

## Slide 14: Questions?