## Slide 1: Non-Data-Communication Overheads in MPI: Analysis on Blue Gene/P
P. Balaji, A. Chan, W. Gropp, R. Thakur, E. Lusk
Argonne National Laboratory
University of Chicago
University of Illinois, Urbana Champaign

## Slide 2: Ultra-scale High-end Computing
Processor speeds no longer doubling every 18-24 months
  High-end Computing systems growing in parallelism
Energy usage and heat dissipation are major issues now
  Energy usage is proportional to V2F
  Lots of slow cores use lesser energy than one fast core
Consequence:
  HEC systems rely less on the performance of a single core
  Instead, extract parallelism out of a massive number of low-frequency/low-power cores
  E.g., IBM Blue Gene/L, IBM Blue Gene/P, SiCortex

## Slide 3: IBM Blue Gene/P System
Second Generation of the Blue Gene supercomputers
Extremely energy efficient design using low-power chips
  Four 850MHz cores on each PPC450 processor
Connected using five specialized networks
  Two of them (10G and 1G Ethernet) are used for File I/O and system management
  Remaining three (3D Torus, Global Collective network, Global Interrupt network) are used for MPI communication
    Point-to-point communication goes through the torus network
    Each node has six outgoing links at 425 MBps (total of 5.1 GBps)

## Slide 4: Blue Gene/P Software Stack
Three Software Stack Layers:
  System Programming Interface (SPI)
    Directly above the hardware
    Most efficient, but very difficult to program and not portable !
  Deep Computing Messaging Framework (DCMF)
    Portability layer built on top of SPI
    Generalized message passing framework
    Allows different stacks to be built on top
  MPI
    Built on top of DCMF
    Most portable of the three layers
    Based off of MPICH2 (integrated into MPICH2 as of 1.1a1)

## Slide 5: Issues with Scaling MPI on the BG/P
Large scale systems such as BG/P provide the capacity needed for achieving a Petaflop or higher performance
This system capacity has to be translated to capability for end users
Depends on MPI’s ability to scale to large number of cores
  Pre- and post-data-communication processing in MPI
    Simple computations can be expensive on modestly fast 850 MHz CPUs
    Algorithmic Issues
      Consider an O(N) algorithm with a small proportionality constant
      “Acceptable” on 100 processors; Brutal on 100,000 processors

## Slide 6: MPI Internal Processing Overheads
Application
MPI
Application
MPI
Pre- and Post-data-communication overheads
Application
MPI
Application
MPI

## Slide 7: Presentation Outline
Introduction
Issues with Scaling MPI on Blue Gene/P
Experimental Evaluation
  MPI Stack Computation Overhead
  Algorithmic Inefficiencies
Concluding Remarks

## Slide 8: Basic MPI Stack Overhead
Application
MPI
Application
DCMF
DCMF
MPI
Application
Application
DCMF
DCMF

## Slide 9: Basic MPI Stack Overhead (Results)
Chart: MPI Stack Overhead (Latency)
| 1 | 2 | 4 | 8 | 16 | 32 | 64 | 128 | 256 | 512 | 1K | 2K | 4K
DCMF | 2.0415 | 2.0448 | 2.0434 | 2.0587 | 2.0474 | 2.0519 | 2.1445 | 2.3285 | 3.6755 | 4.3169 | 5.6103 | 8.1793 | 13.9644
MPI | 3.255 | 3.2049 | 3.3111 | 3.2619 | 3.2817 | 3.2723 | 3.4942 | 3.8054 | 4.7771 | 5.6 | 6.9834 | 12.2832 | 17.9186
Chart: MPI Stack Overhead (Bandwidth)
| 1 | 2 | 4 | 8 | 16 | 32 | 64 | 128 | 256 | 512 | 1K | 2K | 4K | 8K | 16K | 32K | 64K | 128K | 256K | 512K | 1M | 2M
DCMF | 4.8287 | 9.6575 | 19.0735 | 37.676 | 76.2939 | 153.5476 | 307.0951 | 606.5606 | 891.8379 | 1825.3505 | 2332.0896 | 2648.3051 | 2677.8063 | 2771.6186 | 2821.0336 | 2846.732 | 2848.8405 | 2855.2665 | 2858.5313 | 2860.1256 | 2860.2687 | 2860.6676
MPI | 3.549 | 7.0797 | 14.1147 | 28.0421 | 56.3694 | 112.4273 | 223.0536 | 444.9185 | 720.6253 | 1370.8934 | 2211.7515 | 2216.3901 | 2438.9422 | 2637.6408 | 2749.9497 | 2809.8971 | 2830.4121 | 2845.9785 | 2853.8205 | 2857.7696 | 2859.0915 | 2860.0781

## Slide 10: Request Allocation and Queuing
Blocking vs. Non-blocking point-to-point communication
  Blocking: MPI_Send() and MPI_Recv()
  Non-blocking: MPI_Isend(), MPI_Irecv() and MPI_Waitall()
Non-blocking communication potentially allows for better overlap of computation with communication, but…
  …requires allocation, initialization and queuing/de-queuing of MPI_Request handles
What are we measuring?
  Latency test using MPI_Send() and MPI_Recv()
  Latency test using MPI_Irecv(), MPI_Isend() and MPI_Waitall()

## Slide 11: Request Allocation and Queuing Overhead
Chart: Request Allocation and Queueing
| 1 | 2 | 4 | 8 | 16 | 32 | 64 | 128 | 256 | 512 | 1K | 2K | 4K
Blocking | 3.0844 | 3.2595 | 3.282 | 3.2633 | 3.2594 | 3.2741 | 3.296 | 3.4715 | 3.7002 | 4.8277 | 5.6163 | 6.9803 | 12.3223
Non-blocking | 3.4737 | 3.6467 | 3.663 | 3.6516 | 3.6531 | 3.6628 | 3.6887 | 3.8747 | 4.1399 | 5.2389 | 6.0177 | 7.4031 | 12.5618
Chart: Percentage Overhead
| 1 | 2 | 4 | 8 | 16 | 32 | 64 | 128 | 256 | 512 | 1K | 2K | 4K
% Overhead | 11.2054 | 10.6171 | 10.4011 | 10.6347 | 10.7763 | 10.6107 | 10.6448 | 10.4047 | 10.6209 | 7.8495 | 6.6703 | 5.7108 | 1.9066

## Slide 12: Derived Datatype Processing
MPI Buffers

## Slide 13: Overheads in Derived Datatype Processing
Chart: Derived Datatype Latency
| 8 | 16 | 32 | 64 | 128 | 256 | 512 | 1K | 2K | 4K | 8K | 16K | 32K
Contiguous | 3.2428 | 3.2307 | 3.2627 | 3.4669 | 3.7388 | 4.8148 | 5.6461 | 7.035 | 12.318 | 17.964 | 28.8279 | 50.6143 | 94.1719
Vector-Char | 5.6878 | 6.2808 | 7.4492 | 9.9504 | 14.9605 | 26.0071 | 45.6045 | 84.4994 | 166.1655 | 322.9875 | 636.9879 | 1267.8261 | 2523.6359
Vector-Short | 5.1934 | 5.2223 | 5.279 | 5.6021 | 6.2141 | 8.2835 | 10.1394 | 13.5739 | 26.3262 | 43.7047 | 81.4646 | 167.5485 | 323.3532
Vector-Int | 5.2011 | 5.219 | 5.2512 | 5.4881 | 5.9773 | 7.8743 | 9.2297 | 11.7389 | 22.1129 | 35.0308 | 63.4362 | 129.2737 | 246.5135
Vector-Double | 4.8745 | 5.1793 | 5.2087 | 5.4435 | 5.8973 | 7.8487 | 9.1988 | 11.6916 | 21.3911 | 33.4569 | 59.0918 | 116.8915 | 222.113
Chart: Derived Datatype Latency (Short Messages)
| 8 | 16 | 32 | 64 | 128
Contiguous | 3.2428 | 3.2307 | 3.2627 | 3.4669 | 3.7388
Vector-Char | 5.6878 | 6.2808 | 7.4492 | 9.9504 | 14.9605
Vector-Short | 5.1934 | 5.2223 | 5.279 | 5.6021 | 6.2141
Vector-Int | 5.2011 | 5.219 | 5.2512 | 5.4881 | 5.9773
Vector-Double | 4.8745 | 5.1793 | 5.2087 | 5.4435 | 5.8973

## Slide 14: Copies with Unaligned Buffers
For 4-byte integer copies:
  Buffer alignments of 0-4 means that the entire integer is in the same double word  to access an integer, you only need to fetch one double word
  Buffer alignments of 5-7 means that the integer spans two double word boundaries  to access an integer, you need to fetch two double words
Double Word
Integer
Integer
Integer

## Slide 15: Buffer Alignment Overhead
Chart: Buffer Alignment Overhead
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
8 bytes | 5.2011 | 5.2025 | 5.1953 | 5.1935 | 5.1925 | 5.1902 | 5.1886 | 5.191
64 bytes | 5.4881 | 5.488 | 5.4933 | 5.4913 | 5.4922 | 5.5197 | 5.519 | 5.5108
512 bytes | 9.2297 | 9.2316 | 9.2276 | 9.2325 | 9.2348 | 9.453 | 9.4555 | 9.4569
4 Kbytes | 35.0308 | 35.0713 | 35.0304 | 35.0604 | 35.0677 | 37.2558 | 37.1875 | 37.1726
32 Kbytes | 246.5135 | 246.5329 | 246.5311 | 246.5206 | 246.5248 | 263.3844 | 263.383 | 263.3937
Chart: Buffer Alignment Overhead (without 32Kbytes)
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
8 bytes | 5.2011 | 5.2025 | 5.1953 | 5.1935 | 5.1925 | 5.1902 | 5.1886 | 5.191
64 bytes | 5.4881 | 5.488 | 5.4933 | 5.4913 | 5.4922 | 5.5197 | 5.519 | 5.5108
512 bytes | 9.2297 | 9.2316 | 9.2276 | 9.2325 | 9.2348 | 9.453 | 9.4555 | 9.4569
4 Kbytes | 35.0308 | 35.0713 | 35.0304 | 35.0604 | 35.0677 | 37.2558 | 37.1875 | 37.1726

## Slide 16: Thread Communication
Multiple threads calling MPI can corrupt the stack
MPI uses locks to serialize access to the stack
  Current locks are coarse grained  protect the entire MPI call
  Implies these locks serialize communication for all threads
MPI
MPI
MPI
MPI
MPI
Four MPI processes
Four threads in one MPI process

## Slide 17: Overhead of Thread Communication
Chart: Threads vs. Processes
| 1 | 2 | 3 | 4
Threads | 0.991 | 0.85 | 0.834 | 0.824
Processes | 4.47 | 8.933 | 13.404 | 17.878

## Slide 18: Presentation Outline
Introduction
Issues with Scaling MPI on Blue Gene/P
Experimental Evaluation
  MPI Stack Computation Overhead
  Algorithmic Inefficiencies
Concluding Remarks

## Slide 19: Tag and Source Matching
Search time in most implementations is linear with respect to the number of requests posted
Source = 1
Tag = 1
Source = 1
Tag = 2
Source = 2
Tag = 1
Source = 0
Tag = 0

## Slide 20: Overheads in Tag and Source Matching
Chart: Tag Matching Overhead vs. Number of Requests
| 0 | 1 | 2 | 4 | 8 | 16 | 32 | 64 | 128 | 256 | 512 | 1024
Latency | 1.6515 | 1.6668 | 1.6994 | 1.7873 | 1.9749 | 2.7405 | 3.4155 | 4.5839 | 7.985 | 13.9861 | 35.4397 | 77.2832
Chart: Tag Matching Overhead vs. Peers
| 4 | 8 | 16 | 32 | 64 | 128 | 256 | 512 | 1024 | 2048 | 4096
 | 1.745 | 2.9466 | 5.7283 | 22.0483 | 51.4625 | 153.8069 | 585.9611 | 2251.7051 | 8227.7328 | 31542.1897 | 136260.5111

## Slide 21: Unexpected Message Overhead
Chart: Unexpected Message Overhead vs. Number of Requests
| 0 | 1 | 2 | 4 | 8 | 16 | 32 | 64 | 128 | 256 | 512 | 1024
 | 2.3215 | 1.3696 | 1.3844 | 1.4543 | 1.7058 | 1.9045 | 2.4509 | 3.5513 | 5.9961 | 11.3944 | 21.976 | 43.1892
Chart: Unexpected Message Overhead vs. Peers
| 4 | 8 | 16 | 32 | 64 | 128 | 256 | 512 | 1024 | 2048 | 4096
 | 5.4207 | 9.7102 | 21.2093 | 42.1628 | 85.1018 | 178.3913 | 388.3143 | 824.0752 | 1716.3327 | 3478.8153 | 7004.4716

## Slide 22: Multi-Request Operations
Chart: Waitany Time
| 1 | 2 | 4 | 8 | 16 | 32 | 64 | 128 | 256 | 512 | 1024 | 2048 | 4096 | 8192
 | 1.7528 | 1.7869 | 1.8826 | 2.0565 | 3.3401 | 4.9547 | 8.8418 | 17.9593 | 33.2048 | 108.0688 | 243.86 | 500.112 | 1084.7086 | 1795.0048

## Slide 23: Presentation Outline
Introduction
Issues with Scaling MPI on Blue Gene/P
Experimental Evaluation
  MPI Stack Computation Overhead
  Algorithmic Inefficiencies
Concluding Remarks

## Slide 24: Concluding Remarks
Systems such as BG/P provide the capacity needed for achieving a Petaflop or higher performance
System capacity has to be translated to end-user capability
  Depends on MPI’s ability to scale to large number of cores
We studied the non-data-communication overheads in MPI on BG/P
  Identified several bottleneck possibilities within MPI
  Stressed these bottlenecks with benchmarks
  Analyzed the reasons behind such overheads

## Slide 25: Thank You!
Contact:
Pavan Balaji: balaji@mcs.anl.gov
Anthony Chan: chan@mcs.anl.gov
William Gropp: wgropp@illinois.edu
Rajeev Thakur: thakur@mcs.anl.gov
Rusty Lusk: lusk@mcs.anl.gov
Project Website: http://www.mcs.anl.gov/research/projects/mpich2