## Slide 1: Evaluation of ConnectX Virtual Protocol Interconnect for Data Centers
Ryan E. Grant Ahmad Afsahi Pavan Balaji
Department of Electrical and Computer Engineering, Queen’s University
Mathematics and Computer Science, Argonne National Laboratory

## Slide 2: Data Centers: Towards a unified network stack
High End Computing (HEC) systems proliferating into all domains
  Scientific Computing has been the traditional “big customer”
  Enterprise Computing (large data centers) is increasingly becoming a competitor as well
    Google’s data centers
    Oracle’s investment in high speed networking stacks (mainly through DAPL and SDP)
    Investment from financial institutes such as Credit Suisse in low-latency networks such as InfiniBand
A change of domain always brings new requirements with it
  A single unified network stack is the holy grail!
  Maintaining density and power, while achieving high performance

## Slide 3: InfiniBand and Ethernet in Data Centers
Ethernet has been the network of choice for data centers
  Ubiquitous connectivity to all external clients due to backward compatibility
    Internal communication, external communication and management are all unified on to a single network
    There has also been a push for power to be distributed on the same channel as well (using Power over Ethernet), but that’s still not a reality
InfiniBand (IB) in data centers
  Ethernet is (arguably) lagging behind with respect to some of the features provided by other high-speed networks such as IB
    Bandwidth (32 Gbps vs. 10 Gbps today), features (scalability features such as shared queues while using zero-copy communication and RDMA)
    The point of this paper is not about which is better, but to deal with the fact that data centers are looking for ways to converge both technologies

## Slide 4: Convergence of InfiniBand and Ethernet
Researchers have been looking at different ways for a converged InfiniBand/Ethernet fabric
  Virtual Protocol Interconnect (VPI)
  InfiniBand over Ethernet (or RDMA over Ethernet)
  InfiniBand over Converged Enhanced Ethernet (or RDMA over CEE)
VPI is the first convergence model introduced by Mellanox Technologies, and will be the focus of study in this paper

## Slide 5: Virtual Protocol Interconnect (VPI)
Single network firmware to support both IB and Ethernet
Autosensing of layer-2 protocol
  Can be configured to automatically work with either IB or Ethernet networks
Multi-port adapters can use one port on IB and another on Ethernet
Multiple use modes:
  Data centers with IB inside the cluster and Ethernet outside
  Clusters with IB network and Ethernet management
IB Link Layer
IB Port
Ethernet Port
Hardware
TCP/IP support
Ethernet
Link Layer
IB Network
Layer
IP
IB Transport
Layer
TCP
IB Verbs
Sockets
Applications

## Slide 6: Goals of this paper
To understand the performance and capabilities of VPI
Comparison of VPI-IB with VPI-Ethernet with different software stacks
  Openfabrics Verbs
  TCP/IP sockets (both traditional and through the Sockets Direct Protocol)
Detailed studies with micro-benchmarks and a Enterprise Data center setup

## Slide 7: Presentation Roadmap
Introduction
Micro-benchmark based Performance Evaluation
Performance Analysis of Enterprise Data Centers
Concluding Remarks and Future Work

## Slide 8: Software Stack Layout
Sockets Application
Sockets API
Kernel
TCP/IP Sockets Provider
TCP/IP Transport Driver
Driver
User
VPI capable Network Adapter
Sockets Direct Protocol
(Possible) Kernel Bypass
RDMA Semantics
Verbs Application
Verbs API
Ethernet
InfiniBand
Zero-copy Communication

## Slide 9: Software Stack Layout (details)
Three software stacks: TCP/IP, SDP and native verbs
  VPI-Ethernet can only use TCP/IP
  VPI-IB can use any one of the three
TCP/IP and SDP provide transparent portability for existing data center applications over IB
  TCP/IP is more mature (preferable for conservative data centers)
  SDP can (potentially) provide better performance:
    Can internally use more of IB features than TCP/IP, since it natively utilizes IB’s hardware implemented protocol (network and transport)
    But is not as mature: parts of the stack not as optimized as TCP/IP
Native verbs is also a possibility, but requires modifications to existing data center applications (studies by Panda’s group)

## Slide 10: Experimental Setup
Four Dell PowerEdge R805 SMP servers
Each server has two quad-core 2.0 GHz AMD Opteron processors
  12 KB instruction cache and 16 KB L1 data cache on each core
  512 KB L2 cache for each core
  2MB L3 cache on chip
8 GB DDR2 SDRAM on an 1800 MHz memory controller
Each node has one ConnectX VPI capable adapter (4X DDR IB and 10Gbps Ethernet) on a PCIe x8 bus
Fedora Core 5 (linux kernel 2.6.20) was used with OFED 1.4
Compiler: gcc-4.1.1

## Slide 11: One-way Latency and Bandwidth
Chart: Latency
| 1 | 2 | 4 | 8 | 16 | 32 | 64 | 128 | 256 | 512 | 1024
IPoIB | 20.6 | 20.6 | 20.7 | 20.7 | 20.8 | 20.8 | 20.7 | 20.8 | 21.6 | 22 | 23
SDP | 8.38 | 8.53 | 8.68 | 8.66 | 8.69 | 8.74 | 8.92 | 9.29 | 9.5 | 10.1 | 11
10GE (AIC-Rx on) | 13.6 | 13.7 | 13.7 | 13.8 | 13.9 | 13.8 | 14.2 | 14.5 | 14.4 | 15.3 | 16.8
10GE (AIC-Rx off) | 25.2 | 25.2 | 25.9 | 25.7 | 25.9 | 26.2 | 26.1 | 26.2 | 26.8 | 27.9 | 28.7
Native Verbs | 1.22 | 1.24 | 1.22 | 1.25 | 1.27 | 2.18 | 2.28 | 2.57 | 2.91 | 3.2 | 4.04
Chart: Bandwidth
| 1 | 2 | 4 | 8 | 16 | 32 | 64 | 128 | 256 | 512 | 1K | 2K | 4K | 8K | 16K | 32K | 64K | 128K | 256K | 512K | 1M
IPoIB | 19 | 39.01 | 79.61 | 191.95 | 370.34 | 718.81 | 1392.86 | 2645.61 | 4991.39 | 8413.65 | 7791.18 | 7619.14 | 7651.66 | 7793.25 | 7637.62 | 7786.13 | 7786.73 | 7642.89 | 7645.99 | 7771.58 | 7724.45
SDP | 4.44 | 8.93 | 18.26 | 37.52 | 79.63 | 165.56 | 331.86 | 816.99 | 1987.17 | 4763.49 | 5908.81 | 7811.77 | 6092.09 | 6856.4 | 11617.18 | 11685.91 | 9147.94 | 10771.22 | 11349.8 | 11701.53 | 11873.95
10GE | 15.67 | 32.87 | 66.71 | 140.7 | 325.68 | 634.91 | 1404.8 | 2593.3 | 4464.04 | 6871.86 | 9407.26 | 9907.77 | 9908.1 | 9908 | 9907.58 | 9907.6 | 9907.74 | 9907.72 | 9908.04 | 9902.14 | 8572.27
Native Verbs | 24.97 | 50.48 | 99.85 | 263.69 | 407.25 | 810.82 | 1614.5 | 3168.26 | 6180.3 | 10320.08 | 11379.36 | 11909.52 | 12259.12 | 12446.96 | 12541.68 | 12566 | 12622.88 | 12625.12 | 12632.16 | 12633.68 | 12634.32

## Slide 12: Multi-stream Bandwidth
Chart: 10GE
| 1 | 2 | 4 | 8 | 16 | 32 | 64 | 128 | 256 | 512 | 1K | 2K | 4K | 8K | 16K | 32K | 64K | 128K | 256K | 512K | 1M
2 streams | 29.45 | 57.12 | 118.42 | 248.4 | 593.02 | 1137.18 | 2641.5 | 4691.95 | 7657.98 | 9908.72 | 9905.28 | 9905.83 | 9905.33 | 9905.36 | 9904.24 | 9903.26 | 9902.96 | 9904.91 | 9905.89 | 9897.83 | 9905.57
3 streams | 45.21 | 86.19 | 177.26 | 368.6 | 846.13 | 1663.98 | 3885.43 | 6752.45 | 9909.03 | 9906.94 | 9901.49 | 9849.02 | 9863.91 | 9870.62 | 9858.09 | 9861.62 | 9869.88 | 9859.97 | 9903.96 | 9840 | 9819.89
4 streams | 61.98 | 123.08 | 250.3 | 405.96 | 1232.89 | 2239.34 | 5092.68 | 8740.59 | 9909.06 | 9902.77 | 9879.29 | 9871.91 | 9873.95 | 9863.06 | 9862.21 | 9872.65 | 9867.9 | 9857.73 | 9859.54 | 9849.9 | 9831.7
5 streams | 82.75 | 162.85 | 400.91 | 709 | 1125.07 | 3447.56 | 6296.23 | 9907.49 | 9910.48 | 9906.1 | 9891.44 | 9866.01 | 9862.49 | 9870.73 | 9862.32 | 9859.77 | 9866.14 | 9862.73 | 9850.57 | 9835.59 | 9841.99
6 streams | 101.49 | 199.46 | 411.4 | 857.78 | 1764.29 | 4091 | 7411.36 | 9907.8 | 9910.53 | 9907.09 | 9886.51 | 9879.15 | 9858.8 | 9852.32 | 9872.21 | 9856.39 | 9850.84 | 9871.89 | 9849.6 | 9810.9 | 9831.3
7 streams | 117.78 | 232.59 | 470.57 | 1001.49 | 2074.93 | 4764.31 | 8542.81 | 9913.27 | 9912.09 | 9908.09 | 9883.52 | 9867.94 | 9870.3 | 9853.06 | 9852.61 | 9869.13 | 9846.5 | 9849.35 | 9859.43 | 9780.58 | 9778.88
8 streams | 135.38 | 267.18 | 535.33 | 1152.3 | 2357.34 | 5395.43 | 9597.96 | 9911.8 | 9911.39 | 9907.72 | 9888.6 | 9858.19 | 9861.63 | 9864 | 9848.04 | 9857.25 | 9865.61 | 9841.96 | 9839.59 | 9820.56 | 9765.62
Chart: IPoIB
| 1 | 2 | 4 | 8 | 16 | 32 | 64 | 128 | 256 | 512 | 1K | 2K | 4K | 8K | 16K | 32K | 64K | 128K | 256K | 512K | 1M
2 streams | 36.73 | 77.37 | 87.38 | 367.69 | 709.49 | 1307.36 | 2617.39 | 5035.72 | 8988.79 | 10902.19 | 10858.44 | 10861.42 | 10843.38 | 10836.06 | 10823.22 | 10814.07 | 10811.83 | 10803.63 | 10816.06 | 10716.41 | 10512.63
3 streams | 55.37 | 111.94 | 259.41 | 545.81 | 713.17 | 2005.3 | 3839.75 | 7273.02 | 10950.19 | 10878.72 | 10841.74 | 10850.81 | 10821.55 | 10716.18 | 10712.21 | 10702.91 | 10799.77 | 10807.5 | 10782.48 | 10677.97 | 10509.9
4 streams | 79.45 | 162.78 | 352.93 | 728.51 | 1390.2 | 2704.08 | 5127.02 | 10009.32 | 10930.81 | 10869.46 | 10835.57 | 10822.51 | 10827.09 | 10789.2 | 10794.78 | 10787.73 | 10774.73 | 10797.55 | 10783.58 | 10648.83 | 10491.34
5 streams | 100.94 | 207.1 | 440.79 | 903.33 | 1721.32 | 3303.27 | 6353.68 | 10946.76 | 10923.18 | 10859.6 | 10828.26 | 10813.61 | 10806.53 | 10788.64 | 10789.58 | 10786.5 | 10774.62 | 10793.18 | 10764.42 | 10631.12 | 10482.46
6 streams | 123.13 | 174.37 | 526.26 | 697.15 | 1736.9 | 4018.5 | 7741.35 | 10946.28 | 10922.06 | 10852.23 | 10815.78 | 10816.76 | 10791.55 | 10800.67 | 10790 | 10771.98 | 10806.88 | 10765.75 | 10764.96 | 10636.12 | 10458.57
7 streams | 146.58 | 297.17 | 611.02 | 1252.96 | 2088.74 | 4734.86 | 8991.65 | 10942.54 | 10919.28 | 10850.74 | 10822.92 | 10818.69 | 10793.73 | 10805.85 | 10785.65 | 10784.66 | 10776.37 | 10766.36 | 10766.44 | 10634.69 | 10457.91
8 streams | 167.4 | 346 | 621.25 | 1430.81 | 2837.05 | 4719.67 | 10337.82 | 10940.51 | 10916.59 | 10870.7 | 10816.02 | 10834.17 | 10837.62 | 10797.27 | 10700.34 | 10691.2 | 10685.18 | 10781.3 | 10777.53 | 10631.26 | 10474.08
Chart: SDP
| 1 | 2 | 4 | 8 | 16 | 32 | 64 | 128 | 256 | 512 | 1K | 2K | 4K | 8K | 16K | 32K | 64K | 128K | 256K | 512K | 1M
2 streams | 20.59 | 41.35 | 89.6 | 172.41 | 365.93 | 709.7 | 1436.01 | 2970.31 | 5472.57 | 9621.03 | 11349.16 | 10518.09 | 8780.6 | 8373.25 | 11656.88 | 11654.62 | 9882.59 | 11048.15 | 11414.1 | 11748.52 | 11973.08
3 streams | 36.32 | 107.39 | 141.86 | 452.37 | 733.66 | 1462.54 | 2737.04 | 5099.8 | 9234.52 | 11443.98 | 11543.75 | 11289.93 | 10267.37 | 10277.74 | 11604.61 | 11626.79 | 10201.11 | 12411.58 | 12425.85 | 12486.67 | 11958.69
4 streams | 68.28 | 136.68 | 278.79 | 573.38 | 1134.39 | 2150.36 | 3925.71 | 7225.02 | 11426.74 | 11359.08 | 11573.27 | 11369.25 | 10996.17 | 11042.9 | 11579.62 | 11617.61 | 12100.84 | 12370.4 | 12473.33 | 12426.23 | 12011.86
5 streams | 93.61 | 184.67 | 276.86 | 822.41 | 1506.49 | 2135.58 | 5126.32 | 9369.64 | 11510 | 11514.34 | 11520.19 | 11335.24 | 11188.83 | 11320.14 | 11535.7 | 11605.83 | 12213.3 | 12479.23 | 12514.9 | 12510.27 | 12029.66
6 streams | 122.56 | 239.61 | 493.24 | 1036.96 | 1853.52 | 3513.58 | 6346.8 | 11478.26 | 11504.83 | 11494.33 | 11497.43 | 11324.45 | 11230.44 | 11343.6 | 11562.85 | 11588.41 | 12158.29 | 12393.89 | 12328.03 | 12494.05 | 12032.45
7 streams | 140.68 | 277 | 555.49 | 1160.29 | 2265.78 | 3531.6 | 7502.01 | 11483.18 | 11488.36 | 11466.86 | 11453.91 | 11292.7 | 11237.17 | 11290.53 | 11503.93 | 11580.33 | 12189.76 | 12537.41 | 12504.53 | 12497.73 | 12132.36
8 streams | 141.23 | 275.87 | 560.73 | 1256.32 | 2261.59 | 4284 | 7684.89 | 11468.09 | 11455.57 | 11432.57 | 11499.09 | 11267.84 | 11201.04 | 11218.12 | 11468.57 | 11497.5 | 12224.33 | 12511.67 | 12504.26 | 12580.32 | 12258.29

## Slide 13: Simultaneous IB/10GE Communication
Chart: 10GE/IPoIB
| 1 | 2 | 4 | 8 | 16 | 32 | 64 | 128 | 256 | 512 | 1K | 2K | 4K | 8K | 16K | 32K | 64K | 128K | 256K | 512K | 1M
10GE (1 stream) | 13.13 | 29.57 | 66.04 | 135.92 | 313.08 | 592.3 | 1373.33 | 2405.56 | 4350.35 | 6058.49 | 6068.93 | 5934.08 | 5099.84 | 4966.67 | 4955.28 | 5031.03 | 5058.11 | 4978.88 | 5029.64 | 5183.05 | 5307.96
10GE (2 streams) | 30.46 | 61.62 | 180.31 | 252.48 | 578.29 | 1098.03 | 2572.57 | 4516.76 | 5332.73 | 3892.58 | 3985.83 | 3995.26 | 4110.4 | 4127.81 | 4158.85 | 3987.08 | 4111.78 | 4159.71 | 4129.9 | 3942.22 | 3901.9
10GE (3 streams) | 47.81 | 93.07 | 237.24 | 440.05 | 899.18 | 1765.37 | 2593.44 | 6263.93 | 3651.61 | 3681.17 | 3726.6 | 3747.31 | 3727.07 | 3723.04 | 3749.91 | 3798.71 | 3769.06 | 3753.23 | 3725.99 | 3717.42 | 4048.7
10GE (4 streams) | 75.55 | 128.76 | 265.87 | 592.21 | 1219.21 | 2430.18 | 2624.59 | 3692 | 3622.08 | 3622.58 | 3672.07 | 3676.73 | 3707 | 3681.6 | 3690.31 | 3707.94 | 3733.42 | 3684.48 | 3661.12 | 3627.2 | 3622.95
IPoIB (1 stream) | 20.82 | 36.47 | 63.94 | 189.74 | 345.39 | 634.92 | 1364.5 | 2775.19 | 4962.6 | 5864.16 | 5666.02 | 5740.59 | 6268.32 | 6294.51 | 6307.29 | 6342.96 | 6325.03 | 6287.87 | 6230.56 | 6141.75 | 6159.33
IPoIB (2 streams) | 38.56 | 77.96 | 171.18 | 341.06 | 659.22 | 1344.95 | 2732.73 | 5357.49 | 6361.48 | 7410.79 | 7202.04 | 7184.64 | 7130.81 | 7092.95 | 7077.99 | 7172.52 | 7046 | 7113.5 | 7163.51 | 7022.84 | 6947.09
IPoIB (3 streams) | 60.6 | 124.71 | 246.04 | 511.62 | 934.97 | 1988.87 | 2683.39 | 5759.86 | 7693.39 | 7498.94 | 7524.7 | 7476.07 | 7353.5 | 7359.08 | 7383.58 | 7452.82 | 7382.47 | 7316.79 | 7322.15 | 7268.36 | 7105.6
IPoIB (4 streams) | 72.78 | 172.9 | 270.66 | 659.94 | 1334.7 | 2624.59 | 5717.33 | 7928.69 | 7733.18 | 7837.22 | 7539.41 | 7516.91 | 7440.92 | 7405.93 | 7370.61 | 7417.43 | 7498.91 | 7375.45 | 7448.65 | 7251.21 | 7137.62
Aggregate | 148.33 | 301.66 | 536.53 | 1252.15 | 2553.91 | 5054.77 | 8341.92 | 12023.79 | 11694.21 | 11459.8 | 11251.3 | 11223.38 | 11241.21 | 11220.76 | 11236.84 | 11251.53 | 11232.33 | 11273.21 | 11293.41 | 10985.78 | 11154.3
Chart: 10GE/SDP
| 1 | 2 | 4 | 8 | 16 | 32 | 64 | 128 | 256 | 512 | 1K | 2K | 4K | 8K | 16K | 32K | 64K | 128K | 256K | 512K | 1M
10GE (1 stream) | 16.23 | 32.57 | 66.41 | 137.66 | 306.7 | 604.03 | 1379.3 | 2549.49 | 4357.78 | 6609.88 | 6659.43 | 6217.9 | 6068.29 | 6087.72 | 5316.97 | 5230.73 | 7649.02 | 5737.05 | 6094.25 | 5926.53 | 5789.88
10GE (2 streams) | 33.56 | 67.76 | 135.38 | 288.07 | 605.72 | 1203.94 | 2602.98 | 4618.12 | 6866.54 | 4195.85 | 4217.14 | 4365.58 | 4488.63 | 4742.63 | 4426.48 | 4404.13 | 6019.9 | 5155.2 | 4783.08 | 4772.13 | 5033.89
10GE (3 streams) | 56.4 | 113.37 | 229.79 | 602.49 | 936 | 1494.33 | 3841.46 | 6605.55 | 4069.13 | 4017.21 | 4046.82 | 4145.38 | 4136.49 | 4177.78 | 4129.25 | 4250.85 | 4886.63 | 4618.82 | 4438.25 | 4351.48 | 4784.11
10GE (4 streams) | 75.59 | 148.33 | 297.59 | 635.68 | 1287.51 | 2519.17 | 5043.13 | 4151.02 | 4254.11 | 4031.24 | 4031.79 | 4086.4 | 4115.61 | 4241.68 | 4169.5 | 4140.23 | 4896.74 | 4458.91 | 4352.83 | 4327.06 | 4669.55
SDP (1 stream) | 7.89 | 15.73 | 32.8 | 71.41 | 135.54 | 277.32 | 827.41 | 2172.54 | 3845.77 | 5749.83 | 5607.95 | 5997.41 | 5973.34 | 5839.92 | 6853.73 | 6695.58 | 4609.82 | 6642.04 | 6201.57 | 6615.89 | 6786.7
SDP (2 streams) | 31.75 | 62.62 | 127.26 | 273.15 | 531.61 | 1043.65 | 1929.18 | 4160.32 | 5563.84 | 7851.42 | 7804.85 | 7677.03 | 7470.09 | 7292.9 | 7535.49 | 7534.91 | 6291.04 | 7211.16 | 7737.52 | 7698.71 | 7463.37
SDP (3 streams) | 54.59 | 110.73 | 219.61 | 533.6 | 927.26 | 1890.53 | 3318.47 | 5826.48 | 8283.08 | 7974.89 | 7898.08 | 7873.45 | 7761.9 | 7717.76 | 7747.86 | 7892.32 | 7511.76 | 7822.48 | 8106.54 | 8074.28 | 7673.55
SDP (4 streams) | 63.13 | 124.04 | 244.96 | 521.48 | 1009.84 | 1963.61 | 3520.11 | 8182.3 | 8187.78 | 8141.77 | 7965.43 | 7965.13 | 7937.07 | 7808.82 | 7939.54 | 7735.72 | 7416.33 | 7964.57 | 8072.88 | 8074.47 | 7771.32
Aggregate | 138.72 | 272.37 | 542.55 | 1157.16 | 2297.35 | 4482.78 | 8563.24 | 12432.03 | 12441.89 | 12173.01 | 12021.99 | 12051.53 | 12052.68 | 12050.5 | 12109.04 | 12143.17 | 12398.39 | 12441.3 | 12544.79 | 12470.84 | 12497.26

## Slide 14: Presentation Roadmap
Introduction
Micro-benchmark based Performance Evaluation
Performance Analysis of Enterprise Data Centers
Concluding Remarks and Future Work

## Slide 15: Data Center Setup
Three-tier data center
  Apache 2 web server for static content
  JBoss 5 application server for server-side java processing
  MySQL database system
Trace workload: TPC-W benchmark representing a real web-based bookstore
Client
Web Server
(Apache)
Application Server
(JBoss)
Database Server
(MySQL)
10GE
10GE/IPoIB/SDP
10GE/IPoIB/SDP

## Slide 16: Data Center Throughput
Chart: Time (seconds)
Average
82.23
Average
87.15
Average
85.08

## Slide 17: Data Center Response Time (Itemized)
10GE
10GE/IPoIB
10GE/SDP

## Slide 18: Presentation Roadmap
Introduction
Micro-benchmark based Performance Evaluation
Performance Analysis of Enterprise Data Centers
Concluding Remarks and Future Work

## Slide 19: Concluding Remarks
Increasing push for a converged network fabric
  Enterprise data centers in HEC: power, density and performance
Different convergence technologies upcoming: VPI was one of the first such technology introduced by Mellanox
We studied the performance and capabilities of VPI with micro-benchmarks and an enterprise data center setup
  Performance numbers indicate that VPI can give a reasonable performance boost to data centers without overly complicating the network infrastructure
  What’s still needed? Self-adapting switches
    Current switches either do IB or 10GE, not both
    On the roadmap for several switch vendors

## Slide 20: Future Work
Improvements to SDP (of course)
We need to look at other convergence technologies as well
  RDMA over Ethernet (or CEE) is upcoming
    Already accepted into the Open Fabrics Verbs
    True convergence with respect to verbs
      InfiniBand features such as RDMA will automatically migrate to 10GE
      All the SDP benefits will translate to 10GE as well

## Slide 21: Funding Acknowledgments
Natural Sciences and Engineering Research Council of Canada
Canada Foundation of Innovation and Ontario Innovation Trust
US Office of Advanced Scientific Computing Research (DOE ASCR)
US National Science Foundation (NSF)
Mellanox Technologies

## Slide 22: Thank you!
Contacts:
Ryan Grant: ryan.grant@queensu.ca
Ahmad Afsahi: ahmad.afsahi@queensu.ca
Pavan Balaji: balaji@mcs.anl.gov

## Slide 23: Backup Slides

## Slide 24: Data Center Response Time (itemized)
Chart: 10GE
Chart: 10GE/IPoIB
Chart: 10GE/SDP