## Slide 1: Understanding Power Measurement Implications in the Green500 List
Balaji Subramaniam and Wu-chun Feng*

## Slide 2: Future of High-Performance Computing
Source: DARPA IPTO

## Slide 3: Future of High-Performance Computing
HPC is energy/power limited

## Slide 4
Notes: All the supercomputers are huge and draw a lot of power (e.g. Jaguar = 6.9MW power).

## Slide 5: Energy Awareness in HPC
Green500 List
  Benchmark: high-performance LINPACK (HPL)1
  Metric: FLOPS2/Watt
Portable implementation of the LINPACK benchmark for distributed memory systems
Floating point operations per second
Energy efficiency as a first order design constraint

## Slide 6: Motivation(1)
Power Measurement in HPC
  Cannot measure the power of entire supercomputer
    Currently lack such infrastructure
  Cannot measure power for the entire benchmark run
    Jaguar runs HPL for 18 hrs1
    Roadrunner takes 2 hrs1
Caveat:
Cannot improve/manage what we cannot measure
Source: J. Dongarra, LINPACK Benchmark with Time Limits on Multicore & GPU Based Accelerators, ISC’10

## Slide 7: Motivation (2)
Solution
  Measure only fraction of the benchmark run
  Extrapolate system power from a sub-component power

## Slide 8: Motivation (3)
Caveats
Source: J. Dongarra, LINPACK Benchmark with Time Limits on Multicore & GPU Based Accelerators, ISC’10
HPL run on Jaguar supercomputer
Notes: In LU factorization the number of computations done in each step varies as the number of elements to update each time reduces. Therefore performance varies a lot during LINPACK runs as shown in the jaguar figure

## Slide 9: Motivation (4)
Unanswered question
  What power consumption needs to be measured?
    Ex: peak, minimum or average
  When should the power be measured?
  How should the power be measured?
    Ex: extrapolation

## Slide 10: Outline
Background and Motivation
Overview of HPL
Experimental Results
Summary and Future Work

## Slide 11: HPL Overview
Solve linear system of equation of form Ax=b
Double precision arithmetic
Algorithm phases
  Input matrix generation
  Factorize and solve
  Check for correctness
Floating point operations for second phase is given by:
FLOPS = 2/3*N3 + 3/2*N2

## Slide 12: Experimental Setup
Armor (single node)
  2 quad-core Intel Xeon E5405
  4 GB memory
Ice (8 node)
  2 dual-core AMD Opteron 2218
  4 GB memory
HPL-2.0, BLAS: ATLAS
Power Meter: Watts Up? Pro ES
DVFS techniques are *not* used
Notes: Systemg per node config… used gcc with –o3 but no need to stress as we are not comparing performance

## Slide 13: Experimental Results
Notes: Matrix input generation
Factorize and solve
Check for correctness

## Slide 14: Experimental Results

## Slide 15: Experimental Results
What to measure
  Power consumed by second phase is stable
  Average is the best estimate
When to measure?
  Measuring from 50 to 70% of the execution time in HPL would give a good estimate

## Slide 16: Experimental Results

## Slide 17: Experimental Results
How to measure?
  Similar power profiles for all nodes
  Extrapolation is valid

## Slide 18: Summary and Future Work
Cannot improve what we cannot manage
Power measurement methodology for Green500 list
  What, when and how to measure
Future work
  Refining run rules based on community feedback
  Methodology to include network power

## Slide 19: Experimental Setup
Armor (single node)
  2 quad-core Intel Xeon E5405
  4 GB memory
Ice (8 node)
  2 dual-core AMD Opteron 2218
  4 GB memory
Cuda
  Intel Core 2 Duo + Tesla C2050
  4GB Memory
HPL-2.0, BLAS: ATLAS
Power Meter: Watts Up? Pro ES
DVFS techniques are *not* used
Notes: Systemg per node config… used gcc with –o3 but no need to stress as we are not comparing performance

## Slide 20
Notes: The matrix generation and check phase are on CPU and we see a longer execution time for first and third phase than CPU. We can also see the power in the second phase reducing over time. This is because the required computations for LU reduces overtime.
When to measure power: With heterogeneous systems the computations take less time than the matrix generation and check for correctness phase. But it is safe to assume that the LU computation would have started at 40% of execution. So it would be better if we start at 40% and end our measurement at 50%

## Slide 21
Tianhe 1A (Top500 rank =1)
  Peak Power = 4.46 MW
  Power Consumed = 4.04 MW
Jaguar (Top500 rank =2)
  Peak Power = 9.03 MW
  Power Consumed = 6.90 MW
Nebulae (Top500 rank =3)
  Peak Power = 3.04 MW
  Power Consumed = 2.58 MW
Hopper (Top500 rank =5)
  Peak Power = 3.62 MW
  Power Consumed = 2.91 MW
Notes: Tianhe – GPU based - from processor and GPU TDP * 1.5
Jaguar – CPU based - from cabinet power
Nebulae - GPU based - from processor and GPU TDP * 1.5
Hopper – CPU based - from cabinet power