## Slide 1: Dynamic Time Variant Connection Management for PGAS Models on InfiniBand
Abhinav Vishnu1, Manoj Krishnan1
and Pavan Balaji2
1Pacific Northwest National Laboratory
Richland, WA
2Argonne National Laboratory
Argonne, IL

## Slide 2: Outline
Introduction
Background and Motivation
  InfiniBand Connection Semantics
  Global Arrays and ARMCI
Overall Design
  Efficient Connection Teardown
  Connection Cache Management
Performance Evaluation
  Computational Chemistry
  Sub-surface modeling
Conclusions and Future Work

## Slide 3: Introduction
For runtime systems, scalable communication data structures is critical
Communication data structures
  Buffers (data, control messages ..)
  Connections
    End-points (Gemini, Seastar, BG ..)
    One-to-one mapping (IB))
  Registration data structures (Local for MPI, Local + Remote for PGAS)
  ….
Efficient connection management is important
  213 InfiniBand systems in TOP500
PGAS Models are becoming popular

## Slide 4: InfiniBand Connection Management
On-demand pair-wise process creation
  Cluster’02 (VIA), IPDPS’06, Cluster’08 (IB-MPI), CCGrid’10 (IB-PGAS)
  Persistent through the application lifetime
Unreliable datagram based approaches (ICS’07)
  Natural fit for two-sided communication (send/receive model)
  Designing get and bulk data transfer is prohibitive
  Software maintained reliability
eXtended Reliable Connection (XRC)
  Connection memory increases with nodes and not processes (ICS’07, Cluster’08)

## Slide 5: Use Cases for PGAS Models
Frequently combined with non-SPMD execution models
Task Based Computations
  Dynamic load balancing and work stealing
Linear communication over the application execution lifetime
  Time-Variance in execution
  Little temporal reuse (SC’09)
  Connection persistence is not useful

## Slide 6: Problem Statement
Given low temporal locality for PGAS models and non-SPMD executions
  What are the design choices for a disconnection protocol?
  What are the memory benefits and possible performance degradations?

## Slide 7: Outline
Introduction
Background and Motivation
  InfiniBand Connection Semantics
  Global Arrays and ARMCI
Overall Design
  Efficient Connection Teardown
  Connection Cache Management
Performance Evaluation
  Computational Chemistry
  Sub-surface modeling
Conclusions and Future Work

## Slide 8: InfiniBand Transport Semantics
Reliable Connection
  Most frequently used
  Supports In-order delivery, RDMA, QoS ..
Reliable Datagram
  Most RC features, but ..
Unreliable Connection
  RDMA, requires dedicated QP
  No ordering
Unreliable Datagram
  Connectionless
  limited message size to MTU
  No ordering or reliability guarantees

## Slide 9: Global Arrays
Global Arrays is a PGAS programming model
  GA presents a shared view
  Provides one-sided communication model
  Used in wide variety of applications
  Computational Chemistry
    NWChem, Molcas, Molpro …
  Bioinformatics
    ScalaBLAST
  Ground Water Modeling
    STOMP
Physically distributed data
Global Address Space

## Slide 10: Aggregate Remote Memory Copy Interface
Communication Runtime Systems for Global Arrays
  Used in Global Trees, and Chapel
Provides one-sided communication runtime primitives
Currently Supported Platforms
  Commodity Networks
    InfiniBand, Ethernet ..
  Leadership Class Machines
    Cray XE6, Cray XTs
    IBM BG’s
    On-going -> BG/Q and BlueWaters
  Upcoming features
    Fault tolerant continued execution (5.1)
    Energy Efficiency modes (5.2)

## Slide 11: Outline
Introduction
Background and Motivation
  InfiniBand Connection Semantics
  Global Arrays and ARMCI
Overall Design
  Efficient Connection Teardown
  Connection Cache Management
Performance Evaluation
  Computational Chemistry
  Sub-surface modeling
Conclusions and Future Work

## Slide 12: Connection Structure in ARMCI
Master Process
Data Server thread
Client Process

## Slide 13: Connection Cache Management
Number of active connections
  Model?
  Dynamic behavior for task-based computations
Finding a victim connection
  LRU
LRU insufficient with communication cliques
  Multi-phase applications (use-case: Flow + Chemistry)
  Modified-LRU (LRU-M)
  Temporal locality of connections

## Slide 14: Overlap Disconnection Protocol
Client
Data Server
Master Process
Time
WaitProc
Flush
Teardown Req
Acknowledgement
break
break

## Slide 15: Outline
Introduction
Background and Motivation
  InfiniBand Connection Semantics
  Global Arrays and ARMCI
Overall Design
  Efficient Connection Teardown
  Connection Cache Management
Performance Evaluation
  Computational Chemistry and Sub-surface Modeling
Conclusions and Future Work

## Slide 16: Performance Evaluation
Evaluation Test Bed
  160 Tflop system with 2310 Dual socket quad core Barcelona processor
  InfiniBand DDR with PCI Express using DDR Voltaire switches
Original implementation is Global Arrays (GA) version 4.3
  The presented design is available with GA-5.0
Methodologies
  LRU, and LRU-M
  Varying the number of connection entries in connection cache
Applications
  Northwest Chemistry (NWChem)
  Sub-surface Transport on Multiple Phases

## Slide 17: Performance Evaluation with NWChem
Evaluation with pentane input deck on 6144 processes
The connection cache has a total of 128, 32, and 4 entries
Negligible performance degradation for 128 and 32 cache size
Total connections created – 91-117
  3-4 times for 32 cache size
  ~32 times for 4 cache size

## Slide 18: Performance Evaluation :NWChem (Contd)
Evaluation with siosi7 input deck on 4096 processes
The connection cache has a total of 128, 32, and 4 entries
Negligible performance degradation for 128 and 32 connection size
Total connections created – 93-121
  3-4 times for 32 cache size
  ~32 times for 4 cache size

## Slide 19: Performance Evaluation :STOMP
Evaluation on 8192 processes
The connection cache has a total of 128, 32, and 4 entries
LRU-M reduces the overall connection establishment and break time in comparison to LRU

## Slide 20: Conclusions and Future Work
Persistent on-demand connection approaches are insufficient
Presented a design for connection management
  Efficient connection cache management
  A conducive protocol for PGAS Models
Memory benefits for two class of applications
Future Work:
  Solve the problem for two-sided (pair-wise) connections
  Apply the problem to other communication data structures (remote registration caches)

## Slide 21: Questions
Global Arrays
  http://www.emsl.pnl.gov/docs/global/
ARMCI
  http://www.emsl.pnl.gov/docs/parsoft/armci/
HPC-PNL
  http://hpc.pnl.gov