## Slide 1: Optimizing SpMV for Diagonal Sparse Matrices on GPU
Sun Xiangzheng, Zhang Yunquan, Wang Ting, Xianyi Zhang, Liang Yuan and Li Rao
Institute of Software, Chinese Academy of Sciences
Email: zyq@mail.rdcps.ac.cn
Presented by: Pavan Balaji, Argonne National Laboratory

## Slide 2: Outline
Background
CRSD Storage Format
SpMV OpenCL Kernel Based on CRSD Format
Evaluation
Conclusion

## Slide 3: Sparse Matrix-Vector Product
  y = A × x
Important computational kernel in many scientific applications
  PDE solvers one of the primary use cases
Many approaches for Dense Matrix-Vector or Matrix-matrix multiplications
Sparse computations are different
  Many zeros in the matrix: a very small fraction is non-zero elements
    One example is diagonal matrices used in linear equation solvers when each equation only has a small number of variables
  Challenge is to no waste space storing or parsing through zero elements

## Slide 4: Challenges in Sparse Matrix manipulation
Primary method for storing sparse matrices is to find symmetric patterns and use a concise notation to save each pattern
  Such representation is typically referred to as “matrix compression”
Many aspects that disrupt symmetry in real applications
  Idle sections
  Scatter points
  Many applications do not care about exact data: changing some data to zero might be OK

## Slide 5: Our Approach in a Nutshell
CRSD: Compressed Row Segment with Diagonal-pattern
Other approaches exist: CSR, DIA, ELL, HYB
Each approach tries to find symmetric segments
  Different approaches use different models for finding symmetric segments
  Idea is to minimize the number of “stand-alone” scatter elements that we need to store
Two primary differences in our approach
  Two dimensional decomposition of blocks to find symmetric patterns (as opposed to 1D decomposition)
  Application knowledge to zero-out some elements

## Slide 6: Outline
Background
CRSD Storage Format
SpMV OpenCL Kernel Based on CRSD Format
Evaluation
Conclusion

## Slide 7: CRSD Storage Format (1)
Compressed Row Segment with Diagonal-pattern (CRSD)
Diagonal Pattern
  Describe the diagonal distribution
  Diagonal adjacent
    The absolute value of difference of two diagonals’ offset is 1
  Groups the diagonals:
    If two diagonals are adjacent, put them into an adjacent (AD) group;
    After removing the diagonals within the adjacent groups, the original diagonal sequence is broken up into pieces. We assign the diagonals of each piece into a nonadjacent(NAD) group.
  Group representation
    (Group type AD/NAD, the number of diagonals)
（AD，2）
（AD，3）
（NAD，1）
（NAD，2）
（NAD，1）
  {(NAD,1), (AD,2), (NAD,2), (AD,3), (NAD,1)}
Notes: Animation is used to describe that how to group the diagonals for the diagonal pattern

## Slide 8: CRSD Storage Format (2)
Matrix representation using diagonal pattern
  The queue of diagonal patterns
  matrix = { {(NAD,1),{(AD,2),(NAD,2)}, {(AD,2), {NAD,1} }
Idle section process
  Larger number of zeros should be filled
  --- change the diagonal pattern
  Little number of zeros in idle section
  --- maintain the diagonal pattern
Notes: The red line is mark where the diagonal pattern are modified for idle section

## Slide 9: CRSD Storage Format (3)
Row segments
  Matrix is split in row directions
  mrows: the number of rows in each row segments
Matrix is split in two directions
(mrows = 2)
  Diagonal groups in diagonal pattern
  Row segments
  Unit for storage and operation
Scatter points detection
  Only one nonzero on the diagonal in one row segment(like point v55)
Unit for storage and operation
Notes: The animation is used for two direction split.

## Slide 10: CRSD Storage Format (4)
Storage Format
  For nonzeros in diagonal patterns
    matrix: diagonal pattern content
    crsd _dia _index:
      the start row number of each diagonal pattern;
      the number of row segments in each diagonal pattern;
      the column indices of diagonals.
    crsd_dia_val: nonzero value
      the nonzeros in each diagonal pattern are stored contiguously
      the nonzeros locate on one diagonal are stored contiguously.
  For scatter points
    Extract entire row that contains the scatter points.
    Stored in ELLPACK/ITPACK formats
num scatter rows=1
num dia patterns=2
matrix= {{ (NAD,1),(AD,2),(NAD,2) } , { (AS, 1) } }
crsd dia index = { R0, 1, C0, C2, C5, C7, | R2, 2, C0, C3 }
crsd dia val = {{ (v00,v11),(v02,v13,v03,v14),(v05,v16,v07,v18) } , { (v20,v31,v21,v32),(v23,v34) } ,
{ (v42,v53,0,v54),(v45,v56) } }
scatter index = { R5, 4, C3, C4, C5, C6 }
scatter val = { v53, v54, v55, v56 }
Notes: Why scatter points are extracted with the entire row?
Do not change the float operation order for keeping precision
This slide can be quickly presented.
There are two mistakes in this paper, which are marked to be red.

## Slide 11: Outline
Background
CRSD Storage Format
SpMV OpenCL Kernel Based on CRSD Format
Evaluation
Conclusion

## Slide 12: SpMV OpenCL Kernel Based on CRSD Format (1)
Generate OpenCL Kernel based on CRSD
Work assignment:
  Each work-item process one row
  Work-items process nonzeros in one row segment are assigned to one work group
  mrows is a multiple of the wavefront size.

## Slide 13: SpMV OpenCL Kernel Based on CRSD Format (2)
Optimizations:
  Avoid thread divergence
  Loop unrolling
  Accesses to global memory are coalescing
    The contiguous storage for nonzeros
  Utilization of local memory for adjacent group
    The reused x is loaded into local memory

## Slide 14: SpMV OpenCL Kernel Based on CRSD Format (3)
Optimizations :
  Eliminate reading the index array and Calculate the nonzero index directly
      Identify the diagonal pattern to process
      Nonzero index on dth diagonal
      Correspond x index
      Index for result

## Slide 15: Generated SpMV OpenCL Kernel

## Slide 16: Outline
Background
CRSD Storage Format
SpMV OpenCL Kernel Based on CRSD Format
Evaluation
Conclusion

## Slide 17: Evaluation (1)
Platform information:
  CPU: Intel Xeon X5550, 2.67GHz × 2
  Compiler: GCC 4.4.3
  GPU: Tesla C2050
  Memory bandwidth: 144 GB/sec
Performance Comparison
  CPU side:
    Intel MKL 10.2.6.038
  GPU side:
    state-of-the-art implementations (Bell and Garland, 2009)
    DIA, CSR, ELL and HYB(ELL+COO) formats

## Slide 18: Evaluation (2)
1-17 from NIST Matrix Market
  2D/3D problems
  Structural problems
  quantum chemistry problem
8-13 from an astrophysics application [*]
[*] Chana K. H., Li Ligang, Liao Xinhao. Modelling the core convection using ﬁnite
element and ﬁnite diﬀerence methods. Physics of the Earth and Planetary Interiors,
157(2): 124-138. (2006)

## Slide 19: Evaluation(3)
GPU side
DIA performs poor on Matrix 3, 4
  Nonzeros distributes on 655 diagonals
  Nonzeros per row is 44
For DIA in double precision, No performance data for matrix 11, 12, 13
  DIA format size exceeds the limited size on GPU
Speedup compared with different formats
 | Double precision |  |  |  | Single precision |  |  | 
format | DIA | ELL | CSR | HYB | DIA | ELL | CSR | HYB
Avg | 2.04 | 1.24 | 4.57 | 1.54 | 1.92 | 1.50 | 4.59 | 1.97
Max | 11.13 | 1.52 | 9.01 | 2.67 | 11.24 | 1.94 | 9.14 | 3.68

## Slide 20: Evaluation (4)
CPU side
DIA performs poor on Matrix 3, 4, 11, 12, 13 on CPU
  Speedup reaches 199.63 and 202.23 for double and single precision
Performance improvement
Fig.11 For double precision
Fig 12. For Single precision
Speedup |  | DIA | CSR, thr=1 | CSR, thr=8
Double precision | Max | 15.27 | 25.06 | 11.63
 | Avg. | 12.34 | 14.76 | 6.63
Single precision | Max | 13.25 | 39.81 | 12.79
 | Avg. | 9.87 | 24.25 | 7.18

## Slide 21: Outline
Background
CRSD Storage Format
SpMV Kernel Based on CRSD Format
Evaluation
Conclusion

## Slide 22: Conclusion
Diagonal pattern
  Deal with idle section
  X is reused in local memory for adjacent group
OpenCL kernel based on CRSD
  Include index information
  Work assignment is efficient
  Improve performance

## Slide 23
Thank You