## Slide 1: Online Performance Projection for Clusters with Heterogeneous GPUs
Lokendra S. Panwar, Ashwin M. Aji, Wu-chun Feng (Virginia Tech, USA)
Jiayuan Meng, Pavan Balaji (Argonne National Laboratory, USA)

## Slide 2: Diversity in Accelerators
Nov, 2008
Nov, 2013
Performance Share of Accelerators in Top500 Systems
Source: top500.org

## Slide 3: Heterogeneity “Among” Nodes
Clusters are deploying different accelerators
  Different accelerators for different tasks
Example clusters:
  “Shadowfax” at VBI@VT: NVIDIA GPUs, FPGAs
  “Darwin” at LANL: NVIDIA GPUs, AMD GPUs
  “Dirac” at NERSC: NVIDIA Tesla and Fermi GPUs

## Slide 4: Heterogeneity “Among” Nodes
Clusters are deploying different accelerators
  Different accelerators for different tasks
Example clusters:
  “Shadowfax” at VBI@VT: NVIDIA GPUs, FPGAs
  “Darwin” at LANL: NVIDIA GPUs, AMD GPUs
  “Dirac” at NERSC: NVIDIA Tesla and Fermi GPUs
However …
  A unified programming model for “all” accelerators: OpenCL
  CPUs, GPUs, FPGAs, DSPs

## Slide 5: Affinity of Tasks to Processors
Peak performance doesn’t necessarily translate into actual device performance.
Reduction | GFLOPs | Global Memory BW (GB/s) | Actual Time(ms)
NVIDIA C2050 | 1030 | 144 | 0.13
AMD HD5870 | 2720 | 154 | 0.21

## Slide 6: Affinity of Tasks to Processors
Peak performance doesn’t necessarily translate into actual device performance.
OpenCL Program
?
Reduction | GFLOPs | Global Memory BW (GB/s) | Actual Time(ms)
NVIDIA C2050 | 1030 | 144 | 0.13
AMD HD5870 | 2720 | 154 | 0.21

## Slide 7: Challenges for Runtime Systems
It is crucial for heterogeneous runtime systems to embrace different accelerators in clusters w.r.t. performance and power
Examples of OpenCL runtime systems:
  SnuCL
  VOCL
  SOCL
Challenges:
  Efficiently choose the right device for the right task
  Keep the decision making overhead minimal

## Slide 8: Our Contributions
An online workload characterization technique for OpenCL kernels
Our model projects the relative ranking of different devices with little overhead
An end-to-end evaluation of our technique for multiple architectural families of AMD and NVIDIA GPUs

## Slide 9: Outline
Introduction
Motivation
Contributions
Design
Evaluation
Conclusion

## Slide 10: Design
Goal:
  Rank accelerators for a given OpenCL workload
    Accurately AND efficiently
  Decision making with minimal overhead

## Slide 11: Design
Goal:
  Rank accelerators for a given OpenCL workload
    Accurately AND efficiently
  Decision making with minimal overhead
Choices:
  Static Code Analysis:
    Fast
    Inaccurate, as it does not account for dynamic properties:
      Input data dependence, memory access patterns, dynamic instructions

## Slide 12: Design
Goal:
  Rank accelerators for a given OpenCL workload
    Accurately AND efficiently
  Decision making with minimal overhead
Choices:
  Static Code Analysis:
    Fast
    Inaccurate, as it does not account for dynamic properties:
      Input data dependence, memory access patterns, dynamic instructions
  Dynamic Code Analysis:
    Higher accuracy
    Execute either on actual device or through a “emulator”
      Not always feasible to run on actual devices: Data transfer costs, Clusters are “busy”
      Emulators are very slow

## Slide 13: Design – Workload Profiling
Emulator
OpenCL
Kernel
Memory Patterns
Bank Conflicts
Instruction
Mix

## Slide 14: Design – Workload Profiling
“Mini-emulation”
  Emulate a single workgroup
    Collect dynamic characteristics:
      Instruction traces
      Global and Local memory transactions and access patterns
    In typical data-parallel workloads, workgroups exhibit similar runtime characteristics
  Asymptotically lower overhead
Mini
Emulator
OpenCL
Kernel
Memory Patterns
Bank Conflicts
Instruction
Mix

## Slide 15: Design – Device Profiling
GPU1
GPU 2
GPU N
……
Instruction and Memory
Microbenchmarks
Chart: Occupancy
| 3.125E-2 | 6.25E-2 | 0.125 | 0.25 | 0.5 | 1
Global Memory Read | 98.1 | 182.4 | 238.9 | 245.72 | 248.78 | 248.95
Global Memory Write | 118 | 123 | 125 | 131 | 122 | 122
Local Memory Read | 141 | 285 | 572 | 1042 | 1534 | 1504
Local Memory Write | 153 | 308 | 617 | 1234 | 1544 | 1537
Chart: Occupancy
| 3.125E-2 | 6.25E-2 | 0.125 | 0.25 | 0.5 | 1
Global Memory Read | 98.1 | 182.4 | 238.9 | 245.72 | 248.78 | 248.95
Global Memory Write | 118 | 123 | 125 | 131 | 122 | 122
Local Memory Read | 141 | 285 | 572 | 1042 | 1534 | 1504
Local Memory Write | 153 | 308 | 617 | 1234 | 1544 | 1537
Chart: Occupancy
| 3.125E-2 | 6.25E-2 | 0.125 | 0.25 | 0.5 | 1
Global Memory Read | 98.1 | 182.4 | 238.9 | 245.72 | 248.78 | 248.95
Global Memory Write | 118 | 123 | 125 | 131 | 122 | 122
Local Memory Read | 141 | 285 | 572 | 1042 | 1534 | 1504
Local Memory Write | 153 | 308 | 617 | 1234 | 1544 | 1537
Device Throughput Profiles

## Slide 16: Design – Device Profiling
Build device throughput profiles:
  Modified SHOC microbenchmarks to
    Obtain hardware throughput with varying occupancy
    Collect throughputs for instructions, global memory and local memory
  Built only once
Global and Local memory profile of AMD 7970
Chart: Occupancy
| 3.125E-2 | 6.25E-2 | 0.125 | 0.25 | 0.5 | 1
Global Memory Read | 98.1 | 182.4 | 238.9 | 245.72 | 248.78 | 248.95
Global Memory Write | 118 | 123 | 125 | 131 | 122 | 122
Local Memory Read | 141 | 285 | 572 | 1042 | 1534 | 1504
Local Memory Write | 153 | 308 | 617 | 1234 | 1544 | 1537

## Slide 17: Design – Find Performance Limiter
Chart: Occupancy
| 3.125E-2 | 6.25E-2 | 0.125 | 0.25 | 0.5 | 1
Global Memory Read | 98.1 | 182.4 | 238.9 | 245.72 | 248.78 | 248.95
Global Memory Write | 118 | 123 | 125 | 131 | 122 | 122
Local Memory Read | 141 | 285 | 572 | 1042 | 1534 | 1504
Local Memory Write | 153 | 308 | 617 | 1234 | 1544 | 1537
Memory Patterns
Bank Conflicts
Instruction
Mix
Device Profile
Workload Profile
Chart: Projected Time
| Performance Bound
Compute | 4.3
Global Mem | 2.4
Local Mem | 2

## Slide 18: Design – Find Performance Limiter
Single workgroup dynamic characteristics  Full kernel characteristics
  Device occupancy as scaling factor
Chart: Projected Time
| Performance Bound
Compute | 4.3
Global Mem | 2.4
Local Mem | 2
Compute projected theoretical times:
  Instructions
  Global memory
  Local memory
GPUs aggressively try to hide latencies of components
Performance limiter =
max(tlocal, tglobal, tcompute)*
  Compare the normalized predicted times and choose best device
*Zhang et. al. A Quantitative Performance Analysis Model for GPU Architectures, HPCA’2011

## Slide 19: Design
GPU 1
GPU 2
GPU N
……
Instruction and Memory
Benchmarks
Static Profiling
Device
Profile
Chart: Occupancy
| 3.125E-2 | 6.25E-2 | 0.125 | 0.25 | 0.5 | 1
Global Memory Read | 98.1 | 182.4 | 238.9 | 245.72 | 248.78 | 248.95
Global Memory Write | 118 | 123 | 125 | 131 | 122 | 122
Local Memory Read | 141 | 285 | 572 | 1042 | 1534 | 1504
Local Memory Write | 153 | 308 | 617 | 1234 | 1544 | 1537

## Slide 20: Design
Mini-Emulator (Single workgroup)
GPU
Kernel
Memory
Patterns
Bank Conflicts
Instruction
Mix
GPU 1
GPU 2
GPU N
……
Instruction and Memory
Benchmarks
Static Profiling
Dynamic Profiling
Device
Profile
Chart: Occupancy
| 3.125E-2 | 6.25E-2 | 0.125 | 0.25 | 0.5 | 1
Global Memory Read | 98.1 | 182.4 | 238.9 | 245.72 | 248.78 | 248.95
Global Memory Write | 118 | 123 | 125 | 131 | 122 | 122
Local Memory Read | 141 | 285 | 572 | 1042 | 1534 | 1504
Local Memory Write | 153 | 308 | 617 | 1234 | 1544 | 1537

## Slide 21: Design
Mini-Emulator (Single workgroup)
GPU
Kernel
Effective
Instruction
Throughput
Effective
Global Memory
Bandwidth
Effective
Local Memory
Bandwidth
Chart: 
| GPU 1 | GPU 2 | GPU 3 | GPU 4
 | 1 | 0.8 | 1.4 | 1.1
Relative GPU
Performances
Memory
Patterns
Bank Conflicts
Instruction
Mix
GPU 1
GPU 2
GPU N
……
Instruction and Memory
Benchmarks
Static Profiling
Dynamic Profiling
Device
Profile
Perf.
Limiter?
Performance Projection
Chart: Occupancy
| 3.125E-2 | 6.25E-2 | 0.125 | 0.25 | 0.5 | 1
Global Memory Read | 98.1 | 182.4 | 238.9 | 245.72 | 248.78 | 248.95
Global Memory Write | 118 | 123 | 125 | 131 | 122 | 122
Local Memory Read | 141 | 285 | 572 | 1042 | 1534 | 1504
Local Memory Write | 153 | 308 | 617 | 1234 | 1544 | 1537

## Slide 22: Outline
Introduction
Motivation
Contributions
Design
Evaluation
Conclusion

## Slide 23: Experimental Setup
Accelerators:
  AMD 7970 : Scalar ALUs, Cache hierarchy
  AMD 5870: VLIW ALUs
  NVIDIA C2050: Fermi Architecture Cache Hierarchy
  NVIDIA C1060: Tesla Architecture
Simulators:
  Multi2simv4.1 for AMD and GPGPU-Sim v3.0 for NVIDIA devices
  Methodology agnostic to specific emulator
Applications:
Floyd Warshall | FastWalsh Trasnform | MatrixMul (global) | MatrixMul (local)
Num Nodes = 192 | Array Size = 1048576 | Matrix Size = [1024,1024] | Matrix Size = [1024,1024]
Reduction | NBody | AESEncrypt Decrypt | Matrix Transpose
ArraySize =1048576 | NumParticles=32768 | Width=1536, Height=512 | Matrix Size = [1024,1024]

## Slide 24: Application Boundedness : AMD GPUs
Chart: HD 5870
| Fast Walsh Transform | Floyd Warshall | MatrixMultiply (Gmem) | Nbody | AESEncryptDecrypt | Reduction | MatrixMultiply (Lmem) | MatrixTranspose
Gmem | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Lmem | 0 | 0 | 0 | 4.3148 | 2 | 0.73913 | 2.8889 | 0.83529
Compute | 0.61538 | 0.54545 | 0.28205 | 17.9599 | 1.8776 | 0.52174 | 1.1667 | 0.13529
Projected Time (Normalized)
Chart: HD 7970
| Fast Walsh Transform | Floyd Warshall | MatrixMultiply (Gmem only) | Nbody | AESEncryptDecrypt | Reduction | MatrixMultiply (Lmem) | MatrixTranspose
Gmem | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Lmem | 0 | 0 | 0 | 3.1497 | 1.6789 | 0.78387 | 2.4583 | 0.92857
Compute | 0.069767 | 0.0625 | 0.26087 | 9.5928 | 1.6842 | 0.29032 | 1.5 | 0.17857
gmem
gmem
gmem
compute
lmem
lmem
gmem
gmem
gmem
gmem
gmem
gmem
gmem
compute
compute
lmem

## Slide 25: Application Boundedness Summary
Application | AMD 5870 | AMD 7970 | NVIDIA C1060 | NVIDIA C2050
FloydWarshall | gmem | gmem | gmem | gmem
FastWalshTransform | gmem | gmem | gmem | gmem
MatrixTranpose | gmem | gmem | gmem | gmem
MatMul(global) | gmem | gmem | gmem | gmem
MatMul(local) | local | local | gmem | compute
Reduction | gmem | gmem | gmem | compute
NBody | compute | compute | compute | compute
AESEncryptDecrypt | local | compute | compute | compute

## Slide 26: Accuracy of Performance Projection
.
Chart: Actual
| Fast Walsh Transform | Floyd Warshall | MatrixMultiply (Gmem) | Nbody | AESEncryptDecr. | Reduction | MatrixMultiply (Lmem) | MatrixTranspose
C1060 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
C2050 | 0.255 | 0.3173 | 0.42824 | 0.90295 | 0.32274 | 0.94703 | 0.556 | 0.53423
HD 5870 | 0.79723 | 0.48174 | 0.27675 | 1.2807 | 1.2398 | 1.4853 | 0.2798 | 10.1437
HD 7970 | 0.12825 | 0.15099 | 0.38649 | 0.29631 | 0.43158 | 0.18247 | 0.26925 | 16.9062
Chart: Projected
| Fast Walsh Transform | Floyd Warshall | MatrixMultiply (Gmem) | Nbody | AESEncryptDecr. | Reduction | MatrixMultiply (Lmem) | MatrixTranspose
C1060 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
C2050 | 0.83146 | 1.412 | 0.67131 | 0.78486 | 0.60559 | 0.74272 | 0.40804 | 0.57084
HD 5870 | 0.9768 | 0.91123 | 0.4662 | 0.62566 | 1.3892 | 1.8011 | 0.39692 | 12.5565
HD 7970 | 0.16155 | 0.26509 | 0.54987 | 0.17225 | 0.45362 | 0.24276 | 0.22518 | 10.3406

## Slide 27: Accuracy of Performance Projection
.
Chart: Actual
| Fast Walsh Transform | Floyd Warshall | MatrixMultiply (Gmem) | Nbody | AESEncryptDecr. | Reduction | MatrixMultiply (Lmem) | MatrixTranspose
C1060 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
C2050 | 0.255 | 0.3173 | 0.42824 | 0.90295 | 0.32274 | 0.94703 | 0.556 | 0.53423
HD 5870 | 0.79723 | 0.48174 | 0.27675 | 1.2807 | 1.2398 | 1.4853 | 0.2798 | 10.1437
HD 7970 | 0.12825 | 0.15099 | 0.38649 | 0.29631 | 0.43158 | 0.18247 | 0.26925 | 16.9062
Chart: Projected
| Fast Walsh Transform | Floyd Warshall | MatrixMultiply (Gmem) | Nbody | AESEncryptDecr. | Reduction | MatrixMultiply (Lmem) | MatrixTranspose
C1060 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
C2050 | 0.83146 | 1.412 | 0.67131 | 0.78486 | 0.60559 | 0.74272 | 0.40804 | 0.57084
HD 5870 | 0.9768 | 0.91123 | 0.4662 | 0.62566 | 1.3892 | 1.8011 | 0.39692 | 12.5565
HD 7970 | 0.16155 | 0.26509 | 0.54987 | 0.17225 | 0.45362 | 0.24276 | 0.22518 | 10.3406
Best Device | Fast Walsh | Floyd Warshal | Matmul (global) | Nbody | AES Encrypt Decrypt | Reduction | Matmul (local) | Mat Transpose
Actual | 7970 | 7970 | 5870 | 7970 | 2050 | 7970 | 7970 | 2050
Projected | 7970 | 7970 | 5870 | 7970 | 7970 | 7970 | 7970 | 2050

## Slide 28: Accuracy of Performance Projection
.
Chart: Actual
| Fast Walsh Transform | Floyd Warshall | MatrixMultiply (Gmem) | Nbody | AESEncryptDecr. | Reduction | MatrixMultiply (Lmem) | MatrixTranspose
C1060 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
C2050 | 0.255 | 0.3173 | 0.42824 | 0.90295 | 0.32274 | 0.94703 | 0.556 | 0.53423
HD 5870 | 0.79723 | 0.48174 | 0.27675 | 1.2807 | 1.2398 | 1.4853 | 0.2798 | 10.1437
HD 7970 | 0.12825 | 0.15099 | 0.38649 | 0.29631 | 0.43158 | 0.18247 | 0.26925 | 16.9062
Chart: Projected
| Fast Walsh Transform | Floyd Warshall | MatrixMultiply (Gmem) | Nbody | AESEncryptDecr. | Reduction | MatrixMultiply (Lmem) | MatrixTranspose
C1060 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
C2050 | 0.83146 | 1.412 | 0.67131 | 0.78486 | 0.60559 | 0.74272 | 0.40804 | 0.57084
HD 5870 | 0.9768 | 0.91123 | 0.4662 | 0.62566 | 1.3892 | 1.8011 | 0.39692 | 12.5565
HD 7970 | 0.16155 | 0.26509 | 0.54987 | 0.17225 | 0.45362 | 0.24276 | 0.22518 | 10.3406
Best Device | Fast Walsh | Floyd Warshal | Matmul (global) | Nbody | AES Encrypt Decrypt | Reduction | Matmul (local) | Mat Transpose
Actual | 7970 | 7970 | 5870 | 7970 | 2050 | 7970 | 7970 | 2050
Projected | 7970 | 7970 | 5870 | 7970 | 7970 | 7970 | 7970 | 2050

## Slide 29: Emulation Overhead – Reduction Kernel
Chart: Data Size (x)
| 65536 | 131072 | 262144 | 524288 | 1048576
Full Kernel Emulation (C2050) | 2.4086 | 5.0651 | 10.0422 | 20.933 | 43.1819
Single Workgroup Emulation (C2050) | 0.021189 | 0.020476 | 0.020886 | 0.020785 | 0.020505
Full Kernel Emulation (HD 7970) | 2.3 | 9.4 | 18.45 | 37.3 | 72.9
Single Workgroup Emulation (HD 7970) | 0.011 | 0.011 | 0.0109 | 0.011 | 0.011

## Slide 30: Outline
Introduction
Motivation
Contributions
Design
Evaluation
Conclusion

## Slide 31: 90/10 Paradigm -> 10x10 Paradigm
Simplify and specialized tools (“accelerators”) customized for different purposes (“applications”)
  Narrower focus on applications (10%)
  Simplified and specialized accelerators for each classification
Why?
  10x lower power, 10x faster -> 100x energy efficient
Figure credit: A. Chien, Salishan Conference 2010

## Slide 32: Conclusion
We presented a “Mini-emulation” technique for online workload characterization for OpenCL kernels
  The approach is shown to be sufficiently accurate for relative performance projection
  The approach has asymptotically lower overhead than projection using full kernel emulation
Our technique is shown to work well with multiple architectural families of AMD and NVIDIA GPUs
With the increasing diversity in accelerators (towards 10x10*), our methodology only becomes more relevant.
*S. Borkar and A. Chien, “The future of microprocessors,” Communications of the ACM, 2011

## Slide 33: Thank You

## Slide 34: Backup

## Slide 35: Evolution of Microprocessors: 90/10 Paradigm
Derive common cases for applications (90%)
  Broad focus on application workloads
Architectural improvements for 90% of cases
  Design an aggregated generic “core”
  Lesser customizability for applications
Figure credit: A. Chien, Salishan Conference 2010

## Slide 36: 90/10 Paradigm -> 10x10 Paradigm
Simplify and specialized tools (“accelerators”) customized for different purposes (“applications”)
  Narrower focus on applications (10%)
  Simplified and specialized accelerators for each classification
Why?
  10x lower power, 10x faster -> 100x energy efficient
Figure credit: A. Chien, Salishan Conference 2010

## Slide 37: Application Boundedness : NVIDIA GPUs
Chart: C1060
| Fast Walsh Transform | Floyd Warshall | MatrixMultiply (Gmem only) | Nbody | AESEncryptDecrypt | Reduction | MatrixMultiply (Lmem) | MatrixTranspose
Gmem | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Lmem | 0 | 0 | 0 | 15.7563 | 0.44502 | 0.35061 | 0.93512 | 0.41995
Compute | 0.2399 | 0.56378 | 0.37671 | 69.3637 | 10.8384 | 1.3086 | 0.67379 | 0.089985
Projected Time (Normalized)
Chart: C2050
| Fast Walsh Transform | Floyd Warshall | MatrixMultiply (Gmem only) | Nbody | AESEncryptDecrypt | Reduction | MatrixMultiply (Lmem) | MatrixTranspose
Gmem | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Lmem | 0 | 0 | 0 | 12.685 | 0.24189 | 0.28672 | 0.70445 | 0.28786
Compute | 0.17473 | 0.24179 | 0.33983 | 109.7166 | 10.2487 | 0.81537 | 1.5727 | 0.095463
gmem
gmem
gmem
compute
compute
compute
lmem
gmem
gmem
gmem
gmem
gmem
gmem
compute
compute
compute

## Slide 38: Evaluation: Projection Accuracy (Relative to C1060)
Chart: Relative Execution Time
| Fast Walsh Transform | Floyd Warshall | MatrixMultiply (Gmem) | Nbody | AESEncryptDecr. | Reduction | MatrixMultiply (Lmem) | MatrixTranspose
C1060 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
C2050 | 0.255 | 0.3173 | 0.42824 | 0.90295 | 0.32274 | 0.94703 | 0.556 | 0.53423
HD 5870 | 0.79723 | 0.48174 | 0.27675 | 1.2807 | 1.2398 | 1.4853 | 0.2798 | 10.1437
HD 7970 | 0.12825 | 0.15099 | 0.38649 | 0.29631 | 0.43158 | 0.18247 | 0.26925 | 16.9062
Chart: Projected Relative Execution Time
| Fast Walsh Transform | Floyd Warshall | MatrixMultiply (Gmem) | Nbody | AESEncryptDecr. | Reduction | MatrixMultiply (Lmem) | MatrixTranspose
C1060 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
C2050 | 0.83146 | 1.412 | 0.67131 | 0.78486 | 0.60559 | 0.74272 | 0.40804 | 0.57084
HD 5870 | 0.9768 | 0.91123 | 0.4662 | 0.62566 | 1.3892 | 1.8011 | 0.39692 | 12.5565
HD 7970 | 0.16155 | 0.26509 | 0.54987 | 0.17225 | 0.45362 | 0.24276 | 0.22518 | 10.3406
Error | 24.6655 | 40.1612 | 14.9793 | 21.6264 | 10.297 | 11.3965 | 11.3143 | 23.996

## Slide 39: Evaluation: Projection Overhead vs. Actual Kernel Execution of Matrix Multiplication
Chart: Data Size (x = y = z)
| 64 | 128 | 256 | 512 | 1024 | 2048 | 4096 | 8192
Actual Device Execution (C2050) | 0.00016308 | 0.00014615 | 0.00025797 | 0.0016689 | 0.010756 | 0.083114 | 0.66437 | 5.5199
Single Workgroup Emulation (C2050) | 0.15172 | 0.29221 | 0.54927 | 1.1198 | 2.167 | 4.3263 | 8.5867 | 17.0927
Notes: Mini-emulation increases linearly because workload on each emulated thread increases linearly with the data size (for matrix multiply).
On the other hand, the actual execution time increases as O(n^3) per thread.

## Slide 40: Evaluation: Overhead of Mini-emulation vs. Full Kernel Emulation of Matrix Multiplication
Chart: Data Size (x = y = z)
| 64 | 128 | 256 | 512 | 1024
Full Kernel Emulation (C2050) | 0.59886 | 4.8772 | 35.7082 | 308.088 | 2263.42
Single Workgroup Emulation (C2050) | 0.15172 | 0.29221 | 0.54927 | 1.1198 | 2.167
Full Kernel Emulation (HD 7970) | 1.102 | 10.2 | 82.7 | 682 | 5328
Single Workgroup Emulation (HD 7970) | 0.38 | 0.81 | 1.42 | 2.62 | 4.91

## Slide 41: Evaluation: Overhead of Mini-emulation vs. Full Kernel Emulation of Reduction
Chart: Data Size (x)
| 65536 | 131072 | 262144 | 524288 | 1048576
Full Kernel Emulation (C2050) | 2.4086 | 5.0651 | 10.0422 | 20.933 | 43.1819
Single Workgroup Emulation (C2050) | 0.021189 | 0.020476 | 0.020886 | 0.020785 | 0.020505
Full Kernel Emulation (HD 7970) | 2.3 | 9.4 | 18.45 | 37.3 | 72.9
Single Workgroup Emulation (HD 7970) | 0.011 | 0.011 | 0.0109 | 0.011 | 0.011
Notes: Mini-emulation is constant per emulated thread (for reduction).