## Slide 1: Toward the Efficient Use of Multiple Explicitly Managed Memory Subsystems
Antonio J. Peña Pavan Balaji
Argonne National Laboratory Argonne National Laboratory
apenya@anl.gov balaji@anl.gov

## Slide 2: Motivation
Heterogeneity in computing explored:
  Heterogeneus processing
  Heterogeneous memory
Different memory technologies within computers already a reality
  Scratchpad, 3D-stacked, I/O class, …
We expect more memory heterogeneity
Different features:
  Size, resilience, access patterns, energy, …
Examples:
  Scratchpad:
    Cachelike speeds, small sizes
  Vector-specialized (e.g.: GDDR)
    High bandwidth if contiguous accesses
  Low-power memory
    Increased energy/speed ratio
  ECC-enabled memory
    Fault tolerance; speed & size overhead
  I/O class (e.g.: NVRAM)
    Large; reduced speeds & energy
    Faster reading than writing
Notes: 3D: KNL

## Slide 3: Motivation
To efficiently exploit heterogeneous memory:
  Bring them as first-class citizens
  Move from hierarchical to explicitly managed
Application’s data distribution?
  OS? Heuristics? On-the-fly monitoring? Hardware-assisted? Historic data? User hints?
  Need ecosystem to assist users/developers: tools
    Profilers, libraries, runtime systems

## Slide 4: Motivation
Goal:
  Heterogeneous memory systems
  Assess optimal data distribution
Methodology:
  Data-oriented profiling
  Memory object granularity
Solution:
  Valgrind core and tools extensions
  Distribution algorithm
DRAM
NVRAM
SP
3D

## Slide 5: Outline
Background
  Data-Oriented Profiling
  Valgrind, Callgrind, & Extensions
Methodology
  Analysis
  Assumptions and Current Known Limitations
Test Cases
  System Setup
  Applications
Experimental Results
Summary & Future Work

## Slide 6: Background

## Slide 7: Background Data-Oriented Profiling
Today’s profiling techniques help developers focus on troublesome lines of code
Data-oriented profiling complements the traditional algorithm-oriented analysis:
Traditional profiler
c[i] = a [j]* b [k]+ c[l]; ← 15%
Traditional profiler
a[i] = b[j] * c[k]; ← 5%
b[l] = d[m] * 2; ← 5%
c[n] =+ b[o]; ← 5%
Data-oriented profiler
a ← 0%
b ← 15%
c ← 0%
c[i] = a[j] * b[k] + c[l];
a[i] = b[j] * c[k];
b[l] = a[m] * 2;
c[n] += b[o];
a[i] = b[j] * c[k]; b[l] = a[m] * 2; c[n] += b[o];
Traditional profiler
a[i] = b[j] * c[k]; b[l] = d[m] * 2; c[n] += b[o]; ← 15%

## Slide 8: Background Valgrind & Callgrind
Valgrind
Generic instrumentation framework
Ecosystem: set of tools
  Memcheck is just default
Virtual machine – JIT
  Typically overhead around 4x-5x
Rich API to tools
  Notify requested capabilities
  Get debug information
  Get information about thread status
Intercept memory management calls
Client request mechanism
  Start / stop instrumentation from application’s code
Callgrind
Valgrind tool
“Call-graph generating cache and branch prediction profiler”
Purpose: profiling tool
  By source line of code
Cache simulation:
  Cache misses
  Cache hierarchy modeled after the host’s one by default
  Branch predictor
  Hardware prefetcher
Kcachegrind integration: visualization

## Slide 9: Background Valgrind & Callgrind Extensions
To enable the differentiation of memory objects:
  Locate the memory object comprising a given memory address
  Store its associated access data
Added support to be used from tools
During the execution of a profiled application:
  Every data access causing a last-level cache miss is checked against matching object
To tackle profiling overhead for production-sized runs, limit to a region of interest
  Modifying the code to be profiled
Output:
  Per-object cache misses during the
  profiled portion of interest
A. J. Peña and P. Balaji. "A framework for tracking memory accesses in scientific applications", in P2S2 2014 (ICPP Workshop), Minneapolis, MN, Sep. 2014.

## Slide 10: Methodology

## Slide 11: Methodology
Object-differentiated profiling + distribution algorithm (analysis):
  Profile to determine per-object last-level cache misses
  Assess the optimal distribution of the different objects among the memory subsystems
    Minimize processor stall cycles
Compiler
Toolchain
Memory
Profiler
Profile
Analyzer
Source
Code
Executable
Object
Execution
Input
Compiler
Toolchain
Profile
Data
Object
Distribution
Executable
Object
1
2
3
4
5
6
7
7
8

## Slide 12: Methodology Analysis
Multiple knapsack problem:
  Knapsacks: memory subsystems
  Knapsack capacity: memory size
  Items: memory objects
  Item weight: size
  Item value: number of load cache misses
    CPU stall cycles
  Not a textbook problem:
    The different knapsacks modify the value of their items:
      Multiply cache misses by a different factor: average read latency
Maximize the value of the content of a (set of) knapsack(s) given a set of items of different values and sizes

## Slide 13: Methodology Analysis
Greedy approach solving separate 0/1 knapsack problems:
  Target memories in ascending order of average access cycles
  Prioritize the placement of the most “valuable” objects in the faster memories
  In practice not divergent from the optimal global solution
  Removes computational complexity (0/1 knapsack is weakly NP-hard)
  4 KB page granularity
Obj #1
5k Cache Misses
Size: 6
Obj #2
10k Cache Misses
Size: 5
Obj #3
1k Cache Misses
Size: 2
Memory #1
Avg. Latency: 1
Size: 10
Memory #2
Avg. Latency: 10
Size: 100
Total Cost:
5k x 100 + (10k + 1k) x 10

## Slide 14: Methodology Assumptions and Current Known Limitations
Write misses cause no stall cycles:
  Buffered write-through with unlimited buffer size
  In practice, stall cycles caused by read misses >> those of write misses
  We don’t specially penalize memories w/ faster reads than writes (NVRAM)
Average latency estimations for the different memory subsystems
No memory migrations nor reuse of freed space
  (other than by the same memory object)

## Slide 15: Test Cases

## Slide 16: Test Cases System Setup
8-core processor with set-associative cache:
Cache Configuration
Description | Total Size | Assoc. | Line Size
L1 Instruction | 32 KB | 8 | 64 B
L1 Data | 32 KB | 8 | 64 B
LL Unified | 8 MB | 16 | 64 B

## Slide 17: Test Cases System Setup
Baseline system equipped with traditional DRAM-based main memory space
Target: two different heterogeneous memory configuration proposals
Scenario 1
Scenario 2
L1 Instr.
CPUs
3D DRAM
SP
MAIN
DRAM
NVRAM
L1 Data
L2
L1 Instr.
CPUs
L2
3D DRAM
SP
L1 Data
MAIN
DRAM

## Slide 18: Test Cases System Setup
Estimations:
  1 IPC
  No stall cycles caused by hazards
Memory Configuration
Memory |  | Scenario |  | 
Description | Latency | Baseline | Scenario 1 | Scenario 2
L1 | 0 c | 32 KB + 32 KB |  | 
L2 | 20 c | 8 MB |  | 
SP | 20 c | 0 B | 8 MB | 8 MB
3D | 135 c | 0 B | 8 GB | 1 GB
Main | 200 c | 32 GB | 32 GB | 4 GB
NVRAM | 20,000 c | 0 B | 0 B | 32 GB

## Slide 19: Test Cases Applications
MiniMD
“A simple proxy for the force computations in a typical molecular dynamics application”
Reduced version of the LAMMPS molecular dynamics simulator
Multiple large memory objects – different number of cache misses
Setup:
  Reference implementation v1.2
  LJ interactions among 2.9·106 atoms
  8 threads – 26 GB of memory
  23% of cycles from cache misses
HPCCG
“A simple conjugate gradient benchmark code for a 3D chimney domain on an arbitrary number of processors”
Access pattern known to be highly memory demanding and sensitive to different memory architectures
  Sensitivity to memory placement
Setup:
  Reference version 1.0
  400 x 400 x 400 node problem
  8-threaded process – 24 GB memory
  48% of cycles from cache misses

## Slide 20: Experimental Results

## Slide 21: Experimental Results
Compute unoptimized distribution as:
  Invert the “value” of objects with nonzero cache misses
    Those featuring fewer misses are preferably allocated in the fastest memory subsystem
  Discard memory objects not presenting cache misses
    Unoptimized case not the worst possible case because objects without cache misses do not populate the fastest memories
Obj #1
5k Cache Misses
Obj #2
10k Cache Misses
Obj #3
0 Cache Misses
Memory #1
Very Fast
Memory #2
Regular Speed
Memory #3
Slow
Obj #1
5k Cache Misses
Obj #2
10k Cache Misses
Obj #3
0 Cache Misses
Memory #1
Very Fast
Memory #2
Regular Speed
Memory #3
Slow
Worst Case
Our Unoptimized Case

## Slide 22: Experimental Results MiniMD
99% of memory objects (21/26 GB) no cache misses during loop iteration
Scenario 1
  21 objects < SP && fit in SP
  3D > 9 objects > SP && fit in 3D
  Trivial distribution
  No opt. vs unopt. case
  7.6% exec. time improvement w/ respect to baseline architecture
    3D memory performance benefits
Scenario 2
  Memory size restrictions
    Choice at DRAM/NVRAM
  4 obj. small enough for DRAM
    But only room for 3 of them
Mem. | Obj. | Occup. | Cycles | Exec.
SP | 21 | 53% | -4M | 0.0%
3D | 9 | 65% | -743M | -7.6%
DRAM | 0 | 0% |  | 
TOTAL |  |  | -747M | -7.6%
Mem. | Obj. | Occup. | Cycles | Exec.
SP | 21 | 53% | -4M | 0.0%
3D | 5 | 21% | -18M | -0.2%
DRAM | 3 | 93% |  | 
NVRAM | 1 | 4% | +1G | +13.9%
TOTAL |  |  | +1G | +13.7%
Mem. | Obj. | Occup. | Cycles | Exec.
SP | 21 | 53% | -4M | 0.0%
3D | 5 | 21% | -18M | -0.2%
DRAM | 3 | 94% |  | 
NVRAM | 1 | 4% | +130G | +1,330.5%
TOTAL |  |  | +130G | +1,330.3%
Optimized
Unoptimized

## Slide 23: Experimental Results HPCCG
742/760 mem. obj. no misses: 22 GB
9 mem. obj. < SP, but ↓ # cycles
9 other obj. give choices
Scenario 1
  1 obj. > 3D → DRAM
  8 obj. to be distr. DRAM & 3D
Scenario 2
  2 obj. fit only in NVRAM
  7 obj. to be distr. in 3D and DRAM
Mem. | Obj. | Occup. | Cycles | Exec.
SP | 9 | 0% | -2K | 0.0%
3D | 4 | 98% | -497M | -8.3%
DRAM | 5 | 45% |  | 
TOTAL |  |  | -497M | -8.3%
Mem. | Obj. | Occup. | Cycles | Exec.
SP | 9 | 0% | -2K | 0.0%
3D | 7 | 39% | -294M | -4.9%
DRAM | 2 | 60% |  | 
TOTAL |  |  | -294M | -4.9%
Optimized
Unoptimized
Mem. | Obj. | Occup. | Cycles | Exec.
SP | 9 | 0% | -2K | 0.0%
3D | 2 | 95% | -224M | -3.8%
DRAM | 5 | 54% |  | 
NVRAM | 2 | 60% | +193G | +3,236.7%
TOTAL |  |  | +193G | +3,232.9%
Mem. | Obj. | Occup. | Cycles | Exec.
SP | 9 | 0% | -2K | 0.0%
3D | 2 | 95% | -6M | -0.1%
DRAM | 5 | 54% |  | 
NVRAM | 2 | 60% | +193G | +3,236.7%
TOTAL |  |  | +193G | +3,236.6%
Optimized
Unoptimized

## Slide 24: Experimental Results Discussion
SP: low occupancy & contributions to the overall performance
  Most of the small objects do not present LL cache misses
  Expected in highly-tuned code
  TODO: explore splitting + migration
Overall performance improvement with respect to unoptimized distribution:
  Nonnegligible in 2 out of the 4 cases
  MiniMD, scenario 2: over 10x by avoiding placing a particular memory object in NVRAM
  HPCCG, scenario 1: ~4% improvement by placing obj. w/ large misses in fast memories
Hardware | Test Case | 
 | MiniMD | HPCCG
Scenario 1 | 0.0% | 3.7%
Scenario 2 | 1,158.0% | 0.1%

## Slide 25: Conclusions

## Slide 26: Summary
Design of tools providing object-differentiated profiling on Valgrind
Provided methodology for optimized data distribution among memory subsystems
  At object level granularity
Results based on 2 miniapps and 2 configurations of heterogeneous memory:
  Object-differentiated profiling useful for memory distribution in heterogeneous memory systems
Future work:
  Object migration?
  Split objects?

## Slide 27
Thank you
Questions?
apenya@mcs.anl.gov

## Slide 28: Background Valgrind’s Extensions
Statically-Allocated Memory Objects
  Debug information (e.g. gcc -g)
  Information distributed among the different binary objects of an application
    including libraries
  Different scopes determine whether the variables are valid or not
  Asymptotic computational cost:
O(st x (dio + sao))
    st is the maximum stack trace depth
    dio is the number of debug information objects
    sao is the max. # of statically allocated objects for a given IP
A. J. Peña and P. Balaji. "A framework for tracking memory accesses in scientific applications", in P2S2 2014 (ICPP Workshop), Minneapolis, MN, Sep. 2014.

## Slide 29: Background Valgrind’s Core Extensions
Dynamically-Allocated Memory Objects
  Interception of application calls to memory management routines
  Ordered set using starting memory address as sorting index:
    Possible since dynamically allocated objects reside in the global scope
    Binary searches:
  O(log dao)
      dao is # of dynamically alloc. objects
  Merge objects
    If they were created featuring a common stack trace
    These are likely to be considered as a single one from application level
    Examples:
      Loop allocating an array of lists as part of a matrix
      Temporary object in a function
    TODO: linked list detection
A. J. Peña and P. Balaji. "A framework for tracking memory accesses in scientific applications", in P2S2 2014 (ICPP Workshop), Minneapolis, MN, Sep. 2014.

## Slide 30: Background Memory Technologies
Cache
  Levels of increasing size and latency
  Small, hardware-managed, low-latency
  Common CPU stall cycles:
    Nonexistent for L1
    ~10 for L2
    Keep increasing w/ distance to CPU
NVRAM
  Does not require refresh (energy)
  Limited write-erase cycles
  Write speeds lower than reads
  Non byte addressable (at low level)
    High-level libraries
  Usually I/O-based storage
    But we adopt it as het. mem.
Scratchpad
  Like cache, but explicitly managed
  Common in embedded processors & GPUs, but not in compute nodes
  High level of control; prevents issues caused by heuristic management
On-chip 3D-Stacked Memory
  DRAM
  Physically stacked in multiple layers
  Within the microprocessor die
  Low latency – high bandwidth
  Energy dissipation is a problem
  8-16 GB per chip
  30% reduction in access latency
DRAM
  … you know ;)