## Slide 1: Designing Middleware and Network Architectures to allow High Performance Communication for TCP/IP based Applications
Pavan Balaji
Advisor: Prof. Dhabaleswar K. Panda
Network Based Computing Laboratory
Ohio State University

## Slide 2: Current Network Based Computing Systems
System Area Network or Cluster Environment
Wide
Area
Network
Distributed Cluster Environment
High Speed Backbone
Systems connected over a High-Speed Backbone Network
High Speed Cluster Interconnection network

## Slide 3: High Speed Cluster Interconnects
Advent of Several High Speed Cluster Interconnection Networks
  Ex: InfiniBand, Myrinet, 10-Gigabit Ethernet, etc.
  High Performance Communication Protocols over these networks
    Each network has a separate communication protocol
    Each network has a separate interface
Compatibility with other networks
  Incompatible with other cluster interconnects; Incompatible with the WAN
  Can only be used only in the cluster environment
Compatibility with existing applications
  Good to build new applications
  Not so beneficial for existing ones

## Slide 4: Application Requirements
Applications are built around portability
  Rewriting them for every new network is cumbersome and impractical
  As soon as a new network is available, they should RUN !
  A Standard Interface required
Two broadly used standard interfaces
  Message Passing Interface (MPI)
    Scientific Applications (Ex: Physics Simulations, Weather Forecast)
  Sockets Interface
    Commercial Applications (Ex: Data-Center and other Web Architectures)
    Grid-based Applications (Ex: Data-Cutter library, Globus)

## Slide 5: The Sockets Programming Interface
Sockets: Communication Interface to use protocols such as TCP/IP
Performance of the application, depends on TCP/IP
Several GENERIC optimizations have been proposed
  Jacobson Optimization: Integrated Checksum-Copy [Jacob89]
  Header Prediction for single stream communication
  Could not improve performance significantly !
Several optimizations utilizing network features were proposed
  Interrupt Coalescing (most network adapters provide this)
  Checksum Offload (both IP and TCP checksum)
  Still insufficient !!
[Jacob89]: “An analysis of TCP Processing Overhead”, D. Clark, V. Jacobson, J. Romkey and H. Salwen. IEEE Communications

## Slide 6: High Performance Network Features
High Performance Networks support several features
  High Performance
    Multi-gigabit per second throughput
    2-10 μs communication time from memory to memory
  Offloaded Protocol Stack; exposed using user-level protocols
    Network adapter takes care of reliability, data integrity, etc.
  Zero Copy Data Transfer Primitives
    Data moved from application-to-application memory directly
  One-Sided Communication Operations
    Remote Direct Memory Access (RDMA) Protocols
    Node can directly write to or read from remote memory locations
  Network based Atomic Operations
    Network adapter can perform atomic operations on remote memory locations

## Slide 7: High Performance Sockets
Hardware
Kernel
User
Traditional Berkeley Sockets
Application or Library
Traditional
Sockets Interface
Transport Layer (TCP)
IP
Device Driver
Network Adapter
Application or Library
High Performance Sockets
User-level Protocol
High Performance Network Adapter
High Performance Sockets
Network Features
(e.g., Offloaded Protocol)
Device Driver

## Slide 8: Issues with High Performance Sockets
Can applications benefit from the performance of these sockets?
  Limited by the Sockets API itself
  Limited by the requirements of the Sockets semantics
Application or Library
High Performance Sockets
User-level Protocol
Kernel Module
High Performance Network Adapter
Network Features
(e.g., Offloaded Protocol)
Application or Library
Application-Sockets
Interactions
WAN Compatibility

## Slide 9: Direct Data Placement and RDMA over IP
A new initiative by IETF to address the WAN compatibility issue
Utilizes most of the common features provided by networks
  Offloaded Protocol Stack
    Offloads the TCP/IP stack on to the network adapter
  Zero Copy Data Transfer Primitives
  One-sided communication operations
Direct Data Placement (DDP) has two portions
  DDP Protocol
    Based on TCP/IP
    Can help achieve WAN compatibility
  DDP Interface
    Similar to other user-level protocols
    Not good for new applications

## Slide 10: Open Challenges and Proposed Framework
Implementing High Performance Sockets
  What are the design issues involved?
  What is the performance such implementations can achieve?
What are the issues associated with High Performance Sockets?
  We ensured a semantic match
  How about a performance match? Can applications utilize the performance?
A complete solution with the following properties is required:
  Application should directly be able to run; Sockets interface must be retained
    High Performance Sockets can help
  API provides more extensions to handle the above issues when required
    Sockets API needs to be extended to encompass more features
    DDP API can help
  Underlying protocol must support WAN compatibility
    DDP Protocol stack can help

## Slide 11: Presentation Outline
Introduction, Motivation and Problem Statement
Designing High Performance Sockets
  Sockets over Gigabit Ethernet, VIA and InfiniBand
  Performance Results
Issues with High Performance Sockets
An Integrated API for High Performance Sockets and RDMAP/DDP
Concluding Remarks
Continuing and Future Work
Related and Other Publications

## Slide 12: Handling Semantic Mismatches
Design Issues that need to be handled:
  Interaction capability with non High Performance Sockets
  Buffer Advertisement and Flow Control
Performance Issues that need to be handled:
  Flow Control Schemes
    Packetization, Reverse Packetization
  Buffer usage
    NIC-based tag matching (Gigabit Ethernet)
  ACK Collection
    Delayed Acknowledgments, Piggy backing, Unexpected queues

## Slide 13: Interaction Capability
Sockets is a very generic API
  UNIX Sockets, UDP/IP, etc.
  Need to be distinguished and not handled
Connections with non high performance networks
  Remote end might not use high performance sockets
  Needs to be handed over to the appropriate protocol
  Mechanism for TCP Termination at cluster gateways
Nodes running multiple applications
  Some of the applications might not want to use high performance sockets
  Port-level distinction of which sockets implementation the application wants

## Slide 14: Interacting with Traditional Sockets
Hardware
Kernel
User
Traditional Berkeley Sockets
Application or Library
Traditional
Sockets Interface
Transport Layer (TCP)
IP
Device Driver
Network Adapter
Application or Library
Traditional
Sockets Interface
High Performance Sockets
User-level Protocol
TCP/IP
Device Driver
High Performance Network Adapter
High Performance Sockets
Network Features
(e.g., Offloaded Protocol)

## Slide 15: Handling Semantic Mismatches
Design Issues that need to be handled:
  Interaction capability with non High Performance Sockets
  Buffer Advertisement and Flow Control
Performance Issues that need to be handled:
  Flow Control Schemes
    Packetization, Reverse Packetization
  Buffer usage
    NIC-based tag matching (Gigabit Ethernet)
  ACK Collection
    Delayed Acknowledgments, Piggy backing, Unexpected queues

## Slide 16: Buffer Advertisement and Flow Control
User-level protocols require receivers to advertise buffers upfront
  If a buffer is not posted when the data arrives:
    The data is dropped
    Hardware might retry sending the data
    Connection might be terminated for some protocols
Need some kind of a mechanism to ensure that buffers are posted
  Separate Communication Thread
  Explicit synchronization
  Credit-based Flow control mechanism

## Slide 17: Handling Semantic Mismatches
Design Issues that need to be handled:
  Interaction capability with non High Performance Sockets
  Buffer Advertisement and Flow Control
Performance Issues that need to be handled:
  Flow Control Schemes
    Packetization, Reverse Packetization
  Buffer usage
    NIC-based tag matching (Gigabit Ethernet)
  ACK Collection
    Delayed Acknowledgments, Piggy backing, Unexpected queues

## Slide 18: High Performance Sockets over EMP (Gigabit Ethernet)
Latency improvement of up to 4 times
Throughput improvement of up to 53%

## Slide 19: High Performance Sockets over InfiniBand
SDP achieves 500MBps bandwidth compared to 180MBps of IPoIB
Latency of 27us compared to 31us of IPoIB
Improved CPU Utilization

## Slide 20: Presentation Outline
Introduction, Motivation and Problem Statement
Designing High Performance Sockets
Issues with High Performance Sockets
  Applications tuned for TCP/IP communication
  Memory traffic associated with sockets communication
  Impact of two-sided communication in compute-intensive environments
An Integrated API for High Performance Sockets and RDMAP/DDP
Concluding Remarks
Continuing and Future Work
Related and Other Publications

## Slide 21: Impact on Applications tuned for TCP/IP
Several applications are tuned to perform well with TCP/IP
  Workload distribution granularity is chosen with respect to TCP/IP
  This has several implications
    Bandwidth to latency tradeoff depends on workload granularity
    Computation to communication overlap depends on workload granularity
We analyze these with respect to the virtual microscope application
  Built using the data-cutter runtime library
  Executed over TCP/IP as well as High Performance Sockets over VIA
Load Balancer
Processing Nodes
Visualization Client

## Slide 22: Bandwidth to Latency Tradeoff
TCP
VIA
0
1
Reqd BW
0
1
VIA
TCP
Image rendering should be interactive
Response times should be small

## Slide 23: Effects of Guarantees on Updates per Second (Complete Images)
SocketVIA performs better
  TCP can’t give guarantees > 3.25
but…
  Limited improvement
  Design Decisions are bottlenecks
Re-sizing of data blocks
  Try to alleviate the bottlenecks
  Only concern is Updates per Second
  Achievable at low block sizes
  No application changes (in this case)
  Significant performance improvement

## Slide 24: Pipelining: Computation/Communication Overlap
Latency
Message Size (log Scale)
TCP
VIA
Computation
0
1
Compute Nodes
Linear Computation with Message Size
Root Node

## Slide 25: Effect of Heterogeneous Clusters on Demand Driven (DD) Scheduling
Demand Driven Scheduling
  Additional Latency Cost
  SocketVIA should perform better (?)
  Natural overlap of comm. with comp.
  Use of SocketVIA or TCP makes no diff.

## Slide 26: Memory Traffic Associated with Sockets
Sockets semantics assumes buffering of data
  Requires copies on the sender and the receiver sides
  Severe implications on the memory traffic generated
We analyze the impact of copies in TCP/IP sockets
The analysis holds for high performance sockets too
Performed over 10-Gigabit Ethernet and InfiniBand

## Slide 27: TCP/IP Control Path (Sender Side)
Application
Buffer
Socket Buffer
NIC
Driver
write()
Checksum and Copy
Post TX
Kick Driver
Return to Application
Post Descriptor
INTR on transmit success
DMA
Checksum, Copy and DMA are the data touching portions in TCP/IP
Offloaded protocol stacks avoid checksum at the host; copy and DMA are still present
Packet Leaves

## Slide 28: TCP/IP Control Path (Receiver Side)
Application
Buffer
Socket Buffer
NIC
Driver
Wait for read()
read()
Application gets data
Copy
DMA
Packet Arrives
INTR on Arrival
Data might need to be buffered on the receiver side
Pick-and-Post techniques force a memory copy on the receiver side

## Slide 29: Memory Bus Traffic for TCP (receiver)
North Bridge
Application and Socket buffers fetched to L2 $
Application Buffer written back to memory
CPU
NIC
FSB
Memory Bus
I/O Bus
Each network byte requires 4 bytes to be transferred on the Memory Bus (unidirectional traffic)
Assuming 70% memory efficiency, TCP can support at most 4-5Gbps bidirectional on 10Gbps (333MHz/64bit DDR2)
Appln.
Buffer
Socket
Buffer
L2 $
Memory
Appln.
Buffer
Socket
Buffer
Data DMA
Data Copy

## Slide 30: Network to Memory Traffic Ratio
 | Application Buffer Fits in Cache | Application Buffer Doesn’t fit in Cache
Transmit (Worst Case) | 1-4 | 2-4
Transmit (Best Case) | 1 | 2-4
Receive (Worst Case) | 2-4 | 4
Receive (Best Case) | 2 | 4
This table shows the minimum memory traffic associated with network data
In reality socket buffer cache misses, control messages and noise traffic may cause these to be higher
Details of other cases present in the paper

## Slide 31: Multi-Stream Tests: Memory Traffic
Memory Traffic is significantly higher than the network traffic
Comes to within 5% of the practically attainable peak memory bandwidth

## Slide 32: Throughput test: Memory Traffic
Sockets can force up to 4 times more memory traffic compared to the network traffic
RDMA allows has a ratio of 1 !!

## Slide 33: Impact of Sockets in Compute-Intensive Environments
Environments such as data-centers perform heavy computations
Some nodes are lightly loaded, some are heavily loaded
Sockets API is two-sided
  Both sides of the communication do equal work
  Is this alright in such environments?
Some networks such as InfiniBand allow one-sided communication
  A node can read or write into remote nodes memory
  What are the implications of such one-sided communication?

## Slide 34: Cache Coherency in Data-Centers
We use a cache coherence scheme (client-polling) for the analysis:
  Front end nodes (proxy servers) cache content when requested
  Check validity with back-end (application/database servers) on each request
Sockets uses two sided communication for this checking; VAPI uses one-sided
Proxy Server
Web Server (Apache)
Application Server (PHP)
Database Server (MySQL)
WAN
Clients
Storage

## Slide 35: Data-Center: Throughput

## Slide 36: Presentation Outline
Introduction, Motivation and Problem Statement
Designing High Performance Sockets
Issues with High Performance Sockets
Integrated API for High Performance Sockets and RDMAP/DDP
Concluding Remarks
Continuing and Future Work
Related and Other Publications

## Slide 37: Integrated Framework
High Performance
Sockets
The framework should have the following properties:
  Application should directly be able to run; Sockets interface must be retained
  API provides more extensions to handle the above issues when required
  Underlying protocol must support WAN compatibility
Application or Library
High Performance Sockets
User-level Protocol
High Performance Network Adapter
Network Features
(e.g., Offloaded Protocol)
Device Driver
Application or Library
DDP API
Extensions
User-level Protocol
High Performance Network Adapter
Offloaded RDMAP/DDP
Device Driver

## Slide 38: Capabilities of this Framework
The integrated framework satisfies all the stated requirements:
  It allows existing applications to run without any modifications
    High Performance Sockets allows this kind of seamless integration
  Applications have extended API to utilize as and when needed
    High Performance Sockets extended with the DDP API allows this
    Zero-copy data transfer ensures minimal memory traffic
    One-sided operations ensure high performance in compute-intensive applications
    Application re-designing follows logically and only if needed
  Underlying protocol is WAN compatible
    Offloaded RDMAP/DDP ensures that the entire setup is WAN compatible

## Slide 39: Presentation Outline
Introduction, Motivation and Problem Statement
Designing High Performance Sockets
Issues with High Performance Sockets
Integrated API for High Performance Sockets and RDMAP/DDP
Concluding Remarks
Continuing and Future Work
Related and Other Publications

## Slide 40: Concluding Remarks
Traditional Sockets implementations are over TCP/IP
  Cannot achieve a high performance due to several overheads
High Performance Sockets implementations
  Utilize the offloaded stack and other features in the NIC
  Are able to deliver a high performance
Several issues with High Performance Sockets
  Applications are limited by the sockets API and semantics
We proposed an integrated framework:
  API: Extended sockets interface
    All the sockets functionality will be retained; DDP functionality inserted
  Protocol: RDMAP/DDP
    Allows WAN compatibility since its implemented over IP

## Slide 41: Presentation Outline
Introduction, Motivation and Problem Statement
Designing High Performance Sockets
Issues with High Performance Sockets
Integrated API for High Performance Sockets and RDMAP/DDP
Concluding Remarks
Continuing and Future Work
Related and Other Publications

## Slide 42: Continuing and Future Work
Currently working on:
  A software prototype and a simulator for the integrated framework
    Understanding the stack and its requirements
    Estimates of the benefits
  RDMAP/DDP API over TCP Offload Engines
  Application ports to utilize the RDMAP/DDP API
Will be working on:
  NIC-based implementation of the RDMAP/DDP protocol stack

## Slide 43: Presentation Outline
Introduction, Motivation and Problem Statement
Designing High Performance Sockets
Issues with High Performance Sockets
Integrated API for High Performance Sockets and RDMAP/DDP
Concluding Remarks
Continuing and Future Work
Related and Other Publications

## Slide 44: Related Publications
P. Balaji, S. Narravula, K. Vaidyanathan, H. -W. Jin and D. K. Panda, On the Provision of Prioritization and Soft QoS in Dynamically Reconfigurable Shared Data-Centers over InfiniBand. In the proceedings of the IEEE International Symposium on Performance Analysis of Systems and Software (ISPASS), 2005.
P. Balaji, H. Shah and D. K. Panda, Sockets vs RDMA Interface over 10-Gigabit Networks: An In-depth analysis of the Memory Traffic Bottleneck. In the proceedings of the Workshop on Remote Direct Memory Access (RDMA): Applications, Implementations, and Technologies (RAIT); held in conjunction with the IEEE International Conference on Cluster Computing, 2004.
P. Balaji, K. Vaidyanathan, S. Narravula, S. Krishnamoorthy, H. -W. Jin and D. K. Panda, Exploiting Remote Memory Operations to Design Efficient Reconfiguration for Shared Data-Centers over InfiniBand. In the proceedings of the workshop on Remote Direct Memory Access (RDMA): Applications, Implementations, and Technologies (RAIT); held in conjunction with the IEEE International Conference on Cluster Computing, 2004.
H. -W. Jin, P. Balaji, C. Yoo, J . Y. Choi and D. K. Panda, Exploiting NIC Architectural Support for Enhancing IP based Protocols on High Performance Networks. Accepted for publication at the Special Issue of the Journal of Parallel and Distributed Computing (JPDC) on Design and Performance of Networks for Super-, Cluster- and Grid-Computing, 2005.

## Slide 45: Related Publications [more ]
S. Narravula, P. Balaji, K. Vaidyanathan, S. Krishnamoorthy, J. Wu and D. K. Panda, Supporting Strong Coherency for Active Caches in Multi-Tier Data-Centers over InfiniBand. In the proceedings of the workshop on System Area Networks (SAN); held in conjuntion with the IEEE International Symposium on High Performance Computer Architecture (HPCA), 2004.
P. Balaji, S. Narravula, K. Vaidyanathan, S. Krishnamoorthy, J. Wu and D. K. Panda, Sockets Direct Protocol over InfiniBand in Clusters: Is it Beneficial?. In the proceedings of the IEEE International Symposium on Performance Analysis of Systems and Software (ISPASS), 2004.
P. Balaji, J. Wu, T. Kurc, U. Catalyurek, D. K. Panda and J. Saltz, Impact of High Performance Sockets on Data Intensive Applications. In the proceedings of the IEEE International Symposium on High Performance Distributed Computing (HPDC), 2003.
P. Balaji, P. Shivam, P. Wyckoff and D. K. Panda, High Performance User-Level Sockets over Gigabit Ethernet. In the proceedings of the IEEE International Conference on Cluster Computing, 2002.

## Slide 46: Other Publications
M. Islam, P. Balaji, P. Sadayappan and D. K. Panda, QoPS: A QoS based scheme for Parallel Job Scheduling. Published in the IEEE Springer LNCS Journal Series, 2003.
K. Vaidyanathan, P. Balaji, H. -W. Jin and D. K. Panda, Workload-driven Analysis of File Systems in Shared Multi-tier Data-Centers over InfiniBand. In the proceedings of the Eighth Workshop on Computer Architecture Evaluation using Commercial Workloads (CAECW-8); to be held in conjunction with the 11th International Symposium on High Performance Computer Architecture (HPCA-11), 2005.
M. Islam, P. Balaji, P. Sadayappan and D. K. Panda, Towards Provision of Quality of Service Guarantees in Job Scheduling. In the proceedings of the IEEE International Conference on Cluster Computing, 2004.
R. Kurian, P. Balaji, P. Sadayappan, Opportune Job Shredding: An Effective approach for scheduling Parameter Sweep Applications. In the proceedings of the Los Alamos Computer Science Institute Symposium (LACSI), 2003.
R. Gupta, P. Balaji, J. Nieplocha and D. K. Panda, Efficient Collective Operations using Remote Memory Operations on VIA-Based Clusters. In the proceedings of the IEEE International Parallel and Distributed Processing Symposium (IPDPS), 2003.

## Slide 47: Web Pointers
Network Based Computing
Laboratory
Website: http://www.cse.ohio-state.edu/~balaji
Group Homepage: http://nowlab.cis.ohio-state.edu
Email: balaji@cse.ohio-state.edu
NBC-LAB

## Slide 48: Backup Slides

## Slide 49: Sockets over EMP

## Slide 50: FTP Application
Up to 2 times improvement compared to TCP
Notes: Together with the micro-benchmarks, we have tested our sockets layer with real life applications such as the FTP application. Our sockets layer is able to achieve an improvement up to 2 times compared to TCP. Though the bandwidth results of Data Streaming and Non-data streaming sockets show a variation, they perform identically in this application due to the file system overhead of accessing the file before transmitting it.

## Slide 51: Web Server (HTTP/1.0)
Up to 6 times improvement compared to TCP
Notes: The web-server application had been designed as follows: The server keeps waiting for connections. The clients on the other hand connect to the server and send in a request message. For this experiment, we have chosen the request size to be 4 bytes. The server on getting this request sends back a response message of varying sizes. This can be typically thought of as the clients sending a file name and the server sending back the file.
In this application, the factor of improvement for our sockets is up to 6 times. However most of this improvement comes from the connection time. TCP takes about 250us for connection, whereas in EMP, it’s just a data message exchange. So, the connection time is much lesser. To get around this drawback of TCP, some later implementations allow up to 8 requests per connection on a web server. We have also tried our sockets layer with such an implementation.

## Slide 52: Web Server (HTTP/1.1)
Up to 3 times improvement compared to TCP
Notes: With this implementation, we allow up to 8 requests per connection. In this case, we still out perform TCP by a factor of 3. In the worst case, if we allow infinite requests per connection, this test boils down to a simple ping-pong test, in which we have already shown to do significantly better than TCP.

## Slide 53: Sockets Direct Protocol

## Slide 54: Hotspot Latency
SDP is more scalable in hot-spot scenarios

## Slide 55: Data-Center Response Time
SDP shows very little improvement: Client network (Fast Ethernet) becomes the bottleneck
Client network bottleneck reflected in the web server delay: up to 3 times improvement with SDP

## Slide 56: Data-Center Response Time (Fast Clients)
SDP performs well for large files; not very well for small files

## Slide 57: Data-Center Response Time Split-up
IPoIB
SDP

## Slide 58: Data-Center Response Time without Connection Time Overhead
Without the connection time, SDP would perform well for all file sizes

## Slide 59: PVFS Performance using ramfs

## Slide 60: PVFS Performance with sync (ext3fs)
Clients can push data faster to IODs using SDP; de-stage bandwidth remains the same

## Slide 61: Credit Based Flow Control
Sender
Receiver
SQ
RQ
SQ
RQ
Data
Data
Data
Data
ACK
Notes: In the credit based flow control approach, the receiver pre-posts a number of descriptors. The sender loses a credit for every message sent and gains a credit for every acknowledgment received. The sender sends the first message. However, he doesn’t have to wait for an acknowledgment before sending the subsequent message as long as he has enough credits.

## Slide 62: DDPSim: Impact of NIC Processing Speed
Base Alteon:
Class 1: 600/666

## Slide 63: DDPSim: Impact of PCI-X (133 MHz)
Class 1: 600/666
Class 2: 600/666, 133 MHz PCI-X

## Slide 64: DDPSim: Impact of NIC System Bus (533 MHz)
Class 2: 600/666, 133 MHz PCI-X
Class 3: 600/666, 133 MHz PCI-X, 533 MHz System Bus

## Slide 65: DDPSim: Impact of Dual NIC Processors
Class 3: 600/666, 133 MHz PCI-X, 533 MHz System Bus
Class 4: 600/666, 133 MHz PCI-X, 533 MHz System Bus, Dual NIC

## Slide 66: User-Level DDP

## Slide 67: Kernel-Level DDP

## Slide 68: DDPSim: PCI-Express (8x) Bidirectional
Class 5: 600MHz CPU, 133 MHz PCI-X, 533 MHz System Bus, Dual NIC
Class 6: 600MHz CPU, 8x PCI-Express, 533 MHz System Bus, Dual NIC