## Slide 1: Making a Case for a Green500 List
S. Sharma†, C. Hsu†, and W. Feng‡
Presenter: Pavan Balaji
The Ohio State University
Notes: Ad-lib and improvise as needed. I’ve only noted the basics. You do NOT need to say everything word-for-word with respect to what I type on the Notes pages. I am only typing it all out to give you a general idea of what should be said. You do NOT need to say everything exactly word-for-word.
Opening:
My name is Pavan Balaji. I am a graduating PhD student from The Ohio State University, who worked as a research intern with Prof. Feng when he was at Los Alamos National Laboratory.

## Slide 2: Outline
Introduction
  What Is Performance?
  Motivation: The Need for a Green500 List
Challenges
  What Metric To Choose?
  Comparison of Available Metrics
TOP500 as Green500
Conclusion

## Slide 3: What Is Performance?
Performance = Speed, as measured in FLOPS
Notes: We have spent DECADES focusing on performance (i.e., speed) as THE performance metric, e.g., TOP500.
Top 500 Supercomputer List
Gordon Bell Awards at SC
ELAPSED TIME for slides 1-3: 1.5 minutes.

## Slide 4: What Is Performance? TOP500 Supercomputer List
Benchmark
  LINPACK: Solves a (random) dense system of linear equations in double-precision (64 bits) arithmetic.
    Introduced by Prof. Jack Dongarra, U. Tennessee
Evaluation Metric
  Performance (i.e., Speed)
    Floating-Operations Per Second (FLOPS)
Web Site
  http://www.top500.org
Next-Generation Benchmark: HPC Challenge
  http://icl.cs.utk.edu/hpcc/
Performance, as defined by speed, is an important metric, but…
Notes: ELASPED TIME for slides 1-4: 2 minutes

## Slide 5: Reliability & Availability of HPC
Systems | CPUs | Reliability & Availability
ASCI Q | 8,192 | MTBI: 6.5 hrs. 114 unplanned outages/month. HW outage sources: storage, CPU, memory.
ASCI White | 8,192 | MTBF: 5 hrs. (2001) and 40 hrs. (2003). HW outage sources: storage, CPU, 3rd-party HW.
NERSC Seaborg | 6,656 | MTBI: 14 days. MTTR: 3.3 hrs. SW is the main outage source. Availability: 98.74%.
PSC Lemieux | 3,016 | MTBI: 9.7 hrs. Availability: 98.33%.
Google | ~15,000 | 20 reboots/day; 2-3% machines replaced/year. HW outage sources: storage, memory. Availability: ~100%.
MTBI: mean time between interrupts; MTBF: mean time between failures; MTTR: mean time to restore
Notes: Focusing only on performance, as defined by speed, has resulted in unreliable and finicky systems.
These unreliable and finicky systems lead to an exorbitant total cost of ownership, e.g., new buildings, new machine rooms, excessive use of electrical power, loss productivity due to downtime, and so on. See next slide.
Pavan: Below is just FYI. You do not need to explicitly define these, unless asked.
MTBI: wall clock hours / # downtime periods
MTBF: mean time between failures
MTTR: downtime hours / # downtime periods
ONCE MTBI AND MTBF ARE IMPROVED ENOUGH, SW BECOMES THE MAIN SOURCE OF OUTAGE, i.e., there is a cross-over point.
ELAPSED TIME for slides 1-5: 3 minutes

## Slide 6: Costs Associated with HPC
Infrastructure
  Sizable costs associated with system administration and maintenance. (People resources are $$$.)
  Massive construction and operational costs associated with powering and cooling.
    Google
      $2M to buy 30 acres of land by The Dalles Dam (Columbia River)
        Inexpensive power to satisfy their high electrical demand.
        Water can be used to cool its massive server-filled facility directly rather than relying on more expensive A/C.
    Lawrence Livermore National Laboratory
      Building for Terascale Simulation Facility: $55M
      Electrical Costs: $14M/year to power and cool.
Productivity
  Downtime means no compute time, i.e., lost productivity.
Notes: FWIW: Virginia Tech
  Since System X moved into production in January 2006,
    Zero downtime
    99.9% system utilization
ELAPSED TIME for slides 1-6: 4.5 minutes

## Slide 7: Recent Trends in HPC
180/360 TF/s
16 TB DDR
October 2003
BG/L half rack prototype
500 Mhz
512 nodes/1024 proc.
2 TFlop/s peak
1.4 Tflop/s sustained
Low(er)-Power Multi-Core Chipsets
  AMD: Athlon64 X2 (2) and Opteron (2)
  ARM: MPCore (4)
  IBM: PowerPC 970 (2)
  Intel: Smithfield (2) and Montecito (2)
  PA Semi: PWRficient (2)
Low-Power Supercomputing
  Green Destiny (2002)
  Orion Multisystems (2004)
  BlueGene/L (2004)
  MegaProto (2005)
Notes: Recent low-power trends in HPC that seek to address the issues of reliability, availability, and total cost of ownership.
AMD: Each chipset has up to 2 cores.
ARM: MPCore has up to 4 cores.
Etc.

## Slide 8: Perspective
FLOPS Metric of the TOP500
  Performance = Speed (as measured in FLOPS with Linpack)
  May not be “fair” metric in light of recent low-power trends to help address reliability, availability, and total cost of ownership.
The Need for a Different Performance Metric
  Performance = f ( speed, “time to answer”, power consumption, “up time”, total cost of ownership, usability, …)
  Easier said than done …
    Many of the above dependent variables are difficult, if not impossible, to quantify, e.g., “time to answer”, TCO, usability, etc.
The Need for a Green500 List
  Performance = f ( speed, power consumption) as speed and power consumption can be quantified
Notes: Because of these recent low-power trends in HPC -- trends that oftentimes sacrifice speed for other desirable attributes such as reliability, availability, and total cost of ownership -- we need a different set of metrics to define what “performance” means …
Performance should be a function “f” of a multitude of metrics such as peak speed, time-to-answer, power consumption, total cost of ownership, and so on … but many of these dependent variables are difficult to quantify.
We argue that AT A MINIMUM, there is a need for a Green500 List, particularly given that power consumption is indirectly related to many metrics of interest, i.e., reliability, availability, and total cost of ownership.

## Slide 9: Outline
Introduction
  What Is Performance?
  Motivation: The Need for a Green500 List
Challenges
  What Metric To Choose?
  Comparison of Available Metrics
TOP500 as Green500
Conclusion

## Slide 10: Challenges for a Green500 List
What Metric To Choose?
  ED n : Energy-Delay Products, where n is a non-negative int.
        (borrowed from the circuit-design domain)
  Variants of ED n
  Speed / Power Consumed
    FLOPS / Watt, MIPS / Watt, and so on
What To Measure? Obviously, energy or power … but
  Energy (Power) consumed by the computing system?
  Energy (Power) consumed by the processor?
  Temperature at specific points on the processor die?
How To Measure Chosen Metric?
  Power meter? But attached to what? At what time granularity should the measurement be made?
Notes: What to Measure?
We know that we have to measure energy (or power), but energy (or power) of what? Of the entire computing system? Of just the processor? What about measuring the temperature instead (in light of Arrenhius’ equation, see the very last slide of this presentation, i.e., “Improving Reliability & Availability)
How To Measure?
How exactly do we measure the energy (power) of a computing system? Or how about a processor? Do we put probes on the power pins to the CPU ASIC?

## Slide 11: ED n : Energy-Delay Products
Original Application
  Circuit Design
Problem
  For n ≥ 1, the metric is biased towards systems with a larger number of processors as the “delay component” (i.e., aggregate speed) dominates.
  As n increases, the bias towards aggregate speed, and hence, HPC systems with larger numbers of processors, increases dramatically.

## Slide 12: Variants of ED n : V∂ =E(1−∂) D2(1+∂)
Negative values of ∂ (particularly more negative values) marginally offset the bias of the ED n towards speed.
  In our benchmarking, they produced identical rankings to the ED n metric.
Positive values of ∂ place greater emphasis on performance.
  As ∂ increases towards one, the metric approaches the limit E 0D 4 and behaves more like the standard FLOPS metric, which is used for TOP500 List.
Metric of Choice: FLOPS / Watt (again)

## Slide 13: Outline
Introduction
  What Is Performance?
  Motivation: The Need for a Green500 List
Challenges
  What Metric To Choose?
  Comparison of Available Metrics
TOP500 as Green500
Conclusion

## Slide 14: Efficiency of Four-CPU Clusters
Name | CPU | LINPACK (Gflops) | Avg Pwr (Watts) | Time (s) | ED (*106) | ED2 (*109) | Flops/W | V∂=−0.5
C1 | 3.6G P4 | 19.55 | 713.2 | 315.8 | 71.1 | 22.5 | 27.4 | 33.9
C2 | 2.0G Opt | 12.37 | 415.9 | 499.4 | 103.7 | 51.8 | 29.7 | 47.2
C3 | 2.4G Ath64 | 14.31 | 668.5 | 431.6 | 124.5 | 53.7 | 21.4 | 66.9
C4 | 2.2G Ath64 | 13.40 | 608.5 | 460.9 | 129.3 | 59.6 | 22.0 | 68.5
C5 | 2.0G Ath64 | 12.35 | 560.5 | 499.8 | 140.0 | 70.0 | 22.0 | 74.1
C6 | 2.0G Opt | 12.84 | 615.3 | 481.0 | 142.4 | 64.5 | 20.9 | 77.4
C7 | 1.8G Ath64 | 11.23 | 520.9 | 549.9 | 157.5 | 86.6 | 21.6 | 84.3

## Slide 15: Green500 Ranking of Four-CPU Clusters
Green500 Ranking |  |  |  |  |  |  | TOP 500 | Power500
Rank | ED | ED2 | ED3 | V∂=−0.5 | V∂=0.5 | FLOPS/Watt | FLOPS | Watts
1 | C1 | C1 | C1 | C1 | C1 | C2 | C1 | C2
2 | C2 | C2 | C2 | C2 | C3 | C1 | C3 | C7
3 | C3 | C3 | C3 | C3 | C4 | C5 | C4 | C5
4 | C4 | C4 | C4 | C4 | C2 | C4 | C6 | C4
5 | C5 | C5 | C5 | C5 | C5 | C7 | C2 | C6
6 | C6 | C6 | C6 | C6 | C6 | C3 | C5 | C3
7 | C7 | C7 | C7 | C7 | C7 | C6 | C7 | C1

## Slide 16: Outline
Introduction
  What Is Performance?
  Motivation: The Need for a Green500 List
Challenges
  What Metric To Choose?
  Comparison of Available Metrics
TOP500 as Green500
Conclusion

## Slide 17: TOP500 Power Usage
Name | Linpack | Peak Power | MFLOPS/W | TOP500 Rank
BlueGene/L | 367,000 | 2,500 | 146.80 | 1
ASC Purple | 77,824 | 7,600 | 10.24 | 3
Columbia | 60,960 | 3,400 | 17.93 | 4
Earth Simulator | 40,960 | 11,900 | 3.44 | 7
MareNostrum | 42,144 | 1,071 | 39.35 | 8
Jaguar-Cray XT3 | 24,960 | 1,331 | 18.75 | 10
ASC Q | 20,480 | 10,200 | 2.01 | 18
ASC White | 12,288 | 2,040 | 6.02 | 47

## Slide 18: TOP500 as Green500
Relative Rank | TOP500 | Green500
1 | BlueGene/L (IBM) | BlueGene/L (IBM)
2 | ASC Purple (IBM) | MareNostrum (IBM)
3 | Columbia (SGI) | Jaguar-Cray XT3 (Cray)
4 | Earth Simulator (NEC) | Columbia (SGI)
5 | MareNostrum (IBM) | ASC Purple (IBM)
6 | Jaguar-Cray XT3 (Cray) | ASC White (IBM)
7 | ASC Q (HP) | Earth Simulator (NEC)
8 | ASC White (IBM) | ASC Q (HP)

## Slide 19: Conclusion
Metrics for a Green500 Supercomputer List
  Still no definitive metric to use
    By process of elimination, we converged on FLOPS/watt, which is relatively easy to derive from the TOP500 Supercomputer List.
  Insight with respect to current metrics
TOP500 as Green500
  From the data presented, IBM and Cray make the most energy-efficient HPC systems today.

## Slide 20: For More Information
Visit “Supercomputing in Small Spaces” at http://sss.lanl.gov
  Soon to be re-located to Virginia Tech
Contact Wu-chun Feng (a.k.a. “Wu”)
  E-mail: feng@cs.vt.edu
  Phone: (540) 231-1192
  Mailing Address
    2200 Kraft Drive
    Department of Computer Science
    Virginia Tech
    Blacksburg, VA 24060

## Slide 21: EXTRA SLIDES

## Slide 22: Moore’s Law for Power
1
10
100
1000
1.5
1
0.7
0.5
0.35
0.25
0.18
0.13
0.1
0.07
I386 – 1 watt
I486 – 2 watts
Pentium – 14 watts
Pentium Pro – 30 watts
Pentium II – 35 watts
Pentium III – 35 watts
Chip Maximum
Power in watts/cm2
Surpassed
Heating Plate
Not too long to reach
Nuclear Reactor
Year
Pentium 4 – 75 watts
1985
1995
2001
Itanium – 130 watts
Source: Fred Pollack, Intel. New Microprocessor Challenges in the Coming Generations of CMOS Technologies, MICRO32 and Transmeta
Notes: What is the cost here? Increased performance at the cost of power dissipation, and hence, reliability.
Problem: Will Transmeta survive in these economic times and against Intel/AMD? NO.

## Slide 23: Improving Reliability & Availability (Reducing Costs Associated with HPC)
Observation
  High power density a high temperature a low reliability
  Arrhenius’ Equation*
  (circa 1890s in chemistry  circa 1980s in computer & defense industries)
    As temperature increases by 10° C …
      The failure rate of a system doubles.
    Twenty years of unpublished empirical data .
* The time to failure is a function of e-Ea/kT where Ea = activation energy of the failure mechanism being accelerated, k = Boltzmann's constant, and T = absolute temperature
Notes: Approaches:
Address power. Sarita Adve (UIUC), T.N. Vijaykumar (Purdue), Kaushik Roy (Purdue), Dean Tullsen (UCSD). Virtually all the work (except IBM Blue Gene) is simulation-based.
Screw power and ignore efficiency. Assume unreliability … more easily done with Google application though.
Google approach … More easily done because problem is embarrassingly parallel. Sub-tasks are largely decoupled from each other. Availability: 100% (until a couple of weeks ago when Akamai was hacked).
(3) Address power.